## Slide 1
2021
Notes: Welcome to the Emergency Planning and Community Right-to-Know Act, Section 313, Toxics Release Inventory online training for the 2021 reporting year. This is the Advanced Concepts Module of a two-part training course that is made up of this module and a Basic Concepts module. The Advanced Concepts module assumes a basic understanding of the Toxics Release Inventory, or TRI, requirements and focuses on recent changes to the requirements as well as key concepts that will help to ensure accurate TRI reporting. The Basic Concepts module covers the process of determining whether or not your facility is required to report to TRI and, if so, how you actually prepare and submit information to TRI.

## Slide 2: TRI Training Module Agendas
Basic Concepts Module
  Covered Sectors
  Listed Chemicals and Activity Thresholds
  Reporting Exemptions
  Threshold Determination
  Overview of Form R
  Form R Calculation Examples
  Alternate Threshold Rule (Form A)
  TRI-MEweb Introduction
Advanced Concepts Module
  Recent TRI Program Changes
  Advanced Reporting Guidance
  Detailed Guidance for Chemicals of Special Concern
  Tools and Assistance
  TRI-MEweb
v
v
Notes: In this Advanced Concepts course we will cover: updates on recent changes to the TRI program; advanced guidance on threshold determinations and reporting; guidance on how to report for chemicals with special requirements, such as Chemicals of Special Concern; where you can go to get additional information and assistance with TRI requirements, including information on the EPA audit policy; and information on how to submit TRI Forms through TRI-MEweb on EPA’s Central Data Exchange.

## Slide 3: TRI Reporting Requirements
Notes: Let’s briefly review the process for determining whether or not a facility needs to report to TRI and how to report to TRI, which was covered in detail in the Basic Concepts Module.
To be required to report to TRI, your facility must meet ALL of the criteria shown here. A stepwise process can be used to determine if and what you would need to report to TRI. The first step is determining whether or not your facility is covered under EPCRA Section 313 and would, therefore, need to consider its toxic chemicals for TRI reporting. Whether or not your facility is covered is based on the types of activities carried out at the facility and the number of employees working for your facility. NAICS is the North American Industry Classification System, which assigns numeric codes to characterize the activity taking place at the facility. We will talk more about the NAICS codes requirement shortly.
Alternatively, if your facility has been included in a determination by the EPA Administrator under their discretionary authority to add extend reporting requirements to specific facilities, you need not consider your NAICS code or employees for the purposes of determining whether a TRI report is needed.
Then, if you’ve met one of the two criteria above (either are both in a covered sector AND have at least ten full-time employee-equivalents, OR were included in discretionary authority determination), then you proceed to the final step.
The next step is to determine for which TRI chemicals you must submit a TRI report. Covered facilities need to look at the TRI chemicals that are on the list and that may be present at the facility. Next, facilities need to look at how the chemicals are used. Are they manufactured? Processed? Or otherwise used? These are the TRI threshold activities. We will be describing each of these in more detail.
Next, facilities must calculate the quantity of the TRI chemical that is manufactured, processed, or otherwise used, and compare those quantities to the TRI activity thresholds. Only when activity thresholds are exceeded would the facility be required to complete and submit a TRI report, either a Form R or a Form A.

## Slide 4: TRI Process: 2 Step Process
Notes: The process of completing your TRI forms is a two-step process. In the first step, you determine if your facility is required to report to TRI, and if so, you determine which TRI chemicals you handle in your facility, and then which of these you would need to report on.
Step 2, shown on the right, is the release and waste management reporting. This is the information that you would put on a TRI form. What information do facilities report to TRI? For the Form R, which is the more common means of TRI reporting, facilities report on how the TRI chemical is managed as waste, including on-site releases, treatment, energy recovery, recycling of the TRI chemical and off-site transfers, and pollution prevention activities that are conducted at the facility for that chemical.

## Slide 5: SECTION I: RECENT TRI PROGRAM CHANGES

## Slide 6: TRI Program Changes for RY 2021
Key program changes and changes to TRI reporting Form R are listed in the front of the Reporting Forms & Instructions, as well as in TRI-MEweb, and on EPA’s TRI website.
Notes: First, let’s look at the program changes for this reporting year. TRI reporting requirements often change from year to year. It is very important to be aware of the program changes each year before preparing your TRI reports. Program changes can be found on the TRI Website at www.epa.gov/tri, and in the front of the Reporting Forms and Instructions document, which is available for download from the TRI Website. Program changes are also presented in TRI-MEweb, the online reporting tool.

## Slide 7: TRI Program Changes for RY 2021
Updated de minimis levels are in effect for cobalt compounds, 1,2-phenylenediamine (95-54-5), and 1,2-phenylenediamine dihydrochloride (615-28-1).
  1,2-phenylenediamine and 1,2-phenylenediamine dihydrochloride are now classified as Occupational Safety and Health Administration (OSHA) carcinogens due to an assessment by the International Agency for Research on Cancer (de minimis level changed from 1.0% to 0.1%).
  The de minimis levels for cobalt compounds are also changing. Due to a change in the National Toxicology Program’s classification of cobalt, the de minimis levels have been changed to 0.1% for cobalt compounds that release cobalt ions in vivo and 1.0% for all other cobalt compounds
Notes: Effective for RY2021, de minimis levels for 1,2-phenylenediamine (95-54-5) and 1,2-phenylenediamine dihydrochloride (615-28-1) are changed from 1.0% to 0.1%. Additionally, de minimis levels for cobalt compounds are changed to 0.1% for cobalt compounds that release cobalt ions in vivo and 1.0% for all other cobalt compounds.

## Slide 8: Chemical List Changes
Section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA) adds certain per- and polyfluoroalkyl substances (PFAS) to the TRI list of reportable chemicals.
  Additional PFAS may be added to the TRI list for future reporting years due to the automatic addition of PFAS to the TRI list mandated by NDAA Section 7321(c) that occur under certain circumstances:
    EPA finalizing a toxicity value for a PFAS;
    issuing certain Significant New Use Rules (SNURs) under TSCA for a PFAS, or adding a PFAS to certain existing SNURs;
    adding a PFAS as an active chemical on the TSCA Inventory.
  PFAS are individually listed and subject to manufacturing, processing, and otherwise use reporting thresholds of 100 pounds.
  https://www.epa.gov/toxics-release-inventory-tri-program/addition-certain-pfas-tri-national-defense-authorization-act
Notes: Section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA) adds per- and polyfluoroalkyl substances (PFAS) to the TRI list of reportable chemicals. Additional PFAS may be added to the TRI list for future reporting years due to the automatic addition of PFAS to the TRI list mandated by NDAA Section 7321(c) that occur under certain circumstances.

## Slide 9: Chemical List Changes
For RY 2021, four PFAS have been added to the TRI list of reportable chemicals per the requirements of the NDAA. These are:
  Silver(I) perfluorooctanoate (CASRN 335-93-3)
  Perfluorooctyl iodide (CASRN 507-63-1)
  Potassium perfluorooctanoate (CASRN 2395-00-8)
  2-Propenoic acid, 2-methyl-, 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,11,11,12,12,12-heneicosafluorododecyl ester, polymer with 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,10-heptadecafluorodecyl 2-methyl-2-propenoate, methyl 2-methyl-2-propenoate, 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,11,11,12,12,13,13,14,14,14-pentacosafluorotetradecyl 2-methyl-2-propenoate and 3,3,4,4,5,5,6,6,7,7,8,8,8-tridecafluorooctyl 2-methyl-2-propenoate (CASRN 65104-45-2)
Notes: Per the requirements of section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA), four per- and polyfluoroalkyl substances (PFAS) have been added to the TRI list of reportable chemicals. These additions are effective for the 2021 TRI reporting year. The added PFAS are: silver(I) perfluorooctanoate (335-93-3), perfluorooctyl iodide (507-63-1), potassium perfluorooctanoate (2395-00-8), and 2-propenoic acid, 2-methyl-, 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,11,11,12,12,12-heneicosafluorododecyl ester, polymer with 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,10-heptadecafluorodecyl 2-methyl-2-propenoate, methyl 2-methyl-2-propenoate, 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,11,11,12,12,13,13,14,14,14-pentacosafluorotetradecyl 2-methyl-2-propenoate and 3,3,4,4,5,5,6,6,7,7,8,8,8-tridecafluorooctyl 2-methyl-2-propenoate (65104-45-2).

## Slide 10: Chemical List Changes
For RY 2022, four additional PFAS will be added. These are:
  Perfluorobutane sulfonic acid (CASRN 375-73-5)
  Potassium perfluorobutane sulfonate (CASRN 29420-49-3)
  2-Propenoic acid, 2-methyl-, hexadecyl ester, polymers with 2-hydroxyethyl methacrylate, .gamma.-.omega.-perfluoro-C10-6-alkyl acrylate and stearyl methacrylate (CASRN 203743-03-7)
  Perfluorobutanesulfonate (CASRN 45187-15-3)
Notes: In addition, four PFAS will be added to the TRI list of reportable chemicals effective for the 2022 TRI reporting year.

## Slide 11: Source Reduction Activity Reporting
Effective for RY 2021, the source reduction activity codes have been condensed to improve clarity, better reflect industrial activity, and reduce reporting burden.
  The revised set consists of 24 source reduction activity codes (S codes) corresponding to five source reduction categories.
  From this set of 24 codes, 10 have been designated as green chemistry/green engineering codes.
  These codes and related examples are provided in the P2 Reporting Guide: https://ordspub.epa.gov/ords/guideme_ext/f?p=guideme:gd-title:::::title:p2_reporting_guide
Notes: Effective for RY 2021, the source reduction activity codes have been condensed to improve clarity, better reflect industrial activity, and reduce reporting burden. The revised set of codes consists of 24 source reduction activity codes, or S codes, corresponding to five source reduction categories. Ten of these codes have been designated as green chemistry/green engineering codes.

## Slide 12: Discretionary Authority
Under the Emergency Planning and Community Right-to-Know Act (EPCRA) Section 313(b)(2), the EPA Administrator has the discretionary authority to extend TRI reporting requirements to specific facilities.
The Administrator may determine the application of this authority is warranted on the basis of a chemical’s toxicity, the facility’s proximity to other facilities that release the chemical or to population centers, any history of chemical releases at the facility, or other factors the Administrator deems appropriate.
Notes: Under the Emergency Planning and Community Right-to-Know Act (EPCRA) Section 313(b)(2), the EPA Administrator has the discretionary authority to extend TRI reporting requirements to specific facilities based on a chemical’s toxicity, the facility’s proximity to other facilities that release the chemical or to population centers, any history of chemical releases at the facility, or other factors the Administrator deems appropriate.

## Slide 13: Application of TRI Reporting Requirements to Certain Contract Sterilization Facilities
In December 2021, EPA issued a determination extending TRI reporting requirements to 29 facilities for ethylene oxide (EtO) and, for 16 of those facilities, ethylene glycol.
  These facilities will begin reporting to TRI for the 2022 reporting year; reports will be due by July 1, 2023.
  More information is available on EPA’s Discretionary Authority to Extend TRI Reporting Requirements to Certain EtO Facilities webpage: https://www.epa.gov/toxics-release-inventory-tri-program/epas-discretionary-authority-extend-tri-reporting-requirements
Notes: In December 2021, EPA issued a decision extending TRI reporting requirements to 29 facilities for ethylene oxide and, in some cases, ethylene glycol. These facilities will begin reporting to TRI for the 2022 reporting year.

## Slide 14: Default Percentages for Section 6.1 Transfers
Default POTW distribution percentages for the following chemicals and chemical categories have been updated:
  1-Bromopropane (106-94-5)
  Hexabromocyclododecane (TRI chemical category N270)
  Nonylphenol ethoxylates (TRI chemical category N535)
Notes: Default Publicly Owned Treatment Works (POTW) distribution percentages have been updated for three chemicals and chemical categories – see Table III of the Reporting Forms and Instructions. These chemicals and chemical categories are: 1-bromopropane (106-94-5), hexabromocyclododecane (TRI chemical category N270), and nonylphenol ethoxylates (TRI chemical category N535).

## Slide 15: Addition of Natural Gas Processing Facilities to TRI
In November 2021, EPA finalized a rule to add natural gas processing facilities to the scope of the industrial sectors covered by TRI.
  These facilities will begin reporting to TRI for the 2022 reporting year.
  https://www.epa.gov/chemicals-under-tsca/epa-requires-natural-gas-processing-facilities-report-toxics-release-inventory
Notes: In November 2021, EPA finalized a rule to add natural gas processing facilities to the scope of the industrial sectors covered by TRI. These facilities will begin reporting to TRI for the 2022 reporting year.

## Slide 16: SECTION II: ADVANCED REPORTING GUIDANCE

## Slide 17: Chemicals with 25,000/10,000-pound Reporting Thresholds
A TRI-covered facility must submit a TRI Report for a Section 313 Chemical with 25,000/10,000-pound reporting threshold if:
CHEMICALS WITH 25,000/10,000-POUND REPORTING THRESHOLDS
Manufactured (including imported)
more than 25,000 pounds of the chemical in the reporting year
Processed
more than 25,000 pounds of the chemical in the reporting year
Otherwise Used
more than 10,000 pounds of the chemical in the reporting year
OR
OR
Most of the 800+ chemicals and chemical categories on the Section 313 list are chemicals with 25,000/10,000-pound reporting thresholds. Some chemicals have qualifiers (see the Reporting Forms and Instructions, Table II). Guidance documents for many chemicals are available at: https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-list#chemical.
Notes: Let’s briefly review the threshold quantities that would trigger TRI reporting. For chemicals that are not considered to be Chemicals of Special Concern, the thresholds for manufacturing are 25,000 pounds; for processing, 25,000 pounds; and for otherwise use, 10,000 pounds. These are the thresholds for the majority of the TRI chemicals.
Certain EPCRA section 313 chemicals listed in Table II have parenthetic “qualifiers.” These qualifiers indicate that these EPCRA section 313 chemicals are subject to the section 313 reporting requirements if manufactured, processed, or otherwise used in a specific form or when a certain activity is performed. These qualifiers are listed in Table II of the Reporting Forms and Instructions.

## Slide 18: PFAS Activity Thresholds
A TRI-covered facility must file a TRI Report for PFAS Section 313 chemical if:
PFAS THRESHOLDS
Manufactured (including imported)
more than 100 pounds of the chemical in the reporting year
Processed
more than 100 pounds of the chemical in the reporting year
Otherwise Used
more than 100 pounds of the chemical in the reporting year
OR
OR
176 Section 313 chemicals are PFAS
Notes: For chemicals that are per- or poly-fluoroalkyl substances (PFAS), the thresholds for manufacturing, processing, and otherwise use are 100 pounds.

## Slide 19: Chemicals of Special Concern and Activity Thresholds
100 lb/yr (manufactured, processed, or otherwise used):
  Aldrin
  Hexabromocyclododecane
  Lead*
  Lead compounds
  Pendimethalin
  Polycyclic aromatic compounds (PACs)
  Tetrabromobisphenol A
  Trifluralin
  Methoxychlor
10 lb/yr (manufactured, processed, or otherwise used):
  Chlordane
  Heptachlor
  Mercury
  Toxaphene
  Isodrin
  Polychlorinated biphenyls
  Benzo[g,h,i]perylene
  Hexachlorobenzene
  Mercury compounds
  Octachlorostyrene
  Pentachlorobenzene
0.1 g/yr (manufactured, processed, or otherwise used):
  Dioxin and dioxin-like compounds
Chemicals of Special Concern are subject to separate, lower activity thresholds (See 40 CFR § 372.28).
*Excluding lead in stainless steel, brass, or bronze alloys
Notes: The actual threshold quantities that trigger reporting vary depending on the chemical. For eight of the chemicals, the threshold is 100 pounds per year. For those chemicals that are considered to be highly persistent and bioaccumulative, the threshold is 10 pounds per year. And for dioxin and dioxin-like compounds, the threshold is 0.1 grams per year, which reflects the highly toxic nature of this chemical category. For Chemicals of Special Concern, the threshold quantities are the same for manufacturing, processing, and otherwise use.

## Slide 20: Threshold Guidance
Remediation
  Chemicals being remediated are not manufactured, processed, or otherwise used.
  Chemicals used to remediate waste ARE counted as otherwise used.
  Chemicals manufactured when treating or remediating waste ARE counted toward manufacturing threshold
Treatment of wastes generated on-site
  Wastes brought in from off-site for treatment or other management count towards the otherwise use threshold.
Storage
These activities do not constitute threshold activities, but are not exempt from reporting if threshold is exceeded through other activities unless specifically eligible for one of the reporting exemptions.
Chemicals coincidentally manufactured during waste treatment or remediation must be considered.
Recycling on-site for use on-site
Transferring chemicals off-site for further waste management (except off-site transfers for recycling)
  Chemicals sent off-site for recycling are counted as processed.
The following activities are not considered “manufacturing,” “processing,” or “otherwise use”:
Notes: Now we will go over some reminders regarding threshold calculations. Facilities should be aware that there are some activities that are not considered to be threshold activities under TRI. In other words, the activities are not considered manufacturing, processing, or otherwise use. None of the TRI chemicals undergoing these activities would need to be considered towards an activity threshold. These activities are shown here and include: remediating chemicals; treating chemicals in waste generated on-site; storing chemicals; recycling on-site for use on-site; and transfers sent off-site for further waste management, not including recycling.
For example, let’s say a facility stores 50,000 pounds of a chemical on-site. The act of just storing that chemical is not a threshold activity. It’s not manufacturing. It’s not processing. It’s not otherwise use. However the fact that they are storing the chemical on-site probably means that they are also using it in their process. At some point they will pull quantities out of storage and process or otherwise use it in their production process. At that point, they are processing the quantity of the chemical removed from storage, and that quantity gets counted towards their processing threshold. However, if the facility were to stop making a certain product line and continued to store the chemical for the reporting year and never used it, they would not need to consider it towards any threshold.
Facilities should be aware that while these activities are not threshold activities, that is not the same as being exempt from TRI. The activities listed here are not exempt from reporting; but they are not counted toward the threshold determination. However, if a TRI activity threshold is exceeded in some other manner at the facility, then the reporting requirement has been triggered, and any release or waste management associated with the non-threshold activities must be included in the reported quantities for release and waste management for the chemical.
Also, note that TRI chemicals that are coincidentally manufactured, or unintentionally manufactured, during waste treatment or remediation must be considered in manufacturing threshold amounts.

## Slide 21: Threshold Guidance: Combustion
Section 313 chemicals may be coincidentally manufactured during combustion of:
  Oil
  Coal
  Natural gas
  Waste
  Other materials
Includes acid aerosols and metal compounds manufactured as by-products of fuel combustion
Any Section 313 chemicals in fuels combusted for energy are considered otherwise used.
Notes: Some industrial activities may involve more than one TRI threshold activity. For example, combustion can trigger thresholds for both manufacture and otherwise use. Here is some guidance on combustion. Many facilities have on-site combustion processes where TRI chemicals may be present in fuels used, and may be coincidentally manufactured during the combustion of oil, coal, natural gas, waste or other materials. Any TRI chemical in the fuel is considered otherwise used and the quantity would be applied towards the otherwise use threshold. Any TRI chemical generated when the fuel is combusted is considered coincidentally manufactured and the quantity would be applied to the manufacturing threshold. Common TRI chemicals coincidentally manufactured during combustion include acid aerosols, such as sulfuric acid aerosols. Metal compounds are also coincidentally manufactured as byproducts of fuel combustion.
So, when combusting fuels and other materials, be sure to consider both aspects of the combustion process: How much of each TRI chemical is otherwise used, and how much is manufactured?
Note that the non-Chemicals of Special Concern in the fuel otherwise used is eligible for the de minimis exemption, and many of the TRI chemicals found in fuels DO exist below de minimis concentrations. However, TRI chemicals that are coincidentally manufactured during combustion will not fall under the de minimis exemption.

## Slide 22: Exemptions
TRI regulations provide exemptions for specific scenarios.
These exemptions allow for a facility to not consider quantities of toxic chemicals for certain threshold determinations and waste management calculations.
To learn more about TRI exemptions, please visit:
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-list#exemption
Exemption List
Articles
De Minimis
Coal Extraction
Intake Air and Water
Laboratory Activities
Janitorial or Facility Grounds Maintenance
Metal Mining Overburden
Motor Vehicle Maintenance
Operators of Establishments on Leased Property
Owners of Leased Property
Personal Use
Structural Component of the Facility
Notes: TRI regulations provide exemptions for specific scenarios. These exemptions allow for a facility to not consider quantities of toxic chemicals for certain threshold determinations and waste management calculations. The available exemptions are listed on the slide. To learn more about TRI exemptions, please visit the website shown on this slide. The website includes an explanation for each exemption.

## Slide 23: Exemption Guidance
Reminder:
  Even where your activity is covered by an “otherwise use” exemption such as motor vehicle maintenance, if Section 313 chemical are manufactured as by-products, coincidentally as impurities, or otherwise manufactured, they must be considered toward the manufacturing threshold.
  Section 313 chemicals in fuels added to motor vehicles as part of the facility’s service or product do not qualify for the motor vehicle maintenance exemption.
  Laboratory activities exemption only applies to certain activities that take place in a laboratory, and they must be under the direct supervision of a technically qualified individual.
Notes: The Basics Concepts module of the online training goes into more detail on each of the TRI exemptions, but here we have a few reminders.
Any TRI chemicals contained in fuels combusted are otherwise used and count toward the otherwise use threshold. And those TRI chemicals coincidentally manufactured during combustion must be considered towards the manufacturing threshold. This is true even if the activity is covered by an “otherwise use" exemption such as motor vehicle maintenance. If TRI chemicals are manufactured as by-products, coincidentally as impurities, or otherwise manufactured, they must be considered toward the manufacturing threshold.
The TRI chemicals in fuels added to motor vehicles not just meant to be operated by the facility, do not qualify for the motor vehicle maintenance exemption. They would be considered towards the processing threshold and this exemption only applies to the otherwise use of TRI chemicals. For example, some facilities that manufacture vehicles add a few gallons of fuel before the vehicles leave the facility for distribution into commerce. Because those vehicles and the fuel in them are part of the facilities product going into commerce, the chemicals in the fuel are considered processed.
Similarly, the laboratory activities exemption applies to TRI chemicals that are manufactured, processed, or otherwise used in certain activities that take place in a laboratory. Facilities should take care not to apply this exemption more broadly than it should be. If an activity involving a TRI chemical takes place in a laboratory, it does NOT mean that it is necessarily exempt. Only certain activities are exempt.

## Slide 24: Metals and Metal Compound Category
Elemental metals (metals in their neutral state) and their corresponding metal compound categories are listed separately under Section 313.
  Separate activity threshold determinations.
  Report for each listing (e.g., nickel or nickel compound) only if the threshold for each listing is exceeded.
  For metal compounds calculations:
    Use full compound mass for threshold determination.
    Use only parent metal mass for release and waste quantities.
  If threshold exceeded for both the elemental metal and metal category compound (e.g., nickel and nickel compounds), you may report separately or file one combined report.
    If combined, file as metal and metal category compound.
    The reason both the elemental metal and its compound may be reported on the same form is that while the entire weight of the compound is used to determine the threshold, only the amounts of the parent metal are reported.
Notes: Now we will move on to some other chemicals that have unique reporting requirements for which reporting errors more frequently occur. First, let’s look at the unique requirements associated with reporting for metals and metal compound categories. Note that metals and metal category compounds are separately listed under TRI. They each have a separate activity threshold determination – report on the metal only if the threshold for the metal is exceeded, and report for the metal compound only if the threshold for the metal compound is exceeded.
So if a facility handles elemental nickel and nickel compounds at their facility, they should look at the two separately when determining if they need to report. They look at the elemental nickel and see if they manufacture, process, or otherwise use quantities exceeding the threshold for nickel. Separately, they look at their nickel compounds and see if the quantity manufactured, processed, or otherwise used exceeds the threshold for nickel compounds. They look at the two as unrelated chemicals.
However, if the thresholds are exceeded for both the elemental metal and for the metal compound – for example, both for nickel and for nickel compounds, then the facility my submit two separate reports or one combined report for the compound category. Combined reports for elemental metals and metal compounds will need to indicate they are reporting for both under this combined form. So, if the facility exceeded the threshold for nickel and they exceeded the threshold for nickel compounds, they could file a combined report for both elemental nickel and nickel compounds.

## Slide 25: Cyanide Compounds and Hydrogen Cyanide
Cyanide compounds have the form X+CN- where X = any other group (except H+) where a formal dissociation can be made. For example, KCN or Ca(CN)2
  Includes metal (cyanometalates, such as ferricyanides) and non-metal (such as ammonium cyanide) dissociative cyanide complexes
  For threshold determinations, use weight of the entire compound
  For release and other waste management reporting, report weight of entire compound
Hydrogen cyanide (74-90-8)
  An individually listed toxic chemical
  The Corrections to TRI Reporting Requirements rule clarified that hydrogen cyanide is not part of the cyanide compounds category.
Notes: Cyanide compounds are a listed chemical category that includes the cyanide ion and any group where a formal dissociation can be made. When reporting for cyanide compounds, full weight of the compound must be used for both threshold determinations as well as releases and other waste management reporting. This requirement is different from that of metal compound categories and nitrate compound categories where only the metal or nitrate ion is included for calculating releases and other waste management.
Hydrogen cyanide is an individually listed chemical. While hydrogen cyanide meets the structural definition of cyanide compounds, current EPA guidance is to not count hydrogen cyanide as part of cyanide compounds for thresholds and release and waste management reporting.

## Slide 26: Metal Cyanide Compound Guidance
For reporting the metal category compounds, such as cadmium compounds:
  For threshold determinations, use entire weight of compound.
  For release and other waste management reporting, report only the weight of metal portion of the compound.
For cyanide compounds
  For threshold determinations, use weight of entire compound.
  For release and other waste management reporting, report weight of entire compound.
Category description for cyanide compounds states: X+CN- where X+ = any group (except H+) where a formal dissociation can be made. For example, KCN or Ca(CN)2
*
A metal cyanide compound, such as cadmium cyanide, requires separate reporting under both the corresponding metal category compound and cyanide compounds*.
Notes: Metal cyanide compounds, more formally called cyanometalates, are reportable under both the metal compound categories and the cyanide compounds category. Facilities that manufacture, process, or otherwise use a metal cyanide compound need to consider if they exceed the threshold under the cyanide compound category and also under the corresponding metal compound category.
For example, if a facility processes cadmium cyanide, they need to consider if reporting is required under both cadmium compounds and cyanide compounds. In this example, they would use the entire weight of the cadmium cyanide for the cadmium compound category threshold determination and only the weight of the metal portion of the cadmium for the release and waste management reporting. For the cyanide compounds category, they would also use the entire weight for the cadmium cyanide in the threshold determination, just like for the metal compound. However, for the release and other weight management reporting, they also use the entire weight of the cadmium cyanide for reporting under the cyanide compounds category.

## Slide 27: Nitrate Compounds Category
Qualifier: “Water dissociable; reportable only when in aqueous solution”
  For threshold determinations, use weight of entire nitrate compound.
  Calculate only weight of nitrate ion portion when reporting releases and other waste management quantities on Form R.
Common nitrate compounds sources
  Nitrate compounds are produced most commonly when nitric acid is neutralized or in biological treatment of wastewater.
  Nitrate compound releases to surface water may result from stormwater run off.
  Exemption may apply for nitrates in intake water (used for processing or non-contact cooling).
v
v
Notes: The nitrate compounds category also deserves special consideration.
The TRI chemical category is actually ‘water dissociable nitrate compounds’. So, nitrate compounds are only reportable when they are in an aqueous solution.
Nitrate compounds are treated much like metal compounds under TRI. When calculating whether a reporting threshold was exceeded, facilities use the weight of the entire nitrate compound to see if they have manufactured or processed more than 25,000 pounds, or otherwise used more than 10,000 pounds.
If one of these thresholds is exceeded, a TRI form is required. When estimating the quantities released or managed as waste, use only the weight of the nitrate ion portion of the compound. A common error is using the whole weight of the nitrate compound in the release and waste management estimates, and thereby, over-reporting the quantities released or the quantities managed as waste.
Nitrate compounds are most commonly produced when nitric acid is neutralized, or in biological treatment of wastewater. Note that there is an exemption for the otherwise use of TRI chemicals contained in intake water that is used for processing or non-contact cooling.

## Slide 28: Quiz #1: Question 1
A facility processes 200,000 lb of a mixture containing 10% zinc chromate and 15% chromium dioxide by weight.
For which of the following chemical categories was the processing threshold exceeded?
A. Chromium compounds only
B. Zinc compounds only
C. Neither
D. Both

## Slide 29: Quiz #1: Question 2
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby water body.
The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. One mole of HNO3 generates one mole of NaNO3.
Does the facility exceed the manufacturing threshold for nitrate compounds?
Select Yes or No

## Slide 30: Quiz #1: Question 3
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby water body.
The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. One mole of HNO3 generates one mole of NaNO3. The MW of the nitrate ion NO3 = 62.
In this example, should the facility report release of 27,000 lb of nitrate compounds into a stream or water body (Section 5.3 on Form R)?
Select Yes or No

## Slide 31: Ammonia Guidance
Ammonia
  Aqueous ammonia - threshold determination and release and other waste management quantity calculations for aqueous ammonia from any source (i.e., anhydrous ammonia placed in water or water dissociable ammonium salts) is based on 10% of the total ammonia present in aqueous solutions.
  Anhydrous ammonia - include 100% for thresholds and releases
    Including air releases from aqueous ammonia
  Amounts from aqueous sources and anhydrous sources get added together for threshold determinations and ammonia reports.
v
Notes: Ammonia also has some unique requirements. For aqueous ammonia, your threshold determination and your release and waste management quantity calculations are based on 10% of the ammonia present in the aqueous solutions. Remember that the 10% applies only to aqueous solutions. If you have anhydrous ammonia you need to consider 100% for thresholds and releases.

## Slide 32: Ammonia Calculation Examples
In a calendar year, a facility places 25,000 pounds of anhydrous ammonia in water for processing and processes 25,000 pounds of aqueous ammonia from an ammonium salt.
The facility must include all of the 25,000 pounds of anhydrous ammonia in the determination of the processing threshold, but only 10 percent (or 2,500 pounds) of the aqueous ammonia from the ammonium salt in the processing threshold determination.
In a calendar year, a facility uses 30,000 pounds of anhydrous ammonia to neutralize acids in a wastewater stream. The neutralized waste stream (containing aqueous ammonia from dissociated ammonium salts) is then transferred to a POTW.
The quantity to be applied toward threshold determinations is the total quantity of anhydrous ammonia used in the waste stream neutralization, or 30,000 pounds. The quantity of ammonia reported as transferred is 10 percent of the total quantity of aqueous ammonia transferred, or 3,000 pounds.
Notes: Two examples of calculating thresholds and releases of anhydrous and aqueous ammonia are provided on the slide. These examples are from the Ammonia guidance document.

## Slide 33: Acid Aerosols
Hydrochloric and sulfuric acids have a chemical qualifier….They are reportable only if in the aerosol form.
  These aerosols are common combustion products of coal and other fuels combustion (includes mists, vapors, gas, fog, and other airborne forms of any particle size).
Threshold determination for closed-loop reuse systems that generate acid aerosol:
  Acid aerosols are manufactured and otherwise used .
  Applicable for sulfuric and hydrochloric acid only.
Total Amount of Acid in Reuse System
Total Virgin Acid Added in RY
Amount Acid Aerosols Manufactured/ Otherwise Used
Closed-loop Acid Reuse System
+
=
See EPA’s Guidance for Reporting Sulfuric Acid and Guidance for Reporting Hydrochloric Acid for specific calculations
*
Notes: Acid aerosols are also chemicals with unique requirements. Note that both hydrochloric and sulfuric acids have a chemical qualifier that specifies that they are reportable only if they are in the aerosol form. These aerosols are common products of coal and other fuel combustion. For example, sulfuric acid can be coincidentally manufactured when combusting fuels containing sulfur.
Hydrochloric and sulfuric acids are also used by facilities in closed-loop acid reuse systems. In some cases the acid can be aerosolized to apply it to a material or product for the purpose of etching or cleaning. The acid aerosol is typically condensed back to liquid only to be re-aerosolized again and again. Because of the chemical qualifier, facilities would be manufacturing the TRI chemical every time it is aerosolized and otherwise using it again and again in the process.
EPA developed a simplified method for determining whether a threshold has been exceeded. The guidance directs facilities to calculate their threshold quantity by adding the total amount of acid in the reuse system plus the total virgin acid added in the reporting year to get the threshold quantity manufactured and otherwise used.
EPA has developed two separate reporting guidance documents for sulfuric acid and hydrochloric acid where facilities can get more information pertaining to these chemicals.

## Slide 34: Chemical Migration Guidance
Migration of a Section 313 chemical contained in waste disposed or released from one environmental medium to another within the reporting year:
  For example, volatilization from a landfill
  Release estimates must be calculated and reported for all media in Part II, Sections 5, 6, and 8 of Form R.
1,000 lb to air
(Form R: 1,000 lb in Section 5.1)
2,000 lb to surface impoundment
(Form R: 1,000 lb in Section 5.5.3B)
Year 1
Year 1
Notes: Now we will discuss EPA’s Guidance on how to report chemicals that migrate from their initial disposal or release location. Shown is an example of a reportable chemical that is disposed of in an on-site surface impoundment.
If in Year One, a facility placed 2,000 pounds of the chemical into a surface impoundment, and in the same year, 1,000 pounds volatilized to the air, the facility would put the 1,000 pounds to air on their Form R as an air release. And 1,000 pounds would be reported on the Form R as disposed of in the surface impoundment, not 2000 pounds. When the initial disposal and subsequent migration occur during the same reporting year, facilities should put each amount in the appropriate section of the form to show the medium that it actually ended up in.

## Slide 35: Chemical Migration Guidance
Migration of a Section 313 chemical contained in waste disposed or released from one environmental medium to another within the reporting year:
  For example, volatilization from a landfill
  Release estimates must be calculated and reported for all media in Part II, Sections 5, 6, and 8 of Form R.
500 lb leachate in year 2
Not reported on Year 2 Form R
2,000 lb to surface impoundment
(Form R, Section 5.5.3B)
Year 1
Year 2
Notes: However, if chemical migration occurs in a subsequent year from the initial disposal, the chemical migration should not be reported. Facilities are only required to report amounts released or otherwise managed in the year that the amounts were released or otherwise managed.
For example, in Year One, 2000 pounds of this chemical were disposed of in the on-site surface impoundment. That 2000 pounds will go on your Form R as an on-site land disposal, under the surface impoundment section. A year later, leachate has migrated from this surface impoundment, and you know that 500 pounds of the original 2000 pounds has migrated out of the impoundment. Because the migration occurred in a different reporting year, the 500 pounds does not get reported on the Year Two Form at all. It was already reported the previous year in the 2000 pounds disposed to land on-site.

## Slide 36: EPA Compliance Incentives
The Agency implements policies that reduce or waive penalties under certain conditions for facilities that discover, disclose, correct, and prevent future violations.
Current Compliance Incentive Policies, Guidance, and Audit Protocols can be found by visiting:
  https://www.epa.gov/compliance/audit-protocols
V v
Notes: Compliance Incentives are a set of policies and programs that eliminate, reduce, or waive penalties under certain conditions for business, industry, and government facilities which voluntarily discover, promptly disclose, correct noncompliance, and prevent future environmental violations. Information about these incentives, self-disclosure programs, related tools such as environmental audit protocols, Environmental Management Systems, Pollution Prevention, other innovation projects and programs and the environmental benefits achieved by such programs can be found at the website shown here.

## Slide 37: EPA Self-Disclosure Audit Policy
Conditions to qualify (nine criteria):
Systematic Discovery of the Violation Through Environmental Audit or the Implementation of a Compliance Management System
Voluntary Discovery
Prompt Disclosure
Discovery and Disclosure Independent of Government or Third Party Plaintiff
For more information, including a copy of the Audit Policy visit:
  https://www.epa.gov/compliance/epas-audit-policy
Correction and Remediation
Prevent Recurrence
No Repeat Violations
Other Violations Excluded
Cooperation
v
1
v
2
v
3
v
4
v
5
v
7
v
8
v
9
v
6
V v
Notes: Conditions to qualify for the Audit Policy are as follows. The violation had to be from a systematic discovery through an environmental audit or due diligence. It has to have been a voluntary discovery made by the facility. The facility must promptly disclose the violation to the Environmental Protection Agency and the discovery disclosure must be independent of a government or third party plaintiff.
The facility must fix the problem to prevent it from recurring and this audit policy cannot be used repeatedly for the same violations. It only covers the violations for which you are reporting. If other violations are identified over the course of using the audit policy, they may not be covered. You have to cooperate fully with the EPA and other authorities. More details on the audit policy are available from the EPA Website at the address shown here.

## Slide 38: EPA Self-Disclosure Audit Policy
EPA Compliance Incentive Policy available only to small businesses
  Small businesses employ 100 or fewer individuals across all facilities and operations.
Small businesses that meet all four conditions of the policy may have 100% of the gravity-based penalty waived. However, EPA reserves the option to collect any significant economic benefit which may have been realized by the facility.
Conditions to qualify (four criteria):
For more information, including a copy of the Small Business Compliance Policy and a Q&A document, visit:
  https://www.epa.gov/compliance/small-business-compliance
Good Compliance Record
Voluntary Discovery
Prompt Disclosure
Correction and Remediation
v
1
v
2
v
3
v
4
V v
Notes: EPA offers a compliance incentive policy to small businesses that self-disclose violations. The Small Business Compliance Policy is only available to businesses with 100 or fewer employees. If a small business meets the conditions, they may be eligible for 100 percent reduction in the gravity-based penalty. The conditions to qualify are: a good compliance record, voluntary discovery of the violation, prompt disclosure, and correction and remediation of the violation. More information on the Small Business Compliance Policy can be found at the website shown here.

## Slide 39: Revising TRI Data
Revised TRI data that are not trade-secret must be submitted using TRI-MEweb through the Internet via EPA’s CDX. You may only revise back to RY 1991.
If your state or tribe participates in the TRI Data Exchange (TDX) then submitting via CDX to EPA will also satisfy your obligation to report to the state or tribe in which your facility is located if the revision is for RY 2005 through the present reporting year. Otherwise, revisions must also be submitted in the state- or tribe-specified format. To determine if your state or tribe is in TDX go to:
  https://www.epa.gov/toxics-release-inventory-tri-program/tri-data-exchange
v
Notes: The Electronic Reporting rule requires that revisions must made electronically using TRI-MEweb via EPA’s Central Data Exchange. TRI-MEweb now supports revisions for all Reporting Years from 1991 through the present.
Be aware that when submitting revisions to forms for Reporting Year 2005 through the present reporting year via the Central Data Exchange to EPA, it will satisfy your state obligations only for states that participate in the TRI Data Exchange. For states and tribes that do not participate in TDX and revisions for Reporting Years from 1991 to 2004, facilities must remember to also submit the revision to the state/tribe, such as on a diskette or hardcopy.

## Slide 40: Withdrawing TRI Data
You must use TRI-MEweb to withdraw a TRI form (except for trade secrets). You may withdraw forms back to RY 1991.
For more information regarding withdrawals, go to the following tutorial:
  https://www3.epa.gov/tri/tutorials/TRIT-33/
Please be aware if your state or tribe is a TRI Data Exchange (TDX) participant, submitting to EPA via CDX will also satisfy your state obligations for reporting years back to 2005. For states or tribes that are not TDX participants, withdrawals should also be submitted in the specified format for the state/tribe.
v
Notes: The Electronic Reporting rule requires that withdrawals must be made electronically via the Central Data Exchange using TRI-MEweb. Information on how to properly submit TRI data withdrawal requests can be obtained from TRI-MEweb or from the website shown here. As with revisions, submitting withdrawal forms for Reporting Year 2005 through the present reporting year via the Central Data Exchange will only fulfill state obligations for those states and tribes that are TDX participants.

## Slide 41: Submitting Revisions and Withdrawals
Form R submitted to replace previously filed Form A Certification Statement.
  You must withdraw the previously filed Form A Certification Statement and then submit a Form R. The Form R is considered to be a late submission if submitted after the reporting deadline.
For a change in chemical reported (including a metal to a metal compound), you must withdraw the original submission and re-submit for the new chemical. This is not a revision.
EPA may audit revisions or withdrawals at any time.
V v
Notes: Here are a few more reminders regarding revisions and withdrawals. If submitting a Form R to replace a previously filed Form A, this is not considered a revision (do not check the revision box). It is considered a late submission of Form R. You would also need to request that the Form A be withdrawn.
Note that submitting a Form A when a Form R is required is considered a less severe violation than failing to submit either form, but it is considered a late submission.
A common revision is to change the chemical reported from a metal to a metal compound or vice versa. In that case, the original submission must be withdrawn and the form for the new chemical should be submitted. This is not considered a revision.

## Slide 42: EPCRA Section 313 Enforcement
Owners and operators of covered facilities violating any statutory or regulatory requirement are subject to penalties of up to $40,779 per day per violation (periodically adjusted for inflation).
Owners and operators of covered facilities subject to citizen suits could also be liable for attorney fees and litigation costs (EPCRA § 326(f)).
Government’s penalty for Section 313 of EPCRA is determined by applying the statutory penalty factors as described in the Enforcement Response Policy (ERP) to each violation.
  For EPA’s EPCRA enforcement policies, see:
    https://www.epa.gov/sites/production/files/2017-03/documents/epcra313erpamendments2017.pdf
Notes: Companies violating any statutory or regulatory requirement are subject to penalties of up to $40,779 per day per violation. The government’s Enforcement Response Policy is what is used to determine what the penalty will be. More information on EPA EPCRA enforcement policies can be found at the website shown here.

## Slide 43: SECTION III: DETAILED GUIDANCE FOR CHEMICALS OF SPECIAL CONCERN

## Slide 44: Chemicals of Special Concern
Organic Compounds:
  Benzo[g,h,i]perylene, Dioxin and dioxin-like compounds category, Hexabromocyclododecane, Hexachlorobenzene, Octachlorostyrene, Pentachlorobenzene, Polycyclic aromatic compounds (PAC) category, Polychlorinated biphenyls, and Tetrabromobisphenol A
Metals
  Mercury, Mercury compounds category, Lead, and Lead compounds category
Pesticides:
  Aldrin, Chlordane, Heptachlor, Isodrin, Methoxychlor, Pendimethalin, Toxaphene, Trifluralin
Chemicals of Special Concern are subject to separate, lower reporting thresholds and different reporting requirements than the other TRI chemicals.
  Facilities must use Form R (cannot use Form A)
  Quantities can be reported in decimal amounts.
  Cannot use range codes
  Cannot use the de minimis exemption
Notes: Chemicals of Special Concern are those chemicals that are persistent, bioaccumulative, and toxic, meaning that they’re persistent in that they don’t break down in the environment. They’re bioaccumulative in that they tend to accumulate in living tissue, and they’re toxic chemicals. So because of these characteristics, these chemicals have much lower reporting thresholds and they have unique reporting requirements under TRI.
Here are the 21 chemicals that are designated as Chemicals of Special Concern. Nine are organic compounds, two are metals and two are metal compounds, and eight are pesticides. Several of these Chemicals of Special Concern are either banned or severely limited in their use.
The threshold quantity that would trigger reporting for Chemicals of Special Concern varies depending upon the individual chemical. However, when reporting for any of the Chemicals of Special Concern the Form R must be used, quantities reported can include decimal amounts, range codes are not allowed, and you cannot use the de minimis exemption.

## Slide 45: Dioxin and Dioxin-like Compounds
Dioxin and dioxin-like compounds are reported in grams.
The manufacture, process, or otherwise used activity thresholds are 0.1 gram.
Dioxins formed as unwanted by-products when chlorinated materials are involved in combustion or other high-temperature processes, such as:
  Fossil fuel and wood combustion
  Waste incineration
  Metallurgical processes
What it takes to exceed the 0.1 gram activity threshold?
  64,462 tons of coal combusted in a utility boiler
  8.31 million gallons of fuel oil combusted in a utility boiler
  1,230 tons of copper scrap fed to a secondary copper smelter
v
Notes: “Dioxin and Dioxin-like Compounds” is a Chemicals of Special Concern category and, unlike any other TRI chemicals, dioxin and dioxin like compounds are reported using gram units. The dioxin and dioxin-like compound category has a Chemicals of Special Concern activity threshold of 0.1 grams for a reporting year. Facilities manufacturing, processing or otherwise using 1/10th of a gram of dioxin or dioxin-like compounds, would report for this chemical category.
Dioxins can be formed as byproducts when chlorinated materials are involved in combustion or other high-temperature processes. Examples of such processes where dioxins may form include: fossil fuel and wood combustion, waste incineration, or metallurgical processes.
What does it take to exceed a 0.1 gram activity threshold? The list shown here is from the dioxin and dioxin-like compounds guidance document. Using typical concentrations, 64,462 tons of coal combusted in a utility boiler in the reporting year would exceed the dioxin threshold. 8.31 million gallons of fuel combusted would exceed the threshold, again, at typical concentrations of dioxins. Or 1,230 tons of copper scrap fed into a secondary copper smelter would exceed the dioxin threshold.

## Slide 46: Dioxin and Dioxin-like Compounds
Dioxin and dioxin-like compounds category is composed of 17 individually listed compounds.
  In addition to the total mass grams released for the entire chemical category, facilities that have the data are required to report the quantity of each of the 17 individual members, which must add up to the total mass for the category.
Dioxin and Dioxin-like Compounds Toxicity Equivalency (TEQ)
  Each compound has an assigned Toxic Equivalency Factors (TEFs) that is multiplied with the compound mass to yield TEQ.
  TEQ for each of the compounds are summed to provide a category TEQ.
  TEQ values are made available to the public along with mass data.
Emission factors, listed compounds, TEFs, and other guidance:
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-title:::::title:dioxin
v
Notes: The dioxin and dioxin-like compounds category is composed of 17 individually listed compounds.
In addition to reporting the total amount of this chemical category in grams, facilities must also report the quantity in grams of each of the 17 individual compounds in the category, if this information is available. Emission factors for dioxin and dioxin-line compounds are typically for individual compounds within the category.
EPA will use the quantities reported to calculate the Toxicity Equivalency Values, or TEQ values, for the dioxin and dioxin-like compounds reported. This information will be made available to the public along with the mass values reported. The dioxin and dioxin-like compounds guidance document has additional information about this category, including the listed chemicals and commonly used emission factors.

## Slide 47: Lead and Lead Compounds
Raw materials processed by a variety of facilities may contain metallic lead or lead compounds:
  Metal ores
  Coal
  Wood
  Oil & Oil products: heating oils, gasolines
Lead used in solder and other alloys is in the elemental NOT the compound form (i.e., this is lead, not a lead compound).
Lead-acid batteries will typically meet the articles exemption.
Sending old paint containing lead off-site for disposal or treatment is not a threshold activity.
Other sources of lead and lead compounds for Chemicals of Special Concern threshold:
  Lead solder, lead babbitt, castings/molds, contaminants of aluminum and other common base alloys, X-Ray film
  Cement, asphalt, graphite brushes, leaded glass
  Transfers of lead and lead compounds off-site for recycling
v
Pb
Notes: “Lead and Lead Compounds” can be found in a variety of raw materials, such as in metal ores, coal, wood, and in oil products such as heating oils and gasoline.
Lead is also found in circuit board facilities where it is used as solder. And, lead is found in many metal alloys. Lead in solder and alloys is in the elemental, not the compound form. So, facilities using lead solder and metal alloys should consider the quantities of elemental lead in these materials.
Lead acid batteries would typically meet the articles exemption, assuming there are no TRI chemical releases associated with the lead acid batteries.
Old paint can also contain lead. However, removing old paint containing lead and sending it off-site for disposal or treatment is not considered a threshold activity under TRI. Simply transferring a waste containing a TRI chemical off-site for waste management other than recycling is not in itself a threshold activity.

## Slide 48: Lead and Lead Compounds
Chemicals of Special Concern activity threshold for lead and lead compounds:
  100 pounds for lead (not contained in stainless steel, brass, or bronze)
  100 pounds for lead compounds
25,000/10,000-Pound reporting thresholds apply to lead contained in stainless steel, brass, or bronze.*
  25,000-pound thresholds for manufacturing or processing
  10,000-pound threshold for otherwise use
  0.1% de minimis limit applies to lead contained in stainless steel, brass, or bronze
If elemental lead is removed from the qualified alloy, such as vaporization during melting of an alloy, the 100 lb threshold applies.
*
v
Under TRI, lead is classified as a Chemical of Special Concern except for lead contained in stainless steel, brass, and bronze alloys
v
Notes: Elemental lead that is not contained in stainless steel, brass or bronze alloys is considered a Chemical of Special Concern and has a 100 pound threshold. The lead compounds category always has a 100-pound threshold.
There is also a 25,000/10,000-pound reporting thresholds for lead and that applies only to lead that is contained in stainless steel, brass, or bronze: 25,000 pounds for manufacturing and processing, and 10,000 pounds for otherwise use.

## Slide 49: Lead Threshold Determination Flow Chart
Notes: Because there are two different ways to look at lead, for facilities that have both lead in stainless steel, brass and bronze, AND lead not in these alloys, this flowchart can be helpful in determining which thresholds have been exceeded and what reporting requirements apply.
The first step is to quantify all of the lead manufactured processed or otherwise used at the facility, including lead in stainless steel, brass, or bronze and lead in the Chemicals of Special Concern form. If so, the lead in these alloys is not a Chemical of Special Concern and compare that to the thresholds of 25,000 and 10,000 pounds. Then the facility looks only at lead not in stainless steel, brass, or bronze and compares that to the 100 pound threshold for the Chemicals of Special Concern form of lead.
Following this flow chart, if neither threshold is exceeded, then no reporting is required. If only the threshold for the Chemicals of Special Concern form of lead is exceeded then the facility is only required to report on the lead not in stainless steel, brass, or bronze and cannot use a Form A and must follow the reporting requirement specific to Chemicals of Special Concern.
If only the 25,000/10,000-pound reporting thresholds lead is exceeded, then the facility reports on both the lead in the stainless steel, brass or bronze and the lead not in these alloys, and they follow the reporting requirements for Chemicals with 25,000/10,000-pound Reporting Thresholds, including the use of the Form A, if they meet those criteria.
Finally, if both the thresholds for the Chemicals of Special Concern form of lead and for the chemicals with 25,000/10,000-pound reporting thresholds form of lead are exceeded, then the flowchart shows that the facility must report using a Form R on both forms of lead and must follow the reporting requirements for Chemicals of Special Concern.

## Slide 50: Quiz #2: Question 1
A facility combusts 13,600,000 lb of coal to fire its boilers. The coal contains elemental lead (Pb) at 7.0 ppm by weight. In combusting the coal, the facility otherwise uses lead and coincidentally manufactures lead compounds. The facility has no other information about the chemical makeup of the lead compounds manufactured and assumes it is the lowest-weight oxide - PbO. Based on molecular weights (Pb = 207, PbO = 223), the facility knows that 223 lb of PbO is formed for every 207 lb Pb used.
Which of the following thresholds have been exceeded for lead or lead compounds?
A. Otherwise Use only
B. Manufacturing only
C. Neither
D. Both

## Slide 51: Quiz #2: Question 2
The facility in the previous question combusted 13,600,000 pounds of coal in the reporting year and has exceeded the reporting threshold for lead compounds. The facility has no monitoring data on their point source lead emissions from combusting the coal. They determined that their best available information for calculating their point source air emissions is the published emission factor for lead from controlled coal combustion from EPA’s AP-42* which is 4.2E-04 lb Pb/ton of coal combusted.
What are the facility’s point source emissions of lead from coal combustion?
A. 2.86 lb
B. Range Code ‘A’
C. 95.2 lb
D. Either 2.86 lb or Range Code ‘A’

## Slide 52: Polycyclic Aromatic Compounds (PACs) and Benzo[g,h,i]perylene
Chemicals of Special Concern activity threshold
  PACs category threshold: 100 pounds
  Benzo[g,h,i]perylene threshold: 10 pounds
Present in coal, fuel oil, other petroleum products, such as asphalt and roofing tars
Asphaltic concrete (blacktop) typically contains 4 - 10% paving asphalt
Some uses of paving asphalt (blacktop) are NOT EXEMPT
  Paved process areas and roads for process vehicles (e.g., on-site haul trucks) – NOT EXEMPT
  Employee parking lot and non-processes access roads – EXEMPT
See also EPA’s PACs and Persistent Bioaccumulative Toxic (PBT) guidance
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-title:::::title:pacs
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-title:::::title:pbts
Notes: Polycyclic Aromatic Compounds (PACs) and benzo(g,h,i)perylene are both Chemicals of Special Concern. The PACs have a 100 pound threshold. Benzo(g,h,i)perylene has a 10 pound threshold. These chemicals are usually found in the same sources including in coal, fuel oil, petroleum products, and roofing tars. These chemicals can also be coincidentally manufactured during the combustion of fossil fuels.
Because they are found in asphalt, they are typically present in blacktop. Blacktop used for paving an employee parking lot is exempt under the structural exemption, but other uses of blacktop at a facility probably are not because these uses are process-related. For example, blacktop used for roadways that trucks use to bring materials in and product out of the facility would not be exempt. EPA has developed a guidance document that provides much more information on PACs along with specific examples that will help facilities determine their requirements associated with PACs. A similar document for PBTs includes information on benzo[g,h,i]perylene.

## Slide 53: PACs (cont.)
FUEL MATERIAL | TYPICAL CONCENTRATION | QUANTITY NEEDED TO MEET THRESHOLD (GALLONS)
No. 6 Fuel Oil (Bunker C) | 2,461 ppm | 5,140
No. 2 Fuel Oil | 10.0 ppm | 1,410,000
Crude Oil | depends on type of crude | 
Gasoline | 17 ppm | 1,060,000
Paving Asphalt | 178 ppm | 51,800
Notes: This table is an excerpt from the PAC Guidance Document. The guidance document provides typical concentrations for PACs in a number of sources. The table also shows the quantity that would need to be used to meet the threshold at these concentrations. For example, the first line shows No. 6 fuel oil at a typical concentration of 2,461 parts per million of PACs. At this concentration, if a facility uses more than 5,140 gallons for No. 6 Fuel Oil during the reporting year, they would exceed the 100-pound reporting threshold.
Whereas for No. 2 fuel oil, the typical concentration of PACs is significantly lower at 10 parts per million. So, the table shows that a facility would have to use 1.41 million gallons of No. 2 fuel oil at that concentration before you exceed the 100 pound PACs threshold. Again, these are typical concentrations. If your facility has better information, more specific to the fuels actually used at your facility, that information should be used.
Similar data for benzo[g,h,i]perylene in certain fuels are provided in the PBTs guidance document.

## Slide 54: Mercury and Mercury Compounds
Chemicals of Special Concern activity threshold:
  10 pounds for mercury
  10 pounds for mercury compounds
Combustion of fuels is expected to be a main source of mercury triggering a reporting threshold.
Combustion involves the otherwise use of mercury compounds in fuel and the manufacture of elemental mercury.
Amount of fuel required to exceed a threshold:
  No. 2 Fuel Oil: 1.41 x 109 gallons
  No. 6 Fuel Oil: 1.89 x 109 gallons
  Coal: 11,000 – 120,000 tons
Notes: Now let’s look at mercury and mercury compounds. The Chemicals of Special Concern activity threshold is 10 pounds for mercury and it is 10 pounds for mercury compounds. Note that mercury and mercury compounds are two separately listed TRI chemicals. The combustion of fuels is the main source of mercury triggering reporting to TRI. Combustion typically involves the otherwise use of mercury compounds in fuels and the manufacture of elemental mercury. If you do not know the mercury compound present in a fuel, EPA recommends using mercurous oxide for threshold calculations of otherwise use. In the absence of better information, EPA also recommends that facilities assume that all releases and other waste management quantities of mercury from the combustion of coal are in the form of elemental mercury.
EPA has developed a mercury guidance document that provides the amounts of fuels required to exceed the 10 pound threshold for typical concentrations of mercury in those fuels.
However, if a facility has better, more specific information on the fuel that they are actually using, they should base their calculations on that information. If they do not have other information, they can use the default information in the mercury guidance.
Some information from that guidance document is shown here. For example, in the case of No. 2 fuel oil, you would need to use about 1.41 billion gallons of Number 2 fuel oil to exceed the reporting threshold, IF the concentration of mercury in the fuel oil was 1 part per Billion. For Number 6 fuel oil, it would take about 1.89 billion gallons. So, this helps give a sense of whether reporting might be required. Alternatively, if the uses of these fuels is not even close to these quantities and there are no other sources of mercury at the facility, reporting would probably not be required.

## Slide 55: Mercury and Mercury Compounds
Present in some switches and lights
  Bulbs and switches may qualify as articles for which the articles exemption would apply IF less than 0.5 pound of Section 313 chemicals are released from all like items as a result of processing or use of the items during the year.
Mercury may be present in measurement devices such as thermometers or manometers. The addition of mercury to these devices needs to be considered in threshold and release calculations.
Present in Caustics/Acids (if produced in mercury cell process – not common)
May be present in mined ores
Notes: Here are a few other things to consider regarding mercury. In addition to petroleum products, mercury and mercury compounds might be found in switches and lights. Note, however, that the otherwise use of bulbs and switches would be exempt as an article if you are not a bulb or switch manufacturer AND less than half a pound of the mercury is released during the reporting year from all like items during normal conditions of processing or use.
For example, if a facility purchases and installs mercury switches in a piece of equipment that they manufacture, it would likely meet the article exemption, as long as all like items do not release more than half a pound of 313 chemical as a result of processing or use of the items during the year. If mercury is being added to an instrument, that would NOT be covered by the article exemption.
Facilities should also be aware that mercury might be present in caustics and acids – if it is produced using the mercury cell process, which is not now common. In addition, mined ores may be another source of mercury.

## Slide 56: Polychlorinated Biphenyls
Chemicals of Special Concern activity threshold: 10 pounds
Manufacturing: Polychlorinated biphenyls may be manufactured as a product of incomplete combustion (PIC)
Otherwise use:
  On-site treating or disposing polychlorinated biphenyl-contaminated waste received from off-site
  Combusting polychlorinated biphenyl-contaminated oil
Notes: Polychlorinated biphenyls have a reporting threshold of 10 pounds. Facilities should consider where in their process that they may be using or generating polychlorinated biphenyls. Polychlorinated biphenyls can be manufactured as a byproduct of incomplete combustion. Be aware that recycling of polychlorinated biphenyls is considered processing. Also, using polychlorinated biphenyls by: adding them into your process equipment; treating them on-site; or disposing of polychlorinated biphenyl-contaminated waste received from off-site – or combusting polychlorinated biphenyl-contaminated oil; are all counted towards the otherwise use threshold.

## Slide 57: Polychlorinated Biphenyls
Activities NOT considered manufacturing, processing, or otherwise use:
  On-site disposal or treatment of polychlorinated biphenyls
    Exception: if polychlorinated biphenyls were received as wastes from off-site they are counted towards “otherwise use” threshold.
  Off-site shipment of polychlorinated biphenyls for disposal or treatment
Transformers containing polychlorinated biphenyls may be considered articles and thus exempt from consideration towards reporting and release thresholds.
  Leaks may negate article exemption if 0.5 pounds of polychlorinated biphenyls are released in a reporting year.
Notes: Many facilities ask about how they should report when they ship an old polychlorinated biphenyl-containing transformer off-site for disposal. Polychlorinated biphenyl transformers are considered exempt as articles if no polychlorinated biphenyls are released during their normal use. Note that leaks may negate that article exemption. Also, shipping a product off-site for disposal is not a manufacturing, processing, or otherwise use activity– in other words, it is not a threshold activity. Other activities that are not threshold activities include on-site disposal or treatment of polychlorinated biphenyls not received from off-site or the off-site shipment of polychlorinated biphenyls for disposal or treatment.
So, facilities with old transformers that contain polychlorinated biphenyls, and that are just getting rid of them by sending them off-site for disposal, would not need to report on the polychlorinated biphenyls, assuming they had no other sources of polychlorinated biphenyls at the facility. Just shipping a waste off-site for the purposes of further waste management is not a threshold activity.

## Slide 58: SECTION IV: TOOLS AND ASSITANCE

## Slide 59: www.epa.gov/tri
TRI website for reporting materials and guidance includes:
  Electronic versions, or links to electronic versions, of the statutes, regulations, executive orders, chemical-specific guidance documents, and industry-specific guidance documents
TRI GuideME
  Browse frequently asked questions and answers.
  Browse guidance materials.
  Available at: https://epa.gov/tri/guideme
Notes: TRI reporters should be aware that the TRI homepage contains a great deal of information to assist facilities with their TRI reporting. All of the relevant statutes and regulations are available, as well as guidance for specific chemicals and industry sectors.
In addition, the TRI Program has developed a guidance database hosted in GuideME. It allows facilities to browse questions and answers, the reporting forms and instructions, and other guidance materials. GuideME can be accessed at the website shown here or via the TRI website.

## Slide 60: Reference Sources
EPA Industry Guidance located at:
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-list
AP-42: Compilation of Air Pollutant Emission Factors located at:
  https://www.epa.gov/air-emissions-factors-and-quantification/ap-42-compilation-air-emissions-factors
Technology Transfer Network located at:
  https://www.epa.gov/technical-air-pollution-resources
  AP-42
  WATER9 program
  TANKS program
Perry's Chemical Engineer's Handbook; CRC Handbook of Chemistry and Physics; Lange's Handbook of Chemistry
Notes: Here are some additional sources of information and assistance with the TRI reporting, in general. The first is the TRI program webpage which has a great deal of chemical-specific and industry-specific guidance and all of the reporting forms and instructions.
In addition, EPA’s air pollution emission factors are available in a document called the AP-42. The Website for that is also shown here.
There is also a software program called the WATER9 program. This is a PC-based software that assists with estimates of the fate of organic compounds in various wastewater treatment units.
TANKS is also a PC-based program used to estimate emissions of organic chemicals from several different types of storage tanks. This software uses a database of over 100 different liquid organic chemicals. It includes meteorological data which – from over 250 cities in the US to help with those calculations. Those are both also available from the EPA Website shown here.

## Slide 61: Pollution Prevention (P2) Information
Visit the TRI Pollution Prevention web page
  www.epa.gov/tri/p2
P2 Reporting Guide
  https://ordspub.epa.gov/ords/guideme_ext/f?p=guideme:gd:::::gd:p2_reporting_guide
P2 Resources Search Tool:
  https://www.epa.gov/p2/p2-resources-search
Contact Info:
  Helpline: https://www.epa.gov/p2/forms/contact-us-about-pollution-prevention#helpline
  E-mail: p2hub@epa.gov
  Phone: (202) 566-0799
Notes: Facilities that are interested in using source reduction techniques to reduce their TRI chemical use and wastes can get assistance from the EPA’s office of Pollution Prevention and the 2 Hub Resource Center, at the websites and telephone number shown here.

## Slide 62: TRI Contact Information
TRI Technical Support
  For technical questions related to TRI-MEweb and the Central Data Exchange (CDX), please contact the CDX Hotline at helpdesk@epacdx.net or call toll-free at (888) 890-1995.
TRI Information Center
  Provides a toll free number that facilities may call to obtain guidance on TRI reporting requirements and help on completing the TRI reporting forms
  The number is (800) 424-9346. Callers in the Washington, D.C. metropolitan area call (703) 348-5070. The TDD is (800) 553-7672.
TRI Regional Coordinators
  https://www.epa.gov/toxics-release-inventory-tri-program/tri-regional-coordinators
Notes: If you want more information about TRI-MEweb and the central data exchange, please use the CDX hotline and email address shown here. For information on TRI in general, facilities can call the TRI information center at the numbers shown here. Regional coordinators are useful for issues regarding self-disclosing EPCRA 313 violations, compliance with and enforcement of EPCRA 313 (reporting late, data quality, non-reporting, recordkeeping), registering, completing, and submitting Form Rs, and threshold calculations.

## Slide 63: SECTION V: TRI-MEweb

## Slide 64: TRI-MEweb and Submitting Via CDX
Electronic filing via TRI-MEweb is required
  No paper submissions are accepted (except for trade secrets), including revisions and withdrawals.
  TRI-MEweb supports new reporting, revisions & withdrawals for RY 1991 – current year.
  TRI-MEweb resources including tutorials are available to help users at:
    https://www.epa.gov/toxics-release-inventory-tri-program/electronic-submission-tri-reporting-forms
Use hard-copy form only for trade secret reporting
  Information about trade secret reporting at:
    https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:rfi:::::rfi:apx_a
All TRI reports must be prepared and certified by July 1st following the calendar year’s activities (aka Reporting Year (RY))
  July 1, 2022 deadline for RY 2021 (January 1 - December 31, 2021) activities
v
v
Notes: All TRI reports must be submitted via TRI-MEweb with the exception of reports claiming a trade secret. Electronic reporting is also required for all withdrawals or revisions for Reporting Years 1991 through the present.
TRI-MEweb has features to help reporters with their submissions including pre-populating forms with information from prior year reporting, validation and error checking steps, and e-mail confirmation of transmitted and certified submissions. Additionally, tutorials to help users with TRI-MEweb are available on the TRI website.
Paper submissions should only be used for trade secret reporting. Information about trade secret reporting is available on GuideME.

## Slide 65: Accessing TRI-MEweb
TRI-MEweb is accessed through EPA’s Central Data Exchange (CDX)
  CDX is accessed through: https://cdx.epa.gov.
  TRI-MEweb users must have a CDX account.
  Select TRI-MEweb user role: preparer or certifying official.
Within TRI-MEweb, new users must gain access to their facility before preparing forms.
  Option 1: Enter facility’s access code.
  Option 2: Enter TRIFID and Technical Contact Name.
  Option 3: Begin a new facility profile if the facility has never reported to TRI
For assistance with accessing your facility, contact the CDX helpdesk at helpdesk@epacdx.net or call toll-free at (888) 890-1995
v
Notes: To begin using TRI-MEweb, you must register and log into EPA’s Central Data Exchange, also known as CDX, which also hosts many other reporting applications for EPA programs. Users register either as a preparer or a certifying official. Preparers may perform every portion of the submission process except for the final electronic signature or certification step, which must be performed by a certifying official. The certifying official should be in senior management role for the reporting facility or company. Anyone representing the facility may be a preparer.
To begin reporting for a facility, all uses must gain access to their facility’s profile, using one of three options: the first option is to enter the TRI Facility ID and the facility’s technical contact name and phone number. The second option is to enter the facility’s access key, which is provided to the technical contact. The third option is to begin a new profile for a facility that has never reported to TRI.
For CDX and TRI-MEweb related help, including registering for CDX, password resets, accessing your facility profile in TRI-MEweb, or completing an ESA, please contact the CDX helpdesk.

## Slide 66: Starting a Form in TRI-MEweb
To start a new chemical form from scratch (Part II Sections 1.1-1.2, 2.1)
  Select CAS number or category code and name of chemical or chemical category; or
  Select “Add generic chemicals”, if supplier claims trade secret.
  Indicate if Reporting Form R or From A (non-Chemicals of Special Concern only).
TRI-MEweb preloads previous year’s reporting details using “Import Forms.”
The XML uploader handles forms generated by third-party tools.
v
Notes: To begin a Form R or Form A Certification Statement, first facilities identify the TRI chemicals on which they are reporting. Facilities select chemical name, the “chemical abstract service” number or the TRI chemical category code or select it from the list provided in TRI-MEweb. For those facilities that are claiming a trade secret the chemical name is only entered and the public version of the TRI Form R or A shows only the generic descriptive for the chemical.
In some cases, the facility’s chemical supplier may have claimed a trade secret for a particular TRI chemical and the facility does not know the actual name of the TRI chemical for which they are submitting a report. In this scenario, the facility enters the generic descriptive provided.
TRI-MEweb can generate new forms based on prior year reporting use the “Import Forms” feature.
Some third-party form preparation software generates XML output of forms that may be loaded into TRI-MEweb using the XML uploader.

## Slide 67: Production-Related Waste Managed (Section 8.1-8.7)
Notes: Reporting on production-related waste managed often creates questions from reporters.
In Section 8.1, the quantity of the chemical released is reported. In Sections 8.2 and 8.3, the quantities of the chemical used for energy recovery on-site and off-site are reported. Remember, to be reported as energy recovery, the TRI chemical must have a significant heat value and that heat must be recovered. In Sections 8.4 and 8.5, the quantities of the chemical recycled on-site and off-site are reported. And, in Sections 8.6 and 8.7, the quantities of the chemical treated on-site and off-site are reported. Under TRI, treatment means “destroyed”, so metals, which cannot be destroyed, should not be reported in these sections.
Adding up the quantities in section 8.1 through 8.7 gives the total quantity of waste generated from production activities at the facility. This includes the total quantity released, treated, recycled, or used for energy recovery. Some of these quantities may have already been calculated to complete Form R section 5 for on-site releases and section 6 for off-site transfers. The TRI-MEweb application includes a Section 8 calculator tool that will help with these calculations. However, the quantities reported in sections 5 and 6 of the form can differ from those reported in Sections 8.1 through 8.7. The sections 5 and 6 quantities should include any TRI chemicals released and transferred as part of a remedial clean-up action or catastrophic one time event. These non-production-related quantities are NOT included in Sections 8.1 through 8.7. TRI-MEweb will ask if any of the quantities reported in sections 5 and 6 were associated with remedial actions or catastrophic one time events, and if so, how much. Then, using the information already entered into TRI-MEweb, the Section 8 calculator will populate the quantities for the current year column of Section 8. In the Source Reduction and Waste Management portion of the Form R, as shown here, facilities are not only required to report on the current year’s activities, but also the previous year’s quantities and estimates for the next two years.
If your facility reported on this chemical in the previous year, TRI-MEweb will pre-populate the prior year column. Facilities then only need to estimate quantities for the following two years.

## Slide 68: Certifying Official Information
All non-trade secret forms must be certified by an electronic signature from a senior management official.
New certifying officials must submit an electronic signature agreement (ESA) and a facility certification agreement form before pending submissions can be certified.
Returning certifying officials do not need to submit an ESA as long as they continue to represent the same facility year to year.
TRI-MEweb now includes a built-in Certification module, accessible by users registered as certifying officials.
New certifying officials will answer personalized security questions in addition to their CDX password for digital procedures.
Notes: Forms must be signed electronically or certified by certifying officials, who should be in senior management roles for the reporting facility or company. This step certifies that the information reported on the TRI form is accurate and complete.
Certifying officials must submit an electronic signature agreement, also known as an ESA. The ESA is only submitted once so long the certifying official remains with the facility. Thus, existing certifying officials will not need to resubmit an ESA. New certifying officials should complete their ESA well in advance of the July 1st filing deadline to ensure they will be able to certify forms on time.
Certifying officials now certify new reporting, revisions and withdrawals from a Certification module with-in TRI-MEweb. To complete the certification, certifying officials must also answer personalized security questions in addition to their CDX password.

## Slide 69: Signing and Certifying Forms
New Certifying officials must complete the following two requirements
  Electronic signature agreement (ESA)
    Must be completed only once, not annually, applicable to all facility profiles
    Option 1: Real-time ESA approval – verify user’s identity electronically
    Option 2: Mail in signature form – minimum of 5 business days to process
  TRIFID Certification Agreement Form
    Must be completed after access to TRI-MEweb is granted by ESA approval
    Facility profiles are added to TRI-MEweb using access keys or prior year information
    Certifying officials must have a digitally signed TRIFID Certification Agreement for each facility profile before access to any pending submission (s) for certification is granted
New certifying officials must submit an ESA and digitally sign a TRIFID certification agreement form before pending submissions can be reviewed and certified.
Notes: In order to certify forms, certifying officials must complete two steps. The first step is to submit an electronic signature agreement, also known as an ESA, to be able to certify forms. An ESA is submitted only once so long the certifying official continues to represent the facility. There are two options for submitting an ESA. The first option uses a third-party vendor to verify the certifying official’s identity, and is completed in real time. The second option is to mail in a signed paper form generated by TRI-MEweb, which takes a minimum of five business days to process. Certifying officials should complete their ESA well in advance of the July 1st filing deadline to ensure they will be able to certify forms on time.
Secondly, after the ESA is submitted, certifying officials must complete a TRIFID Certification Agreement for each facility they represent, confirming they are authorized to certify forms for the facility. The TRIFID Certification Agreement is completed within TRI-MEweb in the ‘Certification’ section of TRI-MEweb. Similar to the ESA, the TRIFID Certification Agreement is only submitted once so long the certifying official remains with the facility.

## Slide 70: State and Tribal Submission Requirements
For most facilities, reporting via TRI-MEweb automatically satisfies EPA and state or tribal reporting requirements via data sharing through the TRI Data Exchange (TDX).
For facilities in states or tribal lands not participating in TDX, TRI-MEweb will help prepare separate submissions to satisfy state or tribal reporting requirements.
All States currently participate in TDX:
  https://www.epa.gov/toxics-release-inventory-tri-program/tri-data-exchange
TDX does not support reporting for years prior to 2005.
Notes: For facilities in those states or tribes that participate in the TRI Data Exchange (referred to as TDX), a submittal of their TRI forms to EPA automatically fulfills their state obligations. Also, TRI-ME allows facilities in states or tribes that are not TDX participants to generate hard copies or electronic files on CDs or diskettes for their state reporting.
TDX, however, does not support revisions, withdrawals or new reporting for Reporting Years 1991 through 2004, and any TRI reporting for these years must be separately submitted to the state or tribe.

## Slide 71: TRI-MEweb Tutorials
TRI-MEweb has integrated online tutorials to assist users with common functions in the application.
  Tutorials cover areas such as
    Overview
    Registration
    Accessing Your Facility
    Nominating a Certifying Official
    Section 8 Calculator
    Submitting Data
    Certifying Data
    Getting Help
The tutorials can be viewed at:
  https://www.epa.gov/toxics-release-inventory-tri-program/tri-meweb-mini-tutorials
v
Notes: There are other tools available to assist you with your TRI reporting and using the TRI-MEweb application. EPA has developed on-line tutorials that all of the steps needed to access, submit, and certify TRI forms using TRI-MEweb.
These tutorials are available from the EPA Website shown here. There is audio along with the tutorials, so you need to have speakers or a headset.

## Slide 72: eReceipts
Facilities can obtain a copy of their electronic receipt (formerly known as the electronic Facility Data Profile report (eFDP)) using TRI-MEweb under the Submission History tab.
Review your eReceipt immediately after certifying TRI forms in CDX to verify that EPA processed your data correctly.
The eReceipt provides an opportunity to review data submitted to EPA.
It allows EPA to highlight errors and possible issues with your submission.
If you have problems accessing your eReceipt, contact:
  E-mail: tri.efdp@epacdx.net
Notes: Facilities that have filed in the past should be familiar with the Facility Data Profiles report. The facility data profile reports were designed for the paper processing system that ceased to exist in 2014. TRI-MEWeb has renamed these reports “eReceipts”. This report is generated after TRI’s Data Processing Center receives and processes facilities’ forms. The Data Processing Center conducts data quality checks before the form data is accepted into TRI’s database, they also run various data validation of the facility’s location profile. If no discrepancies are found, the form data is flagged for public release and an eReceipt report to confirm completion of data processing is sent to the TRI-MEweb application. The eReceipt has two purposes: First, it’s also called an “echo back” because it echoes back to you the information of the form data that was processed by EPA and is on stand-by for public release. That gives facilities a chance to confirm that the data was captured correctly. Second, it identifies potential errors. Potential errors include: 1) non-technical errors, such as transposing a CAS number; or 2) technical errors, such as an invalid NAICS code; or 3) a significant error, which would be missing information like a chemical identifier, or the certifying signature. Third, it also identifies data quality alerts. Data quality alerts are indications of any significant reporting changes compared to the prior year or any reporting abnormalities that the facility needs to be aware of. Facilities may respond to significant errors pointed out in the eReceipts by submitting a revision.
Facilities may contact the e-mail address shown here if they have any problems accessing their eReceipts reports.

## Slide 73: TRI-MEweb Demo
If you are viewing an Online Training Module, please visit www.epa.gov/tri to view the TRI-MEweb tutorials.
Notes: This concludes the Advanced Concepts Module of the TRI Online Training.
On-line tutorials for using the TRI-MEweb application can be accessed from the TRI homepage at www.epa.gov/tri.
Also, the Basic Concepts module of this Online Training course is available from the TRI homepage.

## Slide 74: END OF MODULE

## Slide 75: Quiz Answers
75
Notes: 75

## Slide 76: Quiz #1: Question 1
A facility processes 200,000 pounds of a mixture containing 10% zinc chromate (ZnCrO4) and 15% chromium dioxide (CrO2) by weight
For which of the following chemical categories was the processing threshold exceeded?
Answer: A is correct
A. Chromium compounds only B. Zinc compounds only
C. Neither D. Both
Chromium compounds only
Zinc compounds only
C. Neither
D. Both
Total chromium compounds processed: (10% + 15%) × (200,000 lb) = 50,000 lb
Total zinc compounds processed: (10%) × (200,000 lb) = 20,000 lb
The processing threshold (25,000 lb) was exceeded for chromium compounds, but not zinc compounds. Both are chemicals with 25,000/10,000-pound reporting thresholds

## Slide 77: Quiz #1: Question 2
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby water body.
The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. 1 mole of HNO3 generates 1 mole of NaNO3.
Does the facility exceed the manufacturing threshold for nitrate compounds?
Answer: Yes
The quantity of nitrate compounds manufactured = (quantity of HNO3 neutralized) × (MW of NaNO3 / MW of HNO3)
NaNO3 manufactured = (20,000 lb) × (85/63) = 26,984 lb (rounded to 27,000)
Nitrate compounds are subject to 25,000/10,000-pound reporting thresholds.
The manufacturing threshold (25,000 lb) is exceeded, so the facility must submit a TRI form for nitrate compounds

## Slide 78: Quiz #1: Question 3
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby water body. The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. 1 mole of HNO3 generates 1 mole of NaNO3
In this example, should the facility report release of 27,000 lb of nitrate compounds as to a stream or water body? (Section 5.3 on Form R)? Yes or no
Answer: No
Releases of nitrate compounds are reported on nitrate ion (NO3-) basis. Based on molecular weights (NaNO3 = 85, NO3- = 62), 62 lb of nitrate ion are generated for every 85 lb of nitrate compounds.
To calculate the quantity of nitrate ion released to the water body in the example described above: (lb of NaNO3) x (MW of NO3- / MW of NaNO3) = (26,984 lb) x (62/85) = 19,682 lb (rounded to 20,000 lb)
On the Form R for nitrate compounds, the facility would report 20,000 lb of the nitrate ion releases to the stream or water body.

## Slide 79: Quiz #2: Question 1
A facility combusts 13,600,000 lb of coal to fire its boilers. The coal contains elemental lead (Pb) at 7.0 ppm by weight. In combusting the coal, the facility otherwise uses lead and coincidentally manufactures lead compounds. The facility has no other information about the chemical makeup of the lead compounds manufactured and assumes it is the lowest-weight oxide – PbO. Based on molecular weights (Pb = 207, PbO = 223), the facility knows that 223 lb of PbO is formed for every 207 lb Pb used.
Which of the following thresholds have been exceeded for lead or lead compounds?
Answer: B is correct
Pb in coal: (13,600,000 lb) * (7 x 10-6) = 95.2 lb
PbO formed: (95.2 lb) * (223/207) = 103 lb
Since lead is expected to be present in coal in compound, you could consider that 103 lb of lead compounds was combusted and, therefore, otherwise used
Total lead combusted (95.2 lb) does not exceed the threshold for otherwise using lead not in stainless steel, brass, or bronze (100 lb)
Total lead oxide manufactured (103 lb) exceeds the threshold for manufacturing and otherwise use of lead compounds (100 lb)
A. Otherwise Use only
C. Neither
B. Manufacturing only
D. Both

## Slide 80: Quiz #2: Question 2
The facility in the previous question combusted 13,600,000 pounds of coal in the reporting year and has exceeded the reporting threshold for lead compounds. The facility has no monitoring data on their point source lead emissions from combusting the coal. They determined that their best available information for calculating their point source air emissions is the published emission factor for lead from controlled coal combustion from EPA’s AP-42* which is 4.2E-04 lb Pb/ton of coal combusted.
What are the facility’s point source emissions of lead from coal combustion?
Answer: A is correct
A. 2.86 lb
C. 95.2 lb
B. Range Code ‘A’
D. Either 2.86 lb or Range Code ‘A’
Point Source Emissions (lb) = EF × W where: EF = emission factor for controlled coal combustion (lb Pb/ton coal), and W = weight of coal combusted (ton)
Weight of coal combusted: (13,600,000 lb coal)/(2,000 lb/ton) = 6,800 tons coal
Point Source Emissions = 4.2E-4 (lb Pb/ton coal) × 6,800 tons coal = 2.86 lb Pb
  Assuming coal combustion was the only source of point source air emissions for this facility, the facility would report 2.86 lb in Section 5.2 of their Form R for lead compounds.
  Range codes cannot be used for Chemicals of Special Concern.
  While threshold determination is based on the weight of the lead compounds, release and waste management calculations are based on the weight of the parent metal (lead) in the metal compound (lead oxide)