## Slide 1
2021
Notes: Welcome to the Emergency Planning and Community Right-to-Know Act, Section 313, Toxics Release Inventory online training for the 2021 reporting year. This is the Basic Concepts Module of a two part training course that is made up of this module and an Advanced Concepts module. The Basic Concepts module will walk you through the process of determining whether or not your facility is required to report to the Toxics Release Inventory, or TRI, and if so, how you actually prepare and submit information to TRI. The Advanced Concepts module assumes a basic understanding of the TRI requirements and focuses on key concepts that will help to ensure accurate TRI reporting.

## Slide 2: TRI Training Module Agendas
Basic Concepts Module
  Covered Sectors
  Listed Chemicals and Activity Thresholds
  Reporting Exemptions
  Threshold Determination
  Overview of Form R
  Form R Calculation Examples
  Alternate Threshold Rule (Form A)
  TRI-MEweb Introduction
Advanced Concepts Module
  Recent TRI Program Changes
  Advanced Reporting Guidance
  Detailed Guidance for Chemicals of Special Concern
  Tools and Assistance
  TRI-MEweb
v
v
Notes: In this module we’ll first provide a brief overview of the TRI program and help you determine whether or not your facility is covered by TRI. We’ll look at the industry sectors covered by TRI and the TRI chemical list and threshold quantities. Next, we’ll cover a number of exemptions to TRI reporting that might apply to your facility. We go over how to determine whether or not your facility exceeded any of the activity thresholds, which would trigger TRI reporting.
And, finally we will look at the Form R and Form A, which are the two reporting options under TRI.
In the Advanced Concepts module, we cover recent changes and updates to the TRI program, guidance on chemicals with special reporting requirements, the EPA audit policy, where you can get additional information and assistance with TRI requirements and submitting TRI Forms through TRI-MEweb

## Slide 3: INTRODUCTION

## Slide 4: What is EPCRA Section 313 and TRI?
Section 313 of EPCRA requires facilities to file a TRI report annually for each Section 313 chemical exceeding an activity threshold (manufacturing, processing, or otherwise use)
  Section 313 chemical list contains more than 800 chemicals and chemical categories
Facilities exceeding an activity threshold must report if they are
  In a “covered sector” (defined by NAICS codes) and have 10 or more employees, or
  Have reporting requirements extended by discretionary authority granted by EPCRA Section 313(b)(2).
Submit TRI reports to U.S. EPA and either
  Designated state officials, or
  Designated tribal office
TRI reports must be submitted by July 1st following the calendar year’s activities (aka Reporting Year (RY))
  July 1, 2022 deadline for RY 2021 (January 1 - December 31, 2021) activities
Notes: Now let’s look at the basic requirements of Toxics Release Inventory reporting. What is TRI? The Toxics Release Inventory was established by Section 313 of the Emergency Planning and Community Right to Know Act, or EPCRA 313. Facilities that are covered under EPCRA 313 must complete a TRI chemical form for each TRI chemical for which they’ve exceeded an activity threshold. There are more than 800 chemicals and chemical categories on the TRI chemical list. A facility must submit a TRI report if they exceed an activity threshold for a TRI chemical, either are in a “covered sector” AND they have the equivalent of ten or more employees, OR are required to report by having reporting requirements extended by the discretionary authority of the EPA Administrator under EPCRA Section 313(b)(2). TRI reports must be sent to the United States EPA and your designated state or tribal authority.

## Slide 5: TRI Reporting Requirements
Notes: To be required to report to TRI, your facility must meet ALL of the criteria shown here. A stepwise process can be used to determine if and what you would need to report to TRI. The first step is determining whether or not your facility is covered under EPCRA Section 313 and would, therefore, need to consider its toxic chemicals for TRI reporting. Whether or not your facility is covered is based on the types of activities carried out at the facility and the number of employees working for your facility. NAICS is the North American Industry Classification System, which assigns numeric codes to characterize the activity taking place at the facility. We will talk more about the NAICS codes requirement shortly.
Alternatively, if your facility has been included in a determination by the EPA Administrator under their discretionary authority to add extend reporting requirements to specific facilities, you need not consider your NAICS code or employees for the purposes of determining whether a TRI report is needed.
Then, if you’ve met one of the two criteria above (either are both in a covered sector AND have at least ten full-time employee-equivalents, OR were included in discretionary authority determination), then you proceed to the final step.
The next step is to determine for which TRI chemicals you must submit a TRI report. Covered facilities need to look at the TRI chemicals that are on the list and that may be present at the facility. Next, facilities need to look at how the chemicals are used. Are they manufactured? Processed? Or otherwise used? These are the TRI threshold activities. We will be describing each of these in more detail.
Next, facilities must calculate the quantity of the TRI chemical that is manufactured, processed, or otherwise used, and compare those quantities to the TRI activity thresholds. Only when activity thresholds are exceeded would the facility be required to complete and submit a TRI report, either a Form R or a Form A.

## Slide 6: TRI Process: 2 Step Process
Notes: The process of completing your TRI forms is a two-step process. In the first step, you determine if your facility is required to report to TRI, and if so, you determine which TRI chemicals you handle in your facility, and then which of these you would need to report on.
Step 2, shown on the right, is the release and other waste management reporting. This is the information that you would put on a TRI form. What information do facilities report to TRI? For the Form R, which is the more common means of TRI reporting, facilities report on how the TRI chemical is managed as waste, including onsite releases, treatment, energy recovery, recycling of the TRI chemical and offsite transfers, and pollution prevention activities that are conducted at the facility for that chemical.
We will cover both of these steps in detail in this Basic Concepts Module.

## Slide 7: SECTION 1: COVERED SECTORS

## Slide 8: Industrial Sectors Covered
INDUSTRIAL SECTOR | NOTES
Manufacturing | Facilities engaged in the mechanical or chemical transformation of materials or substances into new products
Metal Mining | Not including metal mining services, and uranium, radium, and vanadium ores
Coal Mining | Not including coal mining services
Electrical Utilities | Limited to facilities that combust coal and/or oil for the purpose of generating electricity for distribution in commerce
Treatment, Storage, and Disposal Facilities | Limited to facilities regulated under the Resource Conservation and Recover Act, Subtitle C, 42 U.SC. Section 6921 et seq
Solvent Recovery Services | Limited to facilities primarily engaged in solvent recovery services on a contract or fee basis
Chemical Distributors | Facilities engaged in the wholesale distribution of chemicals and allied products
Petroleum Bulk Terminals | Facilities engaged in the wholesale distribution of crude petroleum and petroleum products from bulk liquid storage facilities
Notes: This table shows the private sector industries that are covered by TRI. The covered sectors include: manufacturing; portions of metal mining; portions of coal mining; certain electric utilities; treatment, storage, and disposal facilities; solvent recovery facilities; chemical distributors; and petroleum bulk terminals.
Natural gas processing are covered by TRI reporting requirements effective for reporting year 2022, with first forms due July 1, 2023.

## Slide 9: Covered NAICS Codes
2017 North American Industry Classification System (NAICS) codes are used for TRI reporting
To determine whether your facility’s primary NAICS code is covered by TRI regulations, see:
https://www.epa.gov/toxics-release-inventory-tri-program/tri-covered-industry-sectors
TRI-Covered* Industries NAICS
  212 Mining
  221 Utilities
  31 - 33 Manufacturing
  All Other Miscellaneous Manufacturing (includes some sectors under NAICS 1119, 1133, 2111, 4883, 5417, 8114)
  424 Merchant Wholesalers, Non-durable Goods
  425 Wholesale Electronic Markets and Agents Brokers
  511, 512, 519 Publishing
  562 Hazardous Waste
  Federal Facilities
* Note: For many of these NAICS codes, there are reporting exceptions
Notes: The TRI program uses the 2017 North American Industry Classification System, or “NAICS” codes, to define which facilities are covered under TRI.
The TRI-covered NAICS codes are listed in the Code of Federal Regulations as well as in the TRI Reporting Forms and Instructions document. The list is rather lengthy. And it does include a number of exceptions and limitations.
At the website shown here, facilities can determine whether their primary NAICS code is one that is covered by TRI regulations.

## Slide 10: Federal Facilities
Federal facilities (covered by Executive Order 13423 and its implementing instructions)
  Required to report regardless of their NAICS code
    Includes military bases, federal prisons, national parks, etc
  Other reporting requirements apply
    10 or more full-time employees
    Exceed manufacture, process, or otherwise use thresholds of a listed chemical
  The federal agency or department that owns or operates the facilities is responsible for reporting
  Government owned contractor operated (GOCO) facilities
    Same reporting requirements as non-federal facilities
    Counted as federal facilities in TRI data analysis
  See Federal Facility Reporting Information guidance document
    https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd:::::gd:fed_fac
Notes: Federal facilities may also be covered by TRI. There are no restrictions based on NAICS codes for federal facilities. So, any federal facilities, such as prisons, national parks, or hospitals, could be covered under TRI.
Federal facilities also need to have 10 or more full time employees to be covered by TRI. And, to be required to submit a TRI report, they would need to exceed one or more of the activity thresholds for the TRI chemicals present at the facility. The federal agency or department that owns or operates the facility is responsible for determining whether or not it is required to report. If the facility is operated by a private contractor, this executive order does not alter or remove their legal obligation to report.

## Slide 11: Definition of “Facility”
Facility - all buildings, equipment, structures, and other stationary items which are located on a single site or on contiguous or adjacent sites and which are owned or operated by the same person (or by any person which controls, is controlled by, or under common control with, such person).
EPCRA § 329 (4)
“
TRI reporting requirements are determined by activities at “facilities.”
  Primary NAICS code determination at facility level
  Employee threshold determination at facility level
  Chemical threshold determinations made at facility level
Notes: As previously mentioned, the reporting unit under TRI is the facility. Primary NAICS codes determinations and employee threshold determinations are made at the facility level. Chemical threshold determinations are also made at the facility level. Therefore, the definition of a facility under TRI is very important. EPA defines a facility as “all buildings, equipment, structures, and other stationary items which are located on a single site or contiguous or adjacent sites and which are owned or operated by the same person (or by any person which controls, is controlled by, or under common control with such person).”
A key point here is that establishments or operations owned or operated by the same company or federal agency that are contiguous or adjacent are considered a single facility under TRI. In some instances, a single site or adjacent properties may have multiple and distinct establishments, each considered to be a unique and separate economic unit. Together, these establishments comprise a single facility under TRI if they are owned or operated by the company or agency.

## Slide 12: Multi-Establishment Facility
Multi-establishment facilities may include distinct and separate economic units that have different NAICS codes.
The facility primary NAICS is determined by the establishment with the majority of value added (i.e., greater than 50%).
When a majority is not present, the primary NAICS is determined by the plurality of greatest percentage of value added.
  Value added = sum (value of products exiting the facility)
  - sum (value of products entering the facility)
Notes: If any of these establishments contributes the majority of the economic value, or ‘value added’, of the facility, the NAICS code for that establishment would become the primary NAICS code for the entire facility. Essentially, ‘value added’ can be thought of as the value of the services the establishment provides, or the value of the products leaving the establishment less the value of the materials entering the establishment.

## Slide 13: Example of a Multi-Establishment Facility
Three separate establishments with distinct and separate economic units located on contiguous/ adjacent property owned by same person(s) is one facility under EPCRA (40 CFR §§ 372.22(b) and 372.3)
  Establishment - unique and separate economic unit of a facility (See 40 CFR § 372.3)
Notes: We mentioned that establishments are unique economic units within a facility. In the facility shown here, there are three unique establishments. There is a food processing establishment, a farm, and a warehouse. These establishments are all owned by the same company and are located at adjacent or contiguous sites and, therefore, are together considered a single facility under TRI. However, only the NAICS code of the processing establishment is a covered NAICS code under TRI.
Whether or not this facility would be covered by TRI depends in part on the primary NAICS code of the entire facility. The primary NAICS code for the facility is determined by the economic value added provided by each of the establishments.

## Slide 14: Example of a Multi-Establishment Facility
In this example, the plurality is with the foods processing establishment
Because the processing NAICS code is one that is covered under TRI, the entire facility would need to consider its employee and chemical use thresholds
Notes: In an example case, the processing facility, NAICS code 311421, comprises 40% of the ‘value added’ for the entire facility. The farm and the warehouse each comprise 30%. Therefore, the primary NAICS code for the entire facility is 311421. For more on calculating value added for establishments, see the TRI Reporting Forms and Instructions.
Because the processing NAICS code is one that is covered under TRI, the entire facility would need to consider its employee thresholds and chemical use.

## Slide 15: Employee Threshold
Ten or more full-time employee equivalents (i.e., 20,000 hours) (40 CFR §§372.3 and 372.22(a))
  All persons employed by a facility regardless of function
    Includes operational staff, administrative staff, contractors, dedicated sales staff, company drivers, off-site direct corporate support
  Add all hours from part-time and full-time employees
    Includes holidays, vacation, and sick-leave
  Does NOT include intermittent services from non-employees
    Excludes contract drivers or contractors performing intermittent service functions such as janitorial services
Total hours worked for each employee can be determined using time management systems.
Notes: For private sector facilities that have determined that they meet the primary NAICS code requirements and federal facilities, the next step is to determine whether or not they meet the employee threshold requirement. As mentioned, facilities with 10 or more full-time employees are covered by TRI.
10 or more full-time employees is defined as 20,000 hours worked at or for the facility. This includes operational staff, administrative staff, contractors, sales staff, drivers, and off-site corporate support. The only thing it doesn’t include is contracted drivers and contractors providing intermittent services such as trash removal and janitorial services.
Facilities need to add up all of the hours worked at their facility, both part-time and full-time, and apply that towards this 20,000 hour threshold.

## Slide 16: Discretionary Authority
Under the Emergency Planning and Community Right-to-Know Act (EPCRA) Section 313(b)(2), the EPA Administrator has the discretionary authority to extend TRI reporting requirements to specific facilities.
The Administrator may determine the application of this authority is warranted on the basis of a chemical’s toxicity, the facility’s proximity to other facilities that release the chemical or to population centers, any history of chemical releases at the facility, or other factors the Administrator deems appropriate.
Notes: Under the Emergency Planning and Community Right-to-Know Act (EPCRA) Section 313(b)(2), the EPA Administrator has the discretionary authority to extend TRI reporting requirements to specific facilities based on a chemical’s toxicity, the facility’s proximity to other facilities that release the chemical or to population centers, any history of chemical releases at the facility, or other factors the Administrator deems appropriate.

## Slide 17: Quiz #1: Question 1
Would the facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
Select Yes or No
A manufacturing facility, owned by ABC Corporation, with 100 full-time employees

## Slide 18: Quiz #1: Question 2
A maintenance and warehouse facility, owned by ABC Corporation, with 5 full-time employees, a few blocks away from the manufacturing facility described in Question 1
Would the facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
Select Yes or No

## Slide 19: Quiz #1: Question 3
A maintenance and warehouse facility, owned by ABC Corporation, with 5 full-time employees, next door to the manufacturing facility described in Question 1
Would the facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
Select Yes or No

## Slide 20: SECTION II: LISTED CHEMICALS AND ACTIVITY THRESHOLDS

## Slide 21: Section 313 Chemicals and Chemical Categories
Current list contains over 800 individual chemicals and chemical categories (See Table II of the EPA’s TRI Reporting Forms and Instructions document.) There are 6 parts to the chemical list:
  Chemicals with qualifiers
  Individual non-PFAS listed alphabetically by name and listed by CASRN
  Chemical categories
  Individual PFAS listed alphabetically by name and listed by CASRN
The list can change. Check every year. Changes are listed in the front of the TRI Reporting Forms and Instructions on the TRI website and in TRI-MEweb
Section 313 chemical list and more information available at:
https://www.epa.gov/toxics-release-inventory-tri-program/tri-listed-chemicals
Notes: So what are the TRI chemicals? The current TRI chemical list contains over 800 individual chemicals and chemical categories. The list can be found in EPA’s Reporting Forms and Instructions in Table II, which is available on the TRI website and through the TRI-MEweb reporting application.
The individual TRI chemicals are listed separately for PFAS and non-PFAS. Both groups are listed alphabetically by name and they are also listed again by their CASRN or Chemical Abstract Service Registry Number. There is also a list of chemical categories. Coming up we’ll talk about the differences between individual chemicals and chemical categories in more detail. Be aware that the TRI chemical list changes almost every year. Make sure that you’re always using the most current TRI chemical list.

## Slide 22: Section 313 Metal Compound Chemical Categories
Metal compound chemical categories
Lead compounds
Manganese compounds
Mercury compounds
Nickel compounds
Selenium compounds
Silver compounds
Thallium compounds
Vanadium compounds
Zinc compounds
Note: Elemental metals and metal compounds are separately listed chemicals under Section 313.
Antimony compounds
Arsenic compounds
Barium compounds *
Beryllium compounds
Cadmium compounds
Chromium compounds **
Cobalt compounds
Copper compounds ***
Metal compound categories include any unique chemical substance that contains the element as part of that chemical's infrastructure
  Does not include barium sulfate (CASRN 7727-43-7)
  Except chromite ore and unreacted ore component of processing residue (see RFI for further information)
  Does not include copper phthalocyanine compounds that are substituted with only hydrogen, and/or chlorine and/or bromine
*
**
***
Notes: Facilities need to take care in identifying chemicals used or generated at their facility that may fall within a TRI chemical category group. Chemical categories are groups of individual chemicals which must be considered together towards activity thresholds and reporting under TRI.
Many chemical categories are metal compound chemical categories some of which are shown here. In many cases, the elemental forms of the metal are also reportable as a separately listed TRI chemical.
Let’s look at lead compounds as an example. Any unique chemical substance that contains lead as part of its chemical infrastructure would be considered part of the lead compounds chemical category.
Note that some of these chemical categories also contain qualifiers. For example, in the case of barium compounds, the category does not include barium sulfate; however, all other barium compounds would need to be considered toward this chemical category.

## Slide 23: Other Section 313 Chemical Categories (examples)
Chlorophenols | 
Cyanide compounds | XCN where X=H or any other group where a formal dissociation may occur. For example, KCN or Ca(CN)2
Diisocyanates | 20 individual compounds cited in Category
Dioxin and dioxin-like compounds | 17 individual compounds cited in Category
Ethylenebisdithiocarbamic acide, salts and esters (EBDCs) | Includes a substance that may contain EBDC or EBDC salt or ester as part of its infrastructure
Certain glycol ethers | Complex definition
Nicotine and salts | Includes a substance that may contain it or salt as part of its infrastructure
Nitrate compounds | Water dissociable, reportable only when in aqueous solution
Polybrominated biphenyls (PBBs) | 
Notes: Chemicals can also be grouped into other, non-metal chemical categories. In some cases, the category is defined as a general class of chemicals, for example, in the case of chlorophenols. And in other cases, there is a list of individual chemicals that makes up the chemical category. In the case of dioxin and dioxin-like compounds, there are 17 individual compounds that make up the chemical category. These are just some of the non-metal chemical categories on the TRI chemical list.

## Slide 24: Section 313 Chemicals With Qualifiers
Qualifiers: Listed chemicals with parenthetic qualifiers subject to TRI reporting only if manufactured, processed, or otherwise used in specified form (40 CFR §372.25(g))
Below are some examples (see Table II of EPA’s TRI Reporting Forms and Instructions document for full list of chemical qualifiers):
CHEMICAL | CASRN | QUALIFIER
Aluminum | 7429-90-5 | Fume or dust
Aluminum oxide | 1344-28-1 | Fibrous forms
Asbestos | 1332-21-4 | Friable
Isopropyl alcohol | 67-63-0 | Only manufacturers using the strong acid processes
Hydrochloric acid | 7647-01-0 | Acid aerosols
Phosphorus | 12185-10-3 | Yellow or white
Saccharin | 81-07-2 | Manufacture only
Sulfuric acid | 7664-98-8 | Acid aerosols
Vanadium | 7440-62-2 | Except when contained in an alloy
Zinc | 7440-66-6 | Fume or dust
Notes: Many of the listed TRI chemicals have parenthetic qualifiers. These chemicals are only subject to TRI reporting if they are manufactured, processed, or otherwise used in the specific form described in the qualifier.
The tables shown here are just some of the qualifiers for TRI chemicals. For example, aluminum and zinc, have the qualifier ‘fume or dust’. This means that aluminum would only be considered under TRI in the fume or dust form. Isopropyl alcohol is another example. It would only need to be considered under TRI if the facility is manufacturing isopropyl alcohol and using a process called the ‘strong acid process’.
Another example is sulfuric acid, which is only considered under TRI in an acid aerosol form. Facilities that have aqueous sulfuric acid which are not aerosolizing the acid in any way would not need to consider their sulfuric acid towards the threshold or reporting. These are just some of the qualifiers on the TRI chemical list. Facilities should always be sure to be aware of the chemical qualifiers associated with the chemicals that may be present at their facility.

## Slide 25: Chemical List Changes
Section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA) adds certain per- and polyfluoroalkyl substances (PFAS) to the TRI list of reportable chemicals.
  Additional PFAS may be added to the TRI list for future reporting years due to the automatic addition of PFAS to the TRI list mandated by NDAA Section 7321(c) that occur under certain circumstances:
    EPA finalizing a toxicity value for a PFAS;
    issuing certain Significant New Use Rules (SNURs) under TSCA for a PFAS, or adding a PFAS to certain existing SNURs;
    adding a PFAS as an active chemical on the TSCA Inventory.
  PFAS are individually listed and subject to manufacturing, processing, and otherwise use reporting thresholds of 100 pounds.
  https://www.epa.gov/toxics-release-inventory-tri-program/addition-certain-pfas-tri-national-defense-authorization-act
Notes: Section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA) adds per- and polyfluoroalkyl substances (PFAS) to the TRI list of reportable chemicals. Additional PFAS may be added to the TRI list for future reporting years due to the automatic addition of PFAS to the TRI list mandated by NDAA Section 7321(c) that occur under certain circumstances.

## Slide 26: Chemical List Changes
For RY 2021, four PFAS have been added to the TRI list of reportable chemicals per the requirements of the NDAA. These are:
  Silver(I) perfluorooctanoate (CASRN 335-93-3)
  Perfluorooctyl iodide (CASRN 507-63-1)
  Potassium perfluorooctanoate (CASRN 2395-00-8)
  2-Propenoic acid, 2-methyl-, 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,11,11,12,12,12-heneicosafluorododecyl ester, polymer with 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,10-heptadecafluorodecyl 2-methyl-2-propenoate, methyl 2-methyl-2-propenoate, 3,3,4,4,5,5,6,6,7,7,8,8,9,9,10,10,11,11,12,12,13,13,14,14,14-pentacosafluorotetradecyl 2-methyl-2-propenoate and 3,3,4,4,5,5,6,6,7,7,8,8,8-tridecafluorooctyl 2-methyl-2-propenoate (CASRN 65104-45-2)
Notes: Per the requirements of section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA), four per- and polyfluoroalkyl substances (PFAS) have been added to the TRI list of reportable chemicals. These additions are effective for the 2021 TRI reporting year.

## Slide 27: Toxic Chemical Activity Thresholds
A TRI report must be prepared and submitted for any chemical that has exceeded an activity threshold
Threshold calculations are based on cumulative quantities of each Section 313 chemical manufactured, processed, or otherwise used over the reporting year for the whole facility
Each activity threshold is treated separately:
  Quantify separately amounts of toxic chemicals that are manufactured, processed, or otherwise used at the facility
  Compare amounts in each activity to the toxic chemical’s applicable threshold
Lower thresholds apply to the 21 chemicals/chemical categories designated as Chemicals of Special Concern
Lower thresholds apply to the 176 PFAS
Notes: As previously mentioned, TRI reporting is only triggered when a facility exceeds one or more of the three activity thresholds: manufacturing, processing, and otherwise use. Facilities must quantify the amount of each TRI chemical and chemical category involved in each of these three activities. Then, compare the amounts to the thresholds.
In some cases the same discrete amount of a TRI chemical can go through more than one threshold activity. In such cases, the chemical must be counted towards each threshold activity.
Remember that threshold calculations are based on cumulative quantities of each TRI chemical over the reporting year. If a threshold is exceeded for any of the threshold activities, then a TRI report must be prepared and submitted for that chemical.

## Slide 28: Chemicals with 25,000/10,000-pound Reporting Thresholds
A TRI-covered facility must submit a TRI Report for a Section 313 Chemical with 25,000/10,000-pound reporting threshold if:
NON-CSC, NON-PFAS THRESHOLDS
Manufactured (including imported)
more than 25,000 pounds of the chemical in the reporting year
Processed
more than 25,000 pounds of the chemical in the reporting year
Otherwise Used
more than 10,000 pounds of the chemical in the reporting year
OR
OR
Most of the 800+ chemicals and chemical categories on the Section 313 list are chemicals with 25,000/10,000-pound reporting thresholds
Notes: We’ve talked about the thresholds activities. Now, what are the actual threshold quantities that would trigger TRI reporting? For chemicals that are neither perfluroalkyl nor polyfluoroalkyl substances and are not considered to be Chemicals of Special Concern, are “Chemicals with 25,000/10,000-pound Reporting Thresholds.” The thresholds for manufacturing are 25,000 pounds; for processing, 25,000 pounds; and for otherwise use, 10,000 pounds. These are the thresholds for the majority of the TRI chemicals.

## Slide 29: PFAS Activity Thresholds
A TRI-covered facility must file a TRI Report for PFAS Section 313 chemical if:
PFAS THRESHOLDS
Manufactured (including imported)
more than 100 pounds of the chemical in the reporting year
Processed
more than 100 pounds of the chemical in the reporting year
Otherwise Used
more than 100 pounds of the chemical in the reporting year
OR
OR
176 Section 313 chemicals are PFAS
Notes: For chemicals that are per- or poly-fluoroalkyl substances (PFAS), the thresholds for manufacturing, processing, and otherwise use are 100 pounds.

## Slide 30: TRI-Listed Chemicals of Special Concern
Within the list of chemicals and chemical categories, there is a subset designated as being of special concern and commonly referred to as Chemicals of Special Concern (40 CFR § 372.28)
Chemicals of Special Concern have lower activity thresholds and different reporting requirements than chemicals not listed as Chemicals of Special Concern
  Special rules often apply to Chemicals of Special Concern
21 chemicals and chemical compound categories are classified as Chemicals of Special Concern and have lower activity thresholds
Notes: Chemicals of Special Concern are a subset of the chemicals on the TRI chemical list. Chemicals of Special Concern have lower activity thresholds than other TRI chemicals and they also have some special rules when reporting them to TRI. Currently there are 21 chemicals and chemical categories that are designated as Chemicals of Special Concern under TRI.

## Slide 31: Chemicals of Special Concern and Activity Thresholds
100 lb/yr (manufactured, processed, or otherwise used):
  Aldrin
  Hexabromocyclododecane
  Lead*
  Lead compounds
  Pendimethalin
  Polycyclic aromatic compounds
  Tetrabromobisphenol A
  Trifluralin
  Methoxychlor
10 lb/yr (manufactured, processed, or otherwise used):
  Chlordane
  Heptachlor
  Mercury
  Toxaphene
  Isodrin
  Polychlorinated biphenyls
  Benzo[g,h,i]perylene
  Hexachlorobenzene
  Mercury compounds
  Octachlorostyrene
  Pentachlorobenzene
0.1 g/yr (manufactured, processed, or otherwise used):
  Dioxin and dioxin-like compounds
Chemicals of Special Concerns are subject to separate and lower activity thresholds (See 40 CFR § 372.28)
*Excluding lead in stainless steel, brass, or bronze alloys
Notes: The actual threshold quantities that trigger reporting vary depending on the chemical. For eight of the chemicals, the threshold is 100 pounds per year. For those chemicals that are considered to be highly persistent and bioaccumulative, the threshold is 10 pounds per year. And for dioxin and dioxin-like compounds, the threshold is 0.1 grams per year, which reflects the highly toxic nature of this chemical category. For Chemicals of Special Concern, the threshold quantities are the same for manufacturing, processing, and otherwise use.

## Slide 32: Manufacturing Activities
Manufacturing (EPCRA §313(b)(1)(C)(i) and 40 CFR § 372.3): Generating a Section 313 chemical
Intentionally producing chemicals for:
  Sale
  Distribution
  On-site use or processing (e.g., intermediates)
Coincidentally producing chemicals as impurities* or by-products**:
  At any point at the facility, including waste treatment and fuel combustion
Importing:
  “Cause” to be imported
*Impurity = TRI chemical that still remains with the final facility product as it is distributed into commerce
**By-product = TRI chemical that is separated out from the process mixture before it becomes the final product
Notes: Now, let’s look at each of the threshold activities in more detail. The first is manufacturing. Manufacturing includes intentionally producing the TRI chemical because that is what your facility does – either manufactures the TRI chemical for sale or distribution – or manufactures it to be used on-site in another process.
Chemicals can also be coincidentally manufactured, in which case the chemical is not intentionally manufactured but it is created as an impurity or byproduct in the process. Coincidentally manufacturing a TRI chemical can happen at any point in the facility, including in waste treatment and when combusting fuels.
Importing of a TRI chemical, or causing a TRI chemical to be imported into the United States, is also considered to be a manufacturing activity under TRI.

## Slide 33: Processing Activities
Processing (EPCRA §313(b)(1)(C)(ii) and 40 CFR § 372.3) - preparation of a Section 313 chemical, after its manufacture, for distribution in commerce:
  Use as a reactant to manufacture another substance or product
  Add as a formulation component
  Incorporate as an article component
  Repackage for distribution
  Incidentally include as an impurity
  Quantities sent off-site for recycling
Notes: The next threshold activity is processing. Processing of a TRI chemical involves distributing a TRI chemical into commerce. This can be done either as a reactant in the manufacturing of another substance which is distributed into commerce, or it could be that the TRI chemical is being added as a formulation or article component to a product which is then distributed into commerce. Repackaging of a TRI chemical with subsequent distribution into commerce also is a processing activity under TRI.
Note that, under TRI, processing also includes sending a TRI chemical off-site for recycling.
Finally, processing may also include the unintentional processing of a TRI chemical if it appears as an impurity in a raw material that your facility uses and which leaves the facility in the product.

## Slide 34: Repackaging as a Processing Activity
Repackaging a Section 313 chemical for distribution in commerce is considered processing
Repackaging includes:
  From container to tanker truck and vice versa
  Between similar size containers
  Via pipeline to/from a tank
Repackaging does not include:
  Sampling without repackaging
  Re-labeling
Repackaging without distribution into commerce is not processing
Transfer to a storage tank for mere storage is not processing
Notes: Let’s look at repackaging in more detail. Any repackaging of a TRI chemical for distribution in commerce is considered processing. Repackaging could be from any type of container to any other type of container. The containers could be similar sizes, or they could be very different such as pipelines into tanks or vice-versa.
As long as the TRI chemical is going from one container to another and then is being distributed into commerce, the chemical would be considered processed under TRI. Repackaging does not include taking samples from containers for the purposes of quality assurance and it does not include simple re-labeling of a container. As long as the TRI chemical stays within the container, placing a label on the container itself would not be considered repackaging.
Any repackaging without distribution into commerce would not be considered processing. For example, TRI chemicals contained in a 55 gallon drum that are placed into smaller containers and distributed around the facility to be used at the facility and which are not being distributed into commerce would not be considered towards the processing thresholds.

## Slide 35: Otherwise Use Activities
Otherwise Use (40 CFR §372.3) - includes most activities that are NOT manufacturing or processing
Examples
  Chemical processing aid (e.g., solvents, catalysts, buffers, non-incorporative reagents)
  Manufacturing aid (e.g., lubricants, refrigerants, coolants, hydraulic fluids, metalworking fluids)
  Ancillary activities
    Fuels, cleaners, degreasers
    Chemicals used to remediate or treat wastes
    Fabrication and/or use of tools in your process
    Installation of piping and process-related equipment, e.g., reactors, constructing storage tanks, asphalt roadways
Notes: ‘Otherwise use’ includes most activities that are not considered manufacturing or processing. Chemicals that are otherwise used include chemical processing aids like solvents, manufacturing aids like lubricants, refrigerants, or catalysts. Otherwise use often includes ancillary activities, chemicals that are used, for example, to remediate wastes or chemicals that are used to clean process equipment.
Chemicals that are contained within tools or other equipment at the facility would be considered otherwise used.

## Slide 36: Otherwise Use Activities (continued)
Managing wastes received from off-site also counts as “Otherwise Use”
  Disposal, treatment for destruction on-site, or stabilization that does not result in further distribution in commerce are considered otherwise use if:
    Section 313 chemical was received from off-site for the purposes of further waste management, or
    Section 313 chemical was manufactured as a result of waste management activities on materials received from off-site for the purpose of further waste management
  On-site energy recovery is an otherwise use activity.
  Waste management activities, including on-site recycling, treatment for destruction, waste stabilization and release/disposal of Section 313 chemicals in wastes generated on-site are not threshold activities.
Notes: Otherwise use also includes any disposal, stabilization, or treatment for destruction of a TRI chemical if the chemicals are received from off-site for the express purposes of further waste management.
Also, any on-site combustion of TRI chemicals for energy recovery is also considered an otherwise use activity. This includes energy recovery of wastes generated on-site and wastes received from off-site. In addition, TRI chemicals that are manufactured as a result of waste management activities on any material that is received from off-site for the purpose of waste management would be considered towards your otherwise use threshold. Under TRI, waste management activities include recycling, combustion for energy recovery, treatment for destruction, waste stabilization and release to the environment, including disposal. These activities in themselves, with the exceptions of off-site recycling and on-site energy recovery, are not threshold activities as long as the waste was not received from off-site for the purpose of waste management.

## Slide 37: Calculating Activity Thresholds
The threshold quantity is the total amount manufactured, processed, or otherwise used, NOT the amount released.
Calculate the total amount of Section 313 chemical used for a specific threshold activity.
Each activity threshold is calculated separately and they are not additive.
Calculations for reporting waste management may be different from threshold quantities.
Example of Calculating Activity Thresholds
Over the course of a reporting year, a facility manufactures 24,000 pounds of chemical with 25,000/10,000-pound reporting thresholds, subsequently processes 24,000 pounds, and also happens to otherwise use 9,000 pounds of the same chemical.
That facility has not exceeded the chemicals with 25,000-pound manufacturing and processing thresholds nor the 10,000-pound otherwise use thresholds and would NOT be required to submit a TRI report for that chemical.
Notes: When calculating activity thresholds, facilities must remember that the threshold quantity is the total amount of the chemical that is manufactured, processed, or otherwise used over the reporting year. It is not the amount of TRI chemical that was released or managed as waste. Remember to apply the total amount of the chemical to each activity threshold including all threshold activities at the facility. Note that it is not critical to calculate the threshold quantity exactly; however, it is important to know whether or not you have exceeded the threshold using the best available information.

## Slide 38: Threshold Determination for Compound Categories
Count together all compounds within the same chemical category for each activity, even if different compounds within a category are used in separate operations.
Consider the entire weight of all the different chemical compounds in the same chemical category when determining thresholds.
Note: calculations for release and other waste management estimates of metal compounds are based on the parent metal weight only, and nitrate compounds are based on weight of nitrate ion only.
Notes: When determining thresholds for chemical categories, be sure to count all the compounds that fall within the category even if they’re different compounds used in different operations around your facility. Apply the entire weight of the compounds in the category when determining your thresholds quantities.
Note that while the weight of the entire compound must be applied to the threshold for the chemical category, releases and other waste management estimates for Form R reporting have different requirements for metal and nitrate compounds.

## Slide 39: Activities That Are Not TRI Threshold Activities
Activities that, alone, do NOT constitute a threshold activity
  Storage
  Remediation of on-site contamination (assuming no listed chemicals are manufactured during remediation)
  Re-labeling without repackaging
  Direct reuse on-site
  On-site recycling (not including wastes received from off-site)
  Transfers sent off-site for further waste management (not including recycling)
  Repackaging (and blending, if any) of waste fuels for burning for energy recovery. (However, all fuels, including waste fuels (with blending, if any), are considered otherwise used when combusted for energy recovery.)
Note: While these activities are not included in the threshold determination, releases and wastes from these activities are not exempt from reporting if threshold is exceeded through other activities (unless specifically eligible for one of the reporting exemptions).
Notes: There are some activities that are not considered to be threshold activities under TRI. In other words, the activities are not considered manufacturing, processing, or otherwise use. For example, storage. In itself, storage of a TRI chemical would not need to be considered towards an activity threshold. Remediation of on-site contamination would not be considered a threshold activity as long as the waste was on-site and not brought in from off-site for the purposes of waste treatment or waste management.
As mentioned, re-labeling of a container without repackaging is not considered a threshold activity. Directly reusing a TRI chemical on-site and any on-site recycling of a TRI chemical are not considered threshold activities. Transferring of a TRI chemical off-site for further waste management, not including offsite recycling, is not considered a threshold activity.
None of the TRI chemicals associated with these activities would need to be considered towards an activity threshold. However, if a TRI chemical threshold was exceeded in some other manner at your facility, a TRI form would be required for that chemical. Any release and other waste management reporting for that chemical would need to include any releases or other waste management associated with these activities.

## Slide 40: Quiz #2: Question 1
A plant uses benzene as a raw material to manufacture liquid industrial adhesive. The plant adds 27,000 lb of benzene to its liquid adhesive-making operation during the reporting year, but 3,000 lb are volatilized during the operation. How much of the benzene should be applied toward the processing activity threshold?
Select your choice
A. 27,000 lb
B. 24,000 lb
C. 3,000 lb

## Slide 41: Quiz #2: Question 2
If a facility processes 20,000 lb of 4,4’-methylenedi(phenyl isocyanate) in one operation and 10,000 lb of isophorone diisocyanate in another operation during the reporting year, what should it apply towards its processing threshold for the diisocyanates category?
Select your choice
A. 10,000 lb
B. 20,000 lb
C. 30,000 lb

## Slide 42: Quiz #2: Question 3
A facility processes 18,000 lb copper sulfate, 10,000 lb of cuprous oxide, and otherwise uses 12,000 lb of aqueous sulfuric acid solution in a closed system. For which TRI chemicals or chemical categories would the facility need to submit a TRI form?
Select your choice
A. copper compounds and sulfuric acid
B. only copper compounds
C. only sulfuric acid

## Slide 43: Section III: Reporting Exemptions

## Slide 44: Reporting Exemptions
If an exemption applies, then the amount of Section 313 chemical subject to the exemption does NOT have to be included in:
  Threshold determinations
  Release and other waste management reporting
Recognize that exemptions only apply to certain limited circumstances.
Misusing exemptions may lead to enforcement action.
To learn more about TRI exemptions, please visit:
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-list#exemption
Notes: Next we will be covering a number of exemptions to TRI reporting. The purpose of reporting exemptions is to reduce the burden of reporting associated with small or ancillary operations. If an exemption applies, then all the associated amount of the TRI chemical does not need to be included in threshold determinations or release and other waste management reporting. It’s important to note that exemptions only apply in certain limited circumstances.

## Slide 45: Reporting Exemptions
Types of exemptions (40 CFR § 372.38)
  De minimis
  Article
  Laboratory activities
  NAICS code specific
    Coal mining extraction activities
    Metal mining overburden
  “Otherwise use” exemptions
    Motor vehicle maintenance
    Routine janitorial or facility grounds maintenance
    Structural components
    Personal use
    Intake water and air
Notes: The TRI exemptions include the de minimis exemption, the articles exemption, and the laboratory activities exemption. A number of exemptions apply only to facilities in the metal and coal mining sectors. There are also a series of exemptions for the otherwise use of TRI chemicals in motor vehicle maintenance, routine janitorial or facility grounds maintenance, structural components, personal use, intake water and air.

## Slide 46: De Minimis Exemption
The quantity of a non-Chemical of Special Concern Section 313 chemical in a mixture or other trade name product is eligible for the de minimis exemption (40 CFR §372.38(a)) if the chemical is:
  An OSHA-defined carcinogen present at a concentration of less than 0.1% OR
  Any other non-CSC TRI chemical present at a concentration of less than 1%
The TRI de minimis level appears next to each chemical on the chemical list in Table II of the TRI Reporting Forms and Instructions (1.0, 0.1 or * for Chemicals of Special Concern where de minimis is not allowed (See 40 CFR §372.38(a)))
Notes: Let’s look at a de minimis exemption first. Under the de minimis exemption, the quantity of a non-CSC TRI chemical in a mixture or other trade name product is exempt from TRI if – in the case of an OSHA-defined carcinogen, the TRI chemical is present at a concentration less than 0.1%. Or, in the case of a non-OSHA-defined carcinogen, at a concentration of less than 1%. The de minimis concentrations are provided for each chemical on the TRI chemical list, which is Table II of the reporting forms and instructions. It is also available from the TRI assistance library and the TRI-ME reporting software.

## Slide 47: De Minimis Exemption: How it Works
De minimis exemption generally applies to non-Chemicals of Special Concern:
  In mixtures or trade name products received from off-site, including imported
  Coincidentally manufactured as impurities that remain in products distributed in commerce
De minimis exemption does not apply to:
  Manufactured chemicals (in most cases): this includes by-products produced from manufacturing, processing, otherwise use, or any waste management
  Wastes received from off-site
  Chemicals of Special Concern (except for supplier notification)
Notes: So how does the de minimis exemption work? De minimis exemption generally applies to non-CSC chemicals that are in mixtures or trade name products received from off-site that are processed or otherwise used. This includes TRI chemicals in mixtures that are imported when the concentration of the TRI chemical in the mixture is below the applicable de minimis level. It can also apply if a facility coincidentally manufactures a non-CSC chemical as an impurity, and this impurity remains in a product distributed in commerce, then the quantity of the chemical that is distributed in commerce may be eligible for the de minimis exemption. In other words, the de minimis exemption does not apply to manufacturing of chemicals in most cases, including coincidentally manufacturing of TRI chemicals as by-products, which are removed from the process. The de minimis exemption also does not apply to wastes because waste is not considered to be a mixture. And it does not apply to Chemicals of Special Concern. Chemicals of Special Concern are a subset of the TRI chemicals comprised of 21 chemicals and chemical categories. Chemicals of Special Concern are discussed in detail in the Advanced Concepts Module.

## Slide 48: Chemicals of Special Concern and the De Minimis Exemption
The de minimis exemption cannot be applied to Chemicals of Special Concern.
All other EPCRA section 313 exemptions can apply to Chemicals of Special Concern.
Facilities that receive a mixture and know that Chemicals of Special Concern are present must consider each Chemical of Special Concern in threshold and release calculations – regardless of whether or not supplier notification was provided
Notes: The de minimis exemption cannot be used for Chemicals of Special Concern. As for the supplier notification requirements, suppliers are not required to notify users of the presence of a TRI chemical that is below the de minimis concentration. However, the users of the mixtures containing TRI chemicals are still required to consider all quantities of TRI chemicals known to be present.
The de minimis exemption is the only exemption that does not apply to Chemicals of Special Concern. All of the other exemptions apply to all Section 313 chemicals.

## Slide 49: De Minimis Exemption: How It Works… (cont.)
Processing a non-Chemical of Special Concern in a mixture to below the de minimis concentration does NOT exempt the chemical from threshold determinations and release calculations
De minimis exemption does NOT apply
Threshold determination required
Release calculations required
Toluene > 1%
Acme Industries
Toluene <1%
De minimis exemption does NOT apply
Threshold determination required
Release calculations still required
c
Raw Material Primer Mixture Products (90% Toluene)
c
Paint (<1% Toluene)
TOLUENE CONCENTRATION
Notes: Let’s look at a couple of examples for which the de minimis exemption can and cannot be used. First, let’s say we have a raw material coming into a facility and the raw material is 90% toluene. So in this case it comes into the facility above the de minimis concentration for toluene of 1%. However, during the process, the concentration of the toluene in the production process decreases to a level less than 1% or below the de minimis concentration. Would we be able to apply de minimis exemption?
De minimis would not apply in this situation, even after the point where the concentration of the toluene goes below the 1% de minimis. Once the TRI chemical is above the de minimis concentration, the de minimis exemption cannot be taken for that chemical mixture. So in this case the facility would need to consider the toluene towards its activity thresholds, and towards any release of waste management reporting required.

## Slide 50: De Minimis Exemption: How It Works… (cont.)
Processing a non-Chemical of Special Concern in a mixture to above the de minimis concentration triggers threshold determinations and, if thresholds are met, release calculation requirements
De minimis exemption DOES apply
Threshold determination not required
Release calculations not required
Toluene < 1%
Acme Industries
Concentrated
Toluene > 1%
De minimis exemption does NOT apply
Threshold determination required
Release calculations still required
c
Solvent Raw Material containing trace amounts of toluene containing
c
Paint Stripper
TOLUENE CONCENTRATION
Notes: Now let’s look at an example for which the de minimis exemption can be used. If a raw material coming into a facility contains trace amounts of toluene, less than the 1% de minimis limit, the de minimis exemption does apply. However, during the process, the concentration of the toluene in the production process increases to a level greater than 1% or below the de minimis concentration. Would we be able to apply de minimis exemption at this point?
De minimis would not apply in this situation, after the point where the concentration of the toluene goes above the 1% de minimis. Once the TRI chemical is above the de minimis concentration, the de minimis exemption cannot be taken for that chemical mixture. So in this case the facility would need to consider the toluene towards its activity thresholds, and towards any release of waste management reporting required.

## Slide 51: Article Exemption Applicability
To qualify for the article exemption, the article must meet 3 criteria (40 CFR § 372.3):
  Is formed into a specific shape or design during manufacture; and
  Has end-use functions dependent in whole or in part on its shape or design during end-use; and
  Does NOT release a Section 313 chemical under normal processing or use conditions at a facility
Notes: Next, let’s look at the articles exemption. The article exemption applies to TRI chemicals contained in articles. There are three criteria that must be met to be considered an article under TRI. First, an article is formed into a specific shape or design during its manufacture. Second, an article has an end-use function that is dependent in whole or in part on that shape or design. And, third, an article does not release a TRI chemical under normal processing or use conditions at the facility.

## Slide 52: Article Exemption: How it Works
Releases of a Section 313 chemical from an article may negate the exemption. To maintain the article status, total releases from all like items must be:
  In a form having a specific shape or design; or
  Recycled, directly reused; or
  0.5 pound or less released per year (may be rounded down to zero)
If more than 0.5 pound per year of a Section 313 chemical is released from all like items in a form not having a specific shape or design and is not recycled or directly reused, none of the items meet the articles exemption.
End use must be dependent upon the item’s initial shape or design. (For example, sheet metal must maintain its initial thickness, and wire and pipe must maintain their initial diameter.)
See the articles exemption summary on GuideME for more information:
  https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd:::::gd:articles
Notes: Now let’s look at how the article exemption works in more detail. If a TRI chemical is released from an article during its normal use, it very well may negate the article’s exemption. In order to maintain the article’s status, the total TRI chemicals released from all like articles or like items must be either: 1) in a form having a specific shape or design, or 2) recycled directly or directly reused, or 3) must be less than or equal to half a pound. In a form having a specific shape or design generally means that the releases from the article must still look like and be recognized as pieces of the article. If more than half a pound of TRI chemical is released from all the like items used at the facility in the course of the year, and the releases are not in a form with a specific shape or design, and if they are not recycled or directly reused, none of the items meet the article exemption. Also, because the item’s end use function must depend upon its design or shape, articles cannot be altered significantly. For example sheet metal must maintain its initial thickness, and wire and pipe must maintain its initial diameter to be considered exempt as articles.

## Slide 53: Article Exemption: Examples
Wire is cut to specified lengths. Wastes include off-spec cuts and dust
  Generation of off-spec cuts that are recognizable as articles will not, by themselves, negate the article status
  Dust and off-spec cuts not recognizable as articles, with greater than 0.5 pound of ANY Section 313 chemical released annually, and not recycled or directly reused, negate the article status.
Fluorescent light bulbs containing mercury are installed and used. Following use, the bulbs are crushed for recycling at the facility and mercury is released.
  Crushing bulbs for recycling after use for lighting at the facility is not considered release under normal conditions of processing or use at this facility; the article exemption may apply.
v
v
Notes: Now let’s look at an example where wire is cut into specified lengths. Wire itself would be considered an article, but in cutting the wire to the specified lengths, there is some waste of off-spec cuts and some dust. The generation of the off-spec cuts that are still recognizable as pieces of wire will not by themselves negate the article’s status. Quantities of the dust and off-spec cuts that are not recognizable as pieces of wire and that are greater than half a pound for any TRI chemical and not recycled or directly reused would negate the article status.
Let’s look at the example of fluorescent light bulbs which contain mercury, a TRI chemical. When the bulbs are no longer of use at a facility, they are crushed in an enclosed container for recycling at the facility. In this case the fluorescent bulbs would still be exempt. The normal use of the fluorescent bulbs at this facility as lighting does not release mercury.
While the occasional crushing of bulbs at this facility may release mercury, the crushing is not considered normal use of the bulb at this facility. Therefore, these releases would not disqualify the bulbs from the exemption at this facility if all other criteria are met. Note that the mercury in the bulbs may be exempt from TRI reporting at this facility, but other regulatory requirements associated with the proper management of waste fluorescent bulbs should be followed.

## Slide 54: Article Exemption
Article Exemption is often inappropriately used!
  In many instances when metals are machined, cut, or ground, in any manner, the article exemption may not be applicable.
The articles exemption does not apply to the actual manufacturing of articles.
Notes: Facilities need to be careful that they do not inappropriately use the articles exemption. Because it only takes ½ pound of TRI chemical released or disposed of over the course of a year to negate the articles status, often when metals containing TRI chemicals are machined, cut, or ground, in any manner, the article exemption would not apply. Also, the article exemption does not apply to the actual manufacturing of articles.

## Slide 55: Laboratory Activity Exemptions: How it Works
Section 313 chemicals used in these laboratory activities under the direct supervision of a technically qualified individual ARE exempt from threshold and release and other waste management reporting (40 CFR § 372.38(d)):
  Sampling and analysis
  Research and development
  Quality assurance
  Quality control
Section 313 chemicals used in these laboratory activities are NOT exempt:
  Specialty chemical production
  Pilot-scale plant operations
  Activities not conducted in lab
  Support services
    Photo processing
    Equipment maintenance/cleaning
Notes: The next exemption is the laboratory activities exemption. TRI chemicals that are used in laboratories, under the direct supervision of a technically qualified individual, are exempt if they are used for sampling and analysis, research and development, quality assurance, or quality control. TRI chemicals used in laboratory activities are not exempt in the case of specialty chemical production, pilot-scale plant operation, activities that are not conducted in an actual lab, and support services such as photo processing or equipment maintenance and cleaning.

## Slide 56: Motor Vehicle Maintenance Exemption
Section 313 chemicals used to maintain vehicles operated by the facility are eligible for the exemption from threshold determinations (40 CFR § 372.38(c)(4))
  “Otherwise use” exemption
Motor vehicles include cars, trucks, tanks, and forklifts
Motor vehicle maintenance includes:
  Fueling and adding other fluids (e.g., ethylene glycol)
  Body repairs
  Parts washing
  Lead acid or other types of batteries (e.g., forklifts)
Note: This exemption does NOT apply to “manufacture” of Section 313 chemicals from combustion of fuels
Notes: Next, let’s look at the motor vehicles maintenance exemption. This is one of the ‘otherwise use’ exemptions. The TRI chemicals that are otherwise used to maintain vehicles that are operated by the facility would be eligible for this exemption. By motor vehicles, we are including cars, trucks, military vehicles, and forklifts. Motor vehicle maintenance includes body repairs, painting, parts washing and plating, fueling, and adding other fluids to the vehicle. Note that this is an ‘otherwise use’ exemption, so it does not apply to the manufacture of TRI chemicals from the combustion of fuel in vehicles. Also, if vehicles are a product of the facility and TRI chemicals are being added to that product, either as a fuel or in some other way, that would be considered processing and not ‘otherwise use’. So those chemicals would not be exempt.

## Slide 57: Routine Janitorial or Facility Grounds Maintenance Exemption
Section 313 chemicals contained in products used for non-process related routine janitorial or facility grounds maintenance ARE eligible for exemption (40 CFR § 372.38(c)(2)):
  Phenol in bathroom disinfectants
  Pesticides or fertilizers used on lawns
  “Otherwise use” exemption
Section 313 chemicals used in the following activities are NOT exempt
  Facility equipment maintenance
  Cleaning or maintenance activities that are directly associated with or integral to the production process at the facility
  Note: Chemicals otherwise used in janitorial or grounds maintenance activities may not be exempt if part of your facility’s “process” is to provide these services (e.g., federal hospitals, prisons, parks). Also, chemicals manufactured during routine janitorial or facility ground maintenance are not exempt
Notes: The routine janitorial or facility grounds maintenance exemption covers the otherwise use of TRI chemicals in products and materials used for cleaning facilities and maintaining their grounds. Examples include: pesticides, fertilizers, chemicals that are in cleaners that are used in non-process areas. TRI chemicals that are used for facility equipment maintenance or cleaning or maintenance activities that are directly associated with the production process would not be eligible for the routine janitorial or facility grounds maintenance exemption.
Note that this exemption only applies to chemicals that are “otherwise used”. If part of your facility’s “process” is to provide these types of services, for example, grounds maintenance activities at a national park, then the TRI chemicals may not be considered “otherwise used” and may not be exempt.

## Slide 58: Structural Component Exemption
Section 313 chemicals used as structural components are eligible for exemption (See 40 CFR § 372.38(c)(1)). Building components that are process-related are not “structural components” as contemplated by the exemption
Non-process-related building components that are “structural components” and therefore eligible for the exemption include:
  Potable water pipes and other non-process-related pipes and structures
Processed-related building components that are NOT “structural components” and therefore NOT eligible for the exemption include:
  Refractory brick, boiler tubes, process-related pipes, anodes used in electroplating, grinding wheels, & metal working tools
  Structural components that are integral to a non-industrial facility’s “process” (e.g., federal prisons, hospitals, parks)
Notes: TRI chemicals otherwise used in certain structural components of the facility may also be exempt. However, building components that are process-related are not “structural components” and are not eligible for the exemption. So non-process-related structural items might include water pipes for potable water and any other non-process-related pipes and structures. Typical items that would not be eligible for the exemption – refractory brick, boiler tubes, process-related pipes, anodes used in electroplating, grinding wheels, metal working tools, and things of that nature. Federal facilities may have structural components that are integral to their “process” and the chemicals in these components would NOT qualify for the exemption. For example, the chemicals used as a wood preservative for a Navy pier used to dock ships, would not be exempt.

## Slide 59: Other Section 313 “Otherwise Use” Exemptions
Section 313 chemicals contained in non-process-related items for employee personal use (40 CFR § 372.38(c)(3)):
  Non-Federal Facilities:
    HCFC-22 in air conditioners used solely for employee comfort (exemption does NOT cover process cooling using chemical-based cooling systems)
    Chlorine used to treat on-site potable water
    Phenol used in a facility medical dispensary
  Federal Facilities:
    Does not include TRI chemicals used for providing services to non-employees (e.g., patients in federal hospitals, prisoners, park visitors)
Section 313 chemicals found in intake water and air.
Notes: The remaining otherwise use exemptions apply to personal use of TRI chemicals and TRI chemicals found in intake water and air. With the personal use exemption, chemicals that are used for employee personal use such as refrigerants or air conditioners that are solely for employee comfort, disinfectants used in potable water such as chlorine or phenols used in the medical dispensary are exempt.
Also TRI chemicals that are found in intake water and air, used at a facility, as long as the facility is not responsible for them being in the intake water and air are also exempt under TRI.

## Slide 60: Sector Specific Exemptions
Coal mining extraction activities are exempt from threshold determinations and release reporting (40 CFR § 372.38(g)) (applies to NAICS Codes 212111-212113):
  Coal extraction: physical removal or exposure of ore, coal, minerals, waste rock, or overburden prior to beneficiation, and encompasses all extraction-related activities prior to beneficiation (40 CFR § 372.3)
Chemicals in metal mining overburden that are processed or otherwise used are specifically exempt from TRI reporting (40 CFR § 372.38(h)) (applies to NAICS Codes 212221, 212222, 212230, 212299):
  Overburden: unconsolidated material that overlies a deposit of useful materials or ores (40 CFR § 372.3)
v
v
Notes: There are also a number of industry-specific, or NAICS-code specific exemptions. The first one applies to certain coal mining activities that would be exempt from threshold determinations and release reporting. For coal mining, the exempt activities include the physical removal or exposure of the ore or coal prior to the beneficiation of the material. Similarly, certain metal mining activities are also exempt from TRI reporting.

## Slide 61: Section IV: Threshold Determination

## Slide 62: Chemical Information Management
All non-exempt manufacture/processes/otherwise use of Section 313 chemicals at the facility must be counted towards chemical activity thresholds.
Tracking toxic chemicals entering facility
  Purchasing/Inventory
  Contractors
  Capital purchases (e.g., chillers, process equipment)
  Direct purchases (credit card or other emergency purchases)
  Direct and indirect materials
  Manufacturing byproducts/intermediates generated
Need cooperation and support from all functional groups purchasing or using Section 313 chemicals
Be comprehensive to ensure accurate threshold determination!
Notes: To ensure accurate TRI threshold determination, be sure to consider all activities and sources of the TRI chemicals at the facility. It might help to track chemicals as they enter the facility. Consider chemicals that are purchased or that are in inventory. Consider chemicals used by contractors, because you’re responsible for your contractors’ use of TRI chemicals as well. Don’t forget capital purchases and one time purchases. And don’t forget materials that may be manufactured as byproducts or intermediates. These should all be considered towards activity thresholds.
It helps to get the cooperation and support from all the different groups at the facility who may be purchasing or using TRI chemicals. Be comprehensive. For example, consider TRI chemicals that may be in steel or aluminum alloys that may be above the de minimis concentration. Manganese is one example.

## Slide 63: Threshold Determinations
Identify Chemicals and Concentrations
  SDS
  Product or Specifications
  Available Supplier/ Vendor Product QA/QC data
  Industry Standards (API, ASTM, etc.)
  Waste Profiles
  Process Knowledge
  Other References (AP-42, WebFIRE, Merck Index)
  Supplier Notification
Collect Data to Calculate Thresholds
  Inventory or Purchase Records
  Throughput/Production Data
  Integrated Supplier Records
  EPCRA or Other Env. Reports
  Air Permits / MACT or Similar Standards/ Emission Inventories
  Water Permits / DMR’s / Discharge Reports
  Annual/Biennial Waste Reports
  User Records
  Other Vendor Records (can call vendor)
v
v
Notes: There are a number of different sources of information available to facilities – to both identify the chemicals and concentrations, collect the data, and calculate the thresholds. We have talked about some of these already – such as MSDS’s and product specifications. Facilities should also consider any waste profiles or testing . Also, consider using any other data about the wastes leaving and raw materials entering your facility. Inventory or purchase records are often a good source of information. Production data can help you in quantifying the amounts of TRI chemicals to apply towards thresholds.
Regulatory reports, either air permits or water, chemical analyses associated with permits applications, and waste reports – are all potential sources of information on TRI chemicals.

## Slide 64: TRI Chemicals Contained in Mixtures
For the threshold quantity, only include the amount of the TRI chemical in the mixture, not the weight of the entire mixture.
The de minimis exemption (40 CFR § 372.38(a)) applies to non-Chemicals of Special Concern contained in mixtures at less than 1.0% or 0.1% (for carcinogens).
  The de minimis exemption is related to the concentration of the chemical in a mixture, NOT the quantity of the mixture used.
A metal alloy can be thought of as solid solution. To determine threshold quantity, multiply the concentration of the TRI chemical in the alloy by the total weight of alloy processed or otherwise used.
Notes: When determining threshold quantities, be sure to only include the portion of the mixture that is the TRI chemical, and not the weight of the entire mixture. The de minimis exemption applies only to non-CSC chemicals that are in mixtures and in concentration that is less than 1% or 0.1% for carcinogens. The de minimis exemption allows for low concentrations of TRI chemicals in mixtures to be ignored in most cases.
It is not related to the quantity of the mixture used. Note that metal alloys can be thought of as a solid mixture or solution. Like any other mixture, you would multiply the concentration of the TRI chemical that is in the alloy by the total weight of the alloy to determine the threshold quantity.

## Slide 65: Determining Concentrations in Mixtures or Other Trade Name Products
Determine whether thresholds were exceeded for listed chemicals in a mixture (40 CFR § 372.30(b)(3)):
  Exact concentration: use concentration provided
    SDS = 25% Use 25%
  Upper bound: use upper limit
    SDS < 25% Use 25%
  Range: use the midpoint of the range
    SDS: 30 – 50% Use 40%
  Lower bound: subtract out other known constituents, create a range, and use the midpoint of range
    SDS > 75% toxic chemical Use 87.5% (top of range = 100%)
    SDS > 75% toxic chemical
    15% water Use 80% (range = 75% - 85%)
Notes: Concentration of a TRI chemical can often be obtained from the Safety Data Sheet or other product information. In some cases the exact concentration of the TRI chemical is provided. For example, if a Safety Data Sheet provides a concentration of 25% for a TRI chemical, facilities would use 25% for their activity threshold determinations and any subsequent reporting.
In other cases, the SDS may provide only an upper bound for the TRI chemical. For example, if the SDS says there is at most 25% of the TRI chemical, in those cases facilities would actually use 25%, the upper limit, in their calculations. Oftentimes an SDS will provide a range for a TRI chemical. For example, if the SDS says 30 to 50%, facilities would use the midpoint of the range – in this case, 40%.
In some cases, a lower bound is provided for a TRI chemical in a mixture. If a lower-bound is provided, facilities would subtract out any other known constituents, creating an upper bound, thereby creating their own range, and use the midpoint of the range. For example, if an SDS says the product contains at least 75% of the TRI chemical. In that case, we know that there is anywhere between 75% and 100% of the TRI chemical. The midpoint of that range would be 87.5%.
In some cases, the SDS may say there is at least 75% of the toxic chemical and there is also, for example, 15% water. In this case, we know that the upper bound is 85%. The midpoint of the range of 75 to 85% would be 80%.

## Slide 66: Determining Concentrations in Wastes
If concentration is exact, upper bound, range, or lower bound, use the guidance for mixtures and other trade name products discussed earlier.
If concentration is below detection limit, use engineering judgment:
  If the Section 313 chemical IS expected to be present, assume 1/2 of full detection limit
  If the Section 313 chemical is NOT expected to be present, assume 0
v
v
%
bd
Notes: Facilities don’t always know whether or not the TRI chemical is present in a mixture at a concentration that is above its de minimis. For example, in cases where the SDS gives a range or an upper bound, use the guidance we discussed earlier for how to determine what concentration to use and compare that to the de minimis. In the situation where you know the TRI chemical is present but it’s below the detection limit, use your engineering judgment. If the chemical is expected to be there, assume that it’s at a level of half the full detection limit. If you don’t expect the TRI chemical to be present, you can assume that its concentration is zero.

## Slide 67: Supplier Notification
Supplier notification - requires suppliers of mixtures or trade name products to covered facilities (See 40 CFR § 372.45(a)) to:
  Identify Section 313 chemical(s) by name and CAS number
  Identify Section 313 chemical(s) as being subject to Section 313 requirements
  Provide concentration (or range) of Section 313 chemicals in mixtures and other trade name products (not wastes)
  Provide notification at least annually in writing or attached to the SDS
  Update notification when changes occur
The Regulatory Information section of the SDS should identify any chemicals that are subject to TRI reporting.
Suppliers of mixtures containing Chemicals of Special Concern below de minimis concentrations do not need to supply notification.
Supplier Notification Requirements Guidance Document:
https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-title:::::title:supplier_notification
Notes: Under TRI, facilities that supply TRI chemicals to others must provide information about those TRI chemicals. For example, they must identify the TRI chemical by name and by CAS number and must identify that this chemical is subject to Section 313 or TRI reporting requirements. They must provide a concentration or a range of concentrations for the TRI chemical that is in a mixture or a trade name product.
They must provide this notification at least annually or attach it to the Safety Data Sheet for the chemical. If any changes occur related to the TRI chemical or its concentration, they must provide that information as well. Usually, SDSs contain a Regulatory Information section which should identify the TRI chemicals present and their concentrations.

## Slide 68: Watch for Double Counting
For threshold determinations, Section 313 chemicals recycled from spent or contaminated materials or Section 313 chemicals directly reused:
  Count original amount used only once.
  For materials in use from previous years, count only the quantity added during current reporting year.
Section 313 chemicals that are stockpiled or in inventory but not manufactured, processed, or otherwise used during reporting year are NOT counted for threshold determinations.
v
Chemicals sent off-site for recycling and returned to the facility are considered new materials and counted for threshold determinations
Notes: Be sure to watch out for double counting when calculating threshold quantities. Count the original amount of the chemical used in a threshold activity over the course of the reporting year only once. For materials that are in use from previous years, only count the quantity that was added during the current reporting year. Remember that chemicals that are stored or stockpiled that are not manufactured, processed, or otherwise used during the reporting year are not counted for threshold determinations.
Also note that any chemicals that are sent off-site for recycling and returned to the facility are considered new materials and would be counted again towards activity thresholds.

## Slide 69: Count the Original Amount Used Only Once
Example
If a chemical is blended into a product mixture, and then this mixture is packaged for sale into 55 gallon drums, these are both processing activities, the chemical is “processed” twice. Only count this quantity once towards the processing threshold.
  During Reporting Year, 20,000 lb of toluene were blended with other chemicals to create a paint product.
  The paint product (containing the 20,000 lb of toluene) was then packaged into 55 gallons drums for sale.
  The processing threshold quantity for this facility for Reporting Year = 20,000 lb.
Notes: Be sure to watch out for double counting within the same activity threshold. For example, if a facility blends a TRI chemical in a product mixture and then the mixture is repackaged for sale into another container, those are both considered processing activities – the blending and the repackaging. While a chemical is processed twice, only count the quantity once towards the processing threshold.
For example, let’s look at a facility where 20,000 pounds of toluene were blended with other chemicals to create a paint product. The paint product was then repackaged into 55 gallon drums for sale. The processing threshold quantity for this facility for that reporting year is only 20,000 pounds.

## Slide 70: Multi-Establishment Facility
Reporting as multi-establishment facility (40 CFR §372.30(c))
  Use the ‘Manage Establishments’ option to create multiple establishments for which to submit reporting forms.
  Multi-establishment facilities have the option to file separate Form R reports for each part of the facility.
  Threshold calculations must account for all the facility’s activities and are not performed at the establishment level.
  Form R reports must include all non-exempt releases and other waste management activities at the facility.
  Use the ‘Report by Part’ option in TRI-MEweb to prepare separate Form R reports for the multi-establishment facility.
  Avoid double-counting at the facility of chemicals involved in intra-facility transfers.
Notes: Facilities that are comprised of multiple establishments must take care to avoid both double counting and under counting of TRI chemicals used across the facility. Multi-establishment facilities are facilities that are comprised of separate economic or organizational units within the facility. Sometimes these separate units can create barriers to information exchange and gaps or overlaps in TRI reporting responsibilities. For threshold determinations, facilities must consider the aggregate amount of TRI chemicals used throughout the facility, including all of the establishments. If a threshold is exceeded, a TRI form is required. Multiple establishment facilities can file separate Form R reports for each part of the facility.
On the TRI Form R and in the reporting software, the filer can designate their submittal for a part of the facility. Remember to report all non-exempt releases and other waste management activities of reportable TRI chemicals for all parts of a facility. When reporting as multiple establishments, avoid double-counting of the same chemicals. When facilities do reports as separate establishments within the same facility, the quantities on the reports will be added together by EPA, and the reports that are made available to the public will show the aggregate amounts.

## Slide 71: Example: EPCRA Section 313 Worksheet for Chemicals with 25,000/10,000-pound Reporting Thresholds
Facility Name: Omni Chemical Date Worksheet Prepared:
Toxic Chemical or Chemical Category: Toluene Prepared By: J.S.P.
Reporting Year:
Step 1. Identify amounts of the toxic chemical manufactured, processed, or otherwise used.
Mixture Name or Other Identifier
1. Bulk Toluene SDS 98 23,000 22,500
2. Joe’s Degreaser Purchasing 50 10,000 5,000
3. Bathroom Paint Vendor 5 30,000 1,500
4. Parts Washer Fluid Purchasing 40 10,000 4,000
5.
6.
7.
Subtotal: 22,500 10,500
Information
Source
Percent
by Weight
Total Weight
(in lb)
Amount of the Listed Toxic Chemical by Activity (in lb):
Manufactured
Processed
Otherwise Used
(A) ___________ lb
(B) ___________ lb
(C) ___________ lb
Mixture Name as Listed Above
1. Bathroom Paint Struct. Comp. 100 1,500
2.
3.
4.
5.
6.
7.
Subtotal: 1,500
Step 3. Calculate the amount subject to threshold: 22,500 9,000
Compare to thresholds for section 313 reporting. 25,000 lb 25,000 lb 10,000 lb If any threshold is met, reporting is required for all activities. Do not submit this worksheet with Form R. Retain for your records.
Applicable
Exemption
Exempt Amount of the Toxic Chemical from Above (in lb):
Manufactured
Processed
Otherwise Used
(A1) ___________ lb
(B1) ___________ lb
(C1) ___________ lb
(A - A1) __________ lb
(B - B1) __________ lb
(C - C1) __________ lb
Step 2. Identify exempt forms of the toxic chemical that have been included in Step 1.
Note Fraction or Percent
Exempt (if Applicable)
Notes: Here we show a threshold worksheet, which can help you to quantify the amounts of TRI chemicals to apply towards your activity thresholds and to determine whether or not you’ve exceeded an activity threshold. In this example, Omni Chemical has filled out a worksheet for toluene.
In the first step, they’ve identified all the mixtures or products that contain toluene at their facility. Omni blends toluene into their ‘Omni Mix’ product, and also otherwise uses a degreaser, some paints, and a wash parts washer fluid which all contain toluene. They’ve recorded where this information was obtained, the percent of the TRI chemical by weight, and a total weight of the mixture. They’ve multiplied the percent of the TRI chemical by the total weight to obtain the quantity of the TRI chemical that was either manufactured, processed, or otherwise used. In this case 22,500 pounds of toluene was processed and 10,500 pounds were otherwise used.
The next step is to identify TRI chemicals that may be exempt. In this case, the bathroom paint, the paint that’s used in the bathrooms, is exempt under the structural components exemption. None of the toluene in the bathroom paint would need to be considered towards the otherwise use activity threshold. So the facility is able to subtract the 1,500 pounds in the paint from their total to obtain 9,000 pounds of toluene that was otherwise used at the facility in the reporting year.
Because the threshold for processing of toluene is 25,000 pounds and the otherwise use of toluene is 10,000 pounds, they have not exceeded either threshold and would not need to complete a TRI report for toluene.

## Slide 72: Record Keeping and Documentation
Importance of good record keeping:
  Detailed records improve reporting, accuracy, and data quality.
  Reduces replication of effort
  Well-labeled calculations and engineering assumptions serve as standard operating procedures for future years.
  Helps ensure consistency from year to year, especially if personnel responsible for reporting change.
EPA Requirements
  Records used to complete Form R must be kept for three years from the time the report was submitted (40 CFR § 372.10).
  EPA may review records during a data quality audit.
  Note that EPA may perform data quality audits going back five years, so it may be useful for facilities to keep records beyond the three-year statutory record keeping requirement.
Notes: It’s very important to keep good records. Keeping detailed records improves the reporting accuracy and the quality of the data. Also, it will reduce replication of effort from year to year. Facilities should also keep good records of calculations, information sources, and assumptions, so that they can form the basis of procedures for completing their threshold determinations and reports in future years. Such practices help ensure consistency from year to year especially when the personnel responsible for TRI requirements changes. Also, record keeping is required by EPA. Facilities must keep their records for three years. And, the EPA can review those records if an audit is conducted at the facility.

## Slide 73: Best Practices for Threshold Determinations and TRI Reporting
Begin early
  Implement a program to gather “real-time” data on usage.
  Searches for historical information can be difficult.
Team approach
  Include all relevant personnel (e.g., engineering, purchasing, environmental, waste management, operations).
Recordkeeping & Documentation
  Keep good records and document all work.
v
v
v
Notes: In threshold determinations and TRI reporting, it helps to begin the process early. Facilities should put systems into place that gather the information in real time. Researching information on TRI chemicals, oftentimes more than a year after they were used at your facility, can be difficult. Use a team approach. Spread the work by involving the people that are using or managing these TRI chemicals – engineers, people in purchasing, in the health and safety department are some examples. Be sure to keep good records, and to document your work.

## Slide 74: TRI Process: 2-Part Process
Notes: The process of completing your TRI forms is a two-step process. We have now reviewed the first step, in which you determine if your facility is required to report to TRI, and if so, which TRI chemicals you would need to report on. We are now ready to move on to the second step, shown on the right. This is the actual release and other waste management reporting – in other words, the information that you would put on a TRI form.

## Slide 75: Section V: Overview of Form R

## Slide 76: Overview of Form R
Two principal types of information required:
  Part I: Facility-specific
  Part II: Chemical-specific
One form must be submitted to EPA and to the State/Tribe for each Section 313 chemical or chemical category exceeding applicable thresholds (assuming other reporting criteria are met).
Forms must be submitted electronically via TRI-MEweb. No paper submissions are accepted (except for trade secrets), including revisions and withdrawals.
Notes: In the next part of this module, we’ll talk about the TRI Form R. For each TRI chemical for which an activity threshold is exceeded, a form would be required to be submitted to the EPA and to the designated state or tribal authority.
The Electronic Reporting rule requires electronic reporting for all non-trade secret forms, including new reports, revisions and withdrawals. All non-trade secret TRI reporting, which accounts for nearly all TRI forms submitted, must be submitted using TRI-MEweb.

## Slide 77: Form R Content
  Section 1: Reporting Year
  Section 2: Trade Secret Information
  Section 3: Certification
  Section 4: Facility Identification
  Section 5: Parent Company Info
  Section 1: Toxic Chemical ID
  Section 2: Mixture Component ID
  Section 3: Activities and Uses
  Section 4: Max Amount On-site during CY
  Section 5: On-site Releases
  Section 6: Off-site Transfers
  Section 7: On-site Waste Treatment, Energy Recovery, Recycling Processes
  Section 8: Source Reduction and Waste Management Activities
  Section 9: Miscellaneous Information
v
v
Part I: Facility Identification Information
Part II: Chemical Identification Information
Notes: Let’s look a little closer at the TRI Form R. The TRI Form R is comprised of two main parts. The first part contains facility-specific information about your facility. There are five sections for reporting information about your facility.
The second part covers information about the chemical for which your facility is reporting. There are nine sections in part two. The first four sections identify the chemical, how it is used at the facility, and the maximum amount on site. The next four sections are what we call the meat of the TRI reporting, and this is where facilities report the actual quantities of the TRI chemicals that were managed as waste. The last section is for reporting optional miscellaneous text information.
Note that much more detail and instructions for completing each section of the TRI Form R can be found in the “Reporting Forms and Instructions” document available from the TRI program website and through the TRI assistance library.

## Slide 78: Part I: Facility Identification
Facility Name and Address (Section 4.1)
  Facility name
    Standard facility names are available through the Facility Registry System (https://www.epa.gov/frs/frs-ez-query).
  Street address (no PO Box or other mailing address)
    Mailing address required if different from street address.
Full or Partial Facility and Federal Facility Designation (Section 4.2)
  Facility type (select one)
    Federal facility;
    Government Owned, Contractor Operated (GOCO); or
    Neither
  For multi-establishment facilities, option to indicate reporting for part of a facility (Form R only)
    Facilities reporting by part use the same TRIFID for all reports.
v
Notes: Part one of the Form R requests facility name, address, and TRI Identification number. Identification information is preloaded into TRI-MEweb if your facility has reported in the past. First, confirm the facility name, or select it from a list if there is more than one facility associated with the TRI-MEweb account. Next, specify whether or not the Form you are completing covers the entire facility, or if it only covers part of the facility, with the rest of the TRI reporting for the facility being covered in other form submissions. You can edit facility information that has been preloaded by selecting “Edit” after selecting the facility.
In the facility identification section, facilities also indicate whether they are a federal facility or a “Government Owned Contractor Operated” facility, or neither. Federal facilities’ names should include the federal department or agency followed by the site name. Facilities must indicate if they elect to report by part, that is submit forms for separate parts of a facility.

## Slide 79: Part I: Facility Identification (continued)
Technical and Public Contact information (Sections 4.3 and 4.4)
  List name, phone number, and email
    Technical contact – should be able to explain data to EPA, not disclosed in the public data releases.
    Public contact – should be able to represent the facility’s data to the public.
Primary and Secondary NAICS code(s) (Section 4.5)
  Enter primary 6-digit NAICS code.
  Enter other applicable NAICS codes in decreasing order of significance.
  https://www.census.gov/naics/
  https://www.epa.gov/toxics-release-inventory-tri-program/tri-covered-industry-sectors
Facility Dun and Bradstreet Number(s) (Section 4.6)
v
Notes: Next, facilities enter the industry codes that best represent their operations. NAICS codes are available in TRI-MEweb or can be found in the website shown here. Remember that the primary NAICS code is the code that represents the largest portion of the facility’s operations as defined by “value added”.
Federal facilities enter the highest level department or agency and check “NA” for Dun and Bradstreet number.

## Slide 80: Part I: Facility Identification (continued)
Parent Company Information (Section 5)
  Parent company name (Section 5.1)
  Parent company Dun and Bradstreet number (Section 5.2)
  TRI-MEweb preloads standardized Parent Company names and D&B number for prior TRI reporters. Reporter may change these preloaded values, if necessary.
  For new TRI reporters, the TRI-MEweb software has a list of standardized Parent Company names. If reporters cannot find correct name from the provided list, enter a new name.
To verify the accuracy of facility and parent company D&B number and name, go to: https://www.dnb.com/duns-number/lookup.html or call 1-888-814-1435
v
Notes: Private sector facilities report information on their parent company, including its name and Dun and Bradstreet number. The parent company is the highest level of ownership within the United States and is pre-loaded in TRI-MEweb. If you do not have a parent company, check “No U.S. Parent Company (for TRI Reporting purposes).”
Facilities can search can use the website or phone number shown here to obtain this information to obtain their facility or parent Dun and Bradstreet number.

## Slide 81: Part II: Chemical-Specific Information
EPCRA Section 313 Chemical Identify (Sections 1 and 2)
The vast majority of submitted forms use these sections to identify the EPCRA section 313 chemical being reported:
  CAS Number or Chemical Category Code (Section 1.1)
  Chemical or Chemical Category Name (Section 1.2)
If the supplier withholds the chemical name as a trade secret:
  Generic Chemical Name Provided by Supplier (Section 2.1)
  Do not report chemical name or CAS number.
If claiming chemical name as a trade secret:
  Generic Chemical Name (Section 1.3)
  Do not report chemical name or CAS number on the sanitized form.
v
Notes: Facilities identify the TRI chemicals on which they are reporting. Facilities enter the chemical name and the “chemical abstract service” number or the TRI chemical category code or select it from the list provided in TRI-MEweb. In some cases, the facility’s chemical supplier may have claimed a trade secret for a particular TRI chemical and the facility does not know the actual name of the TRI chemical for which they are submitting a report. In this scenario, the facility enters the generic descriptive provided. For those facilities that are claiming a trade secret the chemical name is only entered and the public version of the TRI Form R shows only the generic descriptive for the chemical.

## Slide 82: Activities and Uses
Activity and Uses of the EPCRA Section 313 Chemical at the Facility (Section 3)
  Check all applicable boxes reflecting all manufacture, process, and otherwise use activities.
  Report only activities taking place at reporting facility.
  Identification of specific subcategories are required certain processing and otherwise use activities.
v
Notes: Next, facilities report the activities and uses of the TRI chemical at the facility. Be sure to check all applicable boxes.

## Slide 83: Activities and Uses (continued)
Section 3 requires indication of more specific subcategories for certain processing and otherwise use activities
3.2a. As a reactant | 3.3a. As a chemical processing aid | 3.3c. Ancillary or other use
P101: Feedstocks | Z101: Process solvents | Z301: Cleaner
P102: Raw materials | Z102: Catalysts | Z302: Degreaser
P103: Intermediates | Z103: Inhibitors | Z303: Lubricant
P104: Initiators | Z104: Initiators | Z304: Fuel
P199: Other | Z105: Reaction terminators | Z305: Flame retardant
 | Z106: Solution buffers | Z306: Waste treatment
3.2b. As a formulation component | Z199: Other | Z307: Water treatment
P201: Additives |  | Z308: Construction Materials
P202: Dyes | 3.3b. As a manufacturing aid | Z399: Other
P203: Reaction diluents | Z201: Process lubricants | 
P204: Initiators | Z202: Metalworking fluids | 
P205: Solvents | Z203: Coolants | 
P206: Inhibitors | Z204: Refrigerants | 
P207: Emulsifiers | Z205: Hydraulic fluids | 
P208: Surfactants | Z299: Other | 
P209: Lubricants |  | 
P210: Flame retardants |  | 
P211: Rheological modifiers |  | 
P299: Other |  | 
v
Notes: Starting with Reporting Year 2018, Form Rs now require a facility to indicate more specific subcategories for certain processing and otherwise use activities. Facilities indicate whether the reported ECRA Section 313 chemical is manufactured (including imported), processed, or otherwise used by the facility and the general nature of such activities and uses at the facility during the calendar year. Specifically, processing categories “as a reactant” and “as a formulation component” now contain subcategories as do all otherwise use categories (i.e., "as a chemical processing aid," "as a manufacturing aid," and "ancillary or other use").

## Slide 84: Maximum On-Site Amount
Select appropriate code indicating the maximum quantity on-site during the reporting year (Form R, Part II Section 4).
Use maximum total (non-exempt) amount present at one time during reporting year, even if the Section 313 chemical is present at more than one location at the facility.
  Based on amount in storage, process, and wastes
  Maximum amount on site may differ from the Tier II-reported maximum amount on site value.
    Tier II is usually by mixtures; Form R is chemical-specific.
    Tier II excludes hazardous wastes; Form R does not.
WEIGHT RANGE IN POUNDS |  | 
Range Code | From | To
01 | 0 | 99
02 | 100 | 999
03 | 1,000 | 9,999
04 | 10,000 | 99,999
05 | 100,000 | 999,999
06 | 1,000,000 | 9,999,999
07 | 10,000,000 | 49,999,999
08 | 50,000,000 | 99,999,999
09 | 100,000,000 | 499,999,999
10 | 500,000,000 | 999,999,999
11 | 1 billion | More than 1 billion
Notes: Facilities are also required to report the maximum quantity of the TRI chemical that was on site at any one time during the reporting year. The quantity is reported by entering a code representing a range of pounds of the chemical. The codes are available from the “Reporting Forms and Instructions” document and from the TRI-ME reporting software. Note that this quantity is comprehensive of all locations and uses of the chemical at the facility including quantities in storage, in the process stream, and in wastes. This is different from Tier two maximum amount on site which includes the weight of the entire mixture and does not include quantities in hazardous wastes.

## Slide 85: Reporting Releases and Other Waste Management
In the following sections, reporters provide quantitative data regarding toxic chemical releases and other waste management including:
  Quantity of the toxic chemical entering each environmental medium on-site (Section 5)
  Transfers to other off-site locations (Section 6)
  On-site waste treatment, energy recovery, and recycling methods and quantities (Sections 7, 8.2, 8.4, and 8.6)
Notes: In completing the Form R, facilities also report how, and how much of, the TRI chemical was released to the environment, transferred off-site for further waste management or managed as a waste on-site. The next slides cover the steps for reporting this information.

## Slide 86: Tools and Data Sources for Release and Other Waste Management Calculations
Previous year Form R report(s) and documentation
Process flow diagrams
Environmental monitoring data
Permit applications
EPCRA, CERCLA, RCRA, NPDES, CAA and other env. reports
Waste management manifests, invoices, and waste profiles
Engineering calculations and other notes
EPA guidance (AP-42, WebFIRE, TANKS, WATER9)
v
Notes: Where do you get the information to calculate your releases and other waste management quantities for your Form R? Some sources are listed here. Previous year Form R reports and documentation are a starting point for many TRI filers. Process flow diagrams, monitoring data – again, you don’t have to collect it for TRI, but you may have already collected it for other purposes. Permit applications are another source – often many release estimates go into the application and that may be useful for TRI reporting.
Other environmental reports may be helpful sources – for example, you may have state pollution prevention reports or RCRA biennial reports. If you have a NPDES permit, you may have discharge monitoring reports that include one or more of the TRI chemicals. Be sure to look across media for potential sources. Waste management manifests can be a good source of information for estimating the quantity of a chemical sent offsite.

## Slide 87: Estimating Quantities Released or Otherwise Managed as Waste
Consider all sources of toxic chemical releases and other waste streams, both routine and non-routine.
Reasonable estimates are required by law.
TRI does not require additional monitoring, but it does require the best reasonable approach for making all calculations.
Data and approach must be documented and should be consistent with the document approach.
The upcoming slides describe an overview of the process.
v
Notes: When estimating release and other waste management quantities for sections 5 and 6 of Part II of the Form R, be sure to consider all sources and uses of the TRI chemical, not just your main feedstocks. For example, consider chemicals that are used to clean production equipment, fuels, maintenance chemicals, catalysts, and lubricants for machinery. These all could be sources of TRI chemicals.
Reasonable estimates are required by law. However, the best approach is usually facility-specific. The data and approach must be documented and should be consistent. Facilities are required to use their best available information. While measuring and monitoring are not required by TRI, it may be that existing measurements and monitoring data are the best available information. Facilities need to determine the best reasonable approach to their estimates.

## Slide 88: Data Precision
EPA allows using two significant figures when reporting releases and other waste management estimates
  The number of significant figures is typically the number of non-zero digits.
  If estimate is more precise, additional significant figures may be used based on precision of data used to calculate estimate
    Regardless of estimation precision, however, non-CSC chemical quantities should be entered in whole numbers in TRI-MEweb.
    Note that certain waste management quantities calculated automatically by TRI-MEweb may include up to two decimals.
For estimates of non-CSC Section 313 chemicals under 1,000 pounds, a range code can be used*:
  A= 1-10 pounds; B = 11-499 pounds; C = 500-999 pounds
    Note: If you enter a range code, TRI data tools used by the public will display the midpoint of the range (e.g., 5, 250, or 750 lb)
Note that similar quantities reported in Section 8 of Form R must be actual values and not ranges. The Section 8 Calculator in TRI-MEweb will assume the midpoint of any ranges reported in Sections 5 and 6 when calculating quantities for Section 8. If you do not wish to use the midpoint of the range in Section 8 calculations, it is best to enter a value rather than a range in Section 5
*
Notes: EPA allows using two significant figures when reporting release and other waste management quantities. If your underlying data support a more precise estimate, additional significant figures may be used. In Sections 5 and 6 of the TRI Form R, facilities have the option of reporting one of three “range codes” in place of actual quantities of chemicals, if the quantity is less than 1,000 pounds, AND if the chemical is not a Chemicals of Special Concern. Range codes cannot be used for Chemicals of Special Concern; instead the actual quantity must be entered for Chemicals of Special Concern.

## Slide 89: Data Precision (continued)
For Chemicals of Special Concern, facilities must report releases and other waste management quantities at a level of precision supported by the data and estimation techniques used.
For Chemicals of Special Concern, 0.1 pound (100 micrograms for dioxins) is the smallest amount required to be reported.
  Estimates < 0.05 pounds (< 50 micrograms for dioxins) can be rounded down to zero pounds
TRI-MEweb will allow for decimal reporting for Chemicals of Special Concern (e.g., 9.3 pounds, 0.2 pounds).
v
Notes: Data precision requirements are different for Chemicals of Special Concern, because of the much lower thresholds associated with these chemicals. While non-CSC chemicals are reported to the nearest whole number, for Chemicals of Special Concern, facilities report to the nearest 10th of a pound. The exception is for dioxin, where quantities should be reported to the nearest 100 micrograms. For Chemicals of Special Concern, reported quantities can be rounded down to zero if less than .05 pounds. Quantities of 50 micrograms or less of dioxin can be rounded down to zero.
When using the TRI-ME web reporting application, the systems recognize the chemicals as either Chemicals of Special Concern or non-CSC and will allow decimal reporting for Chemicals of Special Concern and not for non-CSC chemicals.

## Slide 90: “NA” vs. “0”
All data elements in Sections 5, 6, 7, and 8 must be completed. If you determine that there was no release, transfer, or waste management quantity:
  Use “NA” (not applicable) when no possibility of the Section 313 chemical being released to or otherwise managed as waste in that media (e.g., facility has no on-site landfill; has not transferred any waste to an off-site location; has not performed on-site recycling) OR
  Use “0” when no release occurs or < 0.5 pound of a non-CSC Section 313 chemical from a waste stream is directed towards that medium.
    Example: Discharge to water is zero; however, release possible if control equipment fails.
    Must indicate a Basis of Estimate code (i.e., M1, M2, C, E1, E2, O) for all numerical estimates, including “0.”
v
Notes: It is important for TRI filers to understand the difference between reporting a zero and reporting “N/A,” for “not applicable.” Use “N/A” when there is no possibility of that chemical being released to or otherwise managed as waste in that medium.
For example, in Section 5 of the Form R, facilities enter the quantity of the TRI chemical that went to their on-site landfill. If the facility does not have an on-site landfill, there is no way that the chemical could go to an on-site landfill, so they report “N/A”. Facilities should use zero when no release occurs or less than half a pound of the non-CSC chemical is directed towards that medium. For example, if a facility has a waste stream discharged to water and has control equipment in place that completely removes the TRI chemical from the waste stream prior to discharge, they would enter a zero as the quantity discharged. They use a zero instead of N/A because a discharge is possible if, for example, their control equipment was not removing 100% of the chemical. Note that a Basis of Estimate code is required for all numerical estimates, including zero. A Basis of Estimate code should not be entered when “N/A” is reported.

## Slide 91: Basis of Estimate Codes
One of the following “Basis of Estimate” codes must be listed on the Form R for each release and off-site transfer quantity reported:
  Continuous monitoring (M1)
  Periodic or random monitoring (M2)
  Mass balance calculation (C)
  Published emissions factors (E1)
  Site-specific emissions factors (E2)
  Engineering calculations (O)
    Everything NOT M1, M2, C, E1 or E2 above, such as:
      Best engineering judgment
      Estimated removal efficiencies
      Non-chemical-specific and non-published emission factors
Use the code on the Form R for the method used to estimate the largest portion of the release.
v
Notes: For each chemical quantity entered in Sections 5 and 6 of the Form R, facilities much also indicate how the quantity was estimated by entering a “basis of estimate” code. Is the estimate based on data from a continuous monitoring system? If so, enter a Basis of Estimate code of M1. Enter “M2” if the estimate is based upon periodic or random monitoring. Is the estimate based on a mass balance calculation? That would be a Basis of Estimate Code of C. If the quantity is based on a published emission factor, then enter “E1” as the Basis of Estimate code. E2 is for site-specific emissions factors that are non-published, that were perhaps developed through in-house testing, or were provided by the vendor of your process or pollution control equipment. The last code, “O”, is for “other” and is used for engineering calculations. O is also any other method that is not covered by the other codes.
In some cases, the quantity entered on the TRI Form could be based on multiple estimation techniques. In these cases, enter the basis of estimate code that represents the largest portion of the estimate.

## Slide 92: Estimating Releases When No Data Available
Example
Metal dust observed on floor near or within metalworking operation indicates fugitive air emission occurring and possible transfer off-site; however, no additional data are available:
  Work with operations personnel familiar with the operation to gather relevant information about the releases or waste generation.
  Document the calculations performed and keep records for future reporting and in case of audit.
  Basis of Estimate code 'O' will likely be used.
  Range codes may be used in some situations.
Notes: Another common question is: how do you come up with an estimate when there are no data available? This comes up often in the case of fugitive emissions. Facilities may have a process and a chemical for which they know that fugitive air emissions occur, based on the nature of the process or of the chemical, but do not know how to go about quantifying those fugitive emissions.
The example shown here is for a metalworking operation where there is metal dust on the floor indicating fugitive air emissions are occurring.
How can the facility quantify these fugitive emissions?
Facilities can work with the operations personnel familiar with the operation in determining when the dust is generated, how it is generated, and its composition (and specifically how much of the TRI chemical in question does it contain). Then they use their best engineering judgment to indicate the quantity of release. Because it will not be a precise estimate, they may want to consider using a range code. They will also have to indicate the Basis of Estimate code for the quantity of fugitive emissions, which is likely the “O” Basis of Estimate code for engineering judgment.

## Slide 93: Release or Disposal Quantity Entering Each Medium
Air:
  Fugitive or Non-Point Air Emissions (Section 5.1)
  Stack or Point Air Emissions (Section 5.2)
Water:
  Discharges to Receiving Streams or Water Bodies (Section 5.3)
Land:
  Underground Injection Wells (Section 5.4)
  Disposal to Land On-site (Section 5.5)
Report total releases or disposal of the chemical to each environmental medium on-site (Section 5):
Quantities reported should reflect the sum of all annual releases or disposal from all sources.
v
v
v
Notes: In Section 5 of the Form R, facilities report the quantities of the TRI chemical that are released or disposed of to each environmental medium on-site for that reporting year. Air releases include both fugitive or non-point air emissions, which are reported in Section 5.1, and stack or point air emissions, which are reported in Section 5.2. On-site releases to water are reported in Section 5.3. On-site disposal to land includes eight subcategories, reported as underground injection well types (in Section 5.4) or different land disposal units, such as landfills and surface impoundments (in Section 5.5).
The following slides will detail each part of Section 5 further.

## Slide 94: On-Site Air Emissions
Enter total fugitive releases of the Section 313 chemical, including leaks, evaporative losses, building ventilation, or other non-point air emissions (Section 5.1).
Enter total releases to air from point sources, including stacks, vents, pipes, ducts, storage tanks, or other confined air streams (Section 5.2).
Data sources commonly used for air emissions calculations.
  Air permit applications
  CAA Title V air inventories
  Process and production data
  Published emission factors
  Facility-specific monitoring data and emissions factors
v
Notes: In section 5.1 of the Form R, facilities are required to enter the quantity of the TRI chemical that is released to the air from fugitive and non-point sources. Fugitive and non-point emissions include leaks, evaporative losses, building ventilation, and any other air emissions that cannot be traced to a discreet point.
Next in section 5.2 of the Form R, facilities are asked to enter the quantity of the TRI chemical that was released to the air via stacks or other point sources such as vents, pipes, ducts, storage tanks, and any other confined stream.
In some cases these emissions may already be monitored or estimated for air permits or other regulatory requirements. In other cases they can be estimated from emissions factors and production data.
As with all estimates entered in Sections 5 and 6, enter the basis of estimate code that best represents the estimation technique used.

## Slide 95: On-Site Wastewater Discharges
Releases to streams or water bodies (Section 5.3)
  Use the map provided in TRI-MEweb to select the receiving Stream or Water Body Name. Select as many unique receiving streams or water bodies as needed. If not found, manually enter the name.
  TRI-MEweb will automatically provide the Reach Code (optional), that describes the specific outfall location.
  Enter the Total Quantity of the Section 313 chemical released to each receiving stream or water body.
  Enter the numeric Basis of Estimate code.
  Indicate Percentage from Stormwater of total quantity released (choose NA if not applicable).
  Indicate NA for Section 5.3 if the facility does not discharge the Section 313 chemical to streams or water bodies.
v
Notes: On-site wastewater discharges are reported in Form R Part Two, Section 5.3. First, facilities report releases directly discharged to a stream or water body. Often these are regulated and monitored as part of an NPDES permit. Facilities will use a map TRI-MEweb to identify the name of the water body. If it does not have a name, then report the name of the nearest downstream water body that does have a name.
After entering the total quantity, facilities indicate basic of estimate code and the percentage of the total quantity that can be attributed to stormwater releases.

## Slide 96: Wastewater Considerations
Be inclusive of all on-site sources, including:
process outfalls such as pipes and open trenches
releases from on-site wastewater treatment systems
contribution from stormwater runoff (including unchanneled runoff)
Transfers to publicly-owned treatment works (POTW) (Section 6.1) and other off-site wastewater treatment facilities (Section 6.2) are reported separately
Wastewater Data Sources
  Discharge monitoring report (DMR) or related wastewater monitoring reports
  Other monitoring data such as permit applications
  Flowmeter data
  If no monitoring data exists, estimate based on process knowledge and/or mass balance calculation
v
Notes: Be inclusive of all on-site discharges, including stormwater runoff. If applicable, the facility must include quantities of Section 313 chemicals in stormwater in the total quantity released (by weight) and report the indicate the percentage contributed by stormwater. Remember that wastewater released by the facility directly to a stream or water body are reported as an on-site wastewater discharge. Off-site transfers to a POTW or other off-site wastewater treatment facility are reported separately as off-site transfers for further waste management.
To calculate the quantity of the TRI chemical discharged, facilities may have monitoring data available, such as may be required under a NPDES report. If no monitoring data exist, facilities should use the most appropriate methods including general process knowledge and mass balance calculations.

## Slide 97: On-Site Underground Injection Wells
Underground injection to Class I wells (Section 5.4.1)
  Enter total amount of Section 313 chemical injected into Class I wells at facility and basis of estimate code.
Underground injection to Class II - V wells (Section 5.4.2)
  Enter total amount of Section 313 chemical injected into Class II - V wells at facility and basis of estimate code.
Note: Basis of estimate code must be entered for all quantities.
v
Notes: Facilities also must report releases of the TRI chemical to underground injection wells. Underground injection wells are classified and regulated under the Safe Drinking Water Act. Quantities are entered separately for Class one wells and for Class two through five wells. Facilities that do not have underground injection wells should check “NA” in this section.

## Slide 98: Other Disposal to Land On-Site
Enter quantity of toxic chemical entering each on-site land disposal option (Section 5.5).
  On-site landfills: RCRA Subtitle C (Section 5.5.1A)
  On-site landfills: other (Section 5.5.1B)
  On-site land treatment and application farming (Section 5.5.2)
  On-site surface impoundments: RCRA Subtitle C (Section 5.5.3A)
  On-site surface impoundments: Other (Section 5.5.3B)
  Other disposal (includes spills or leaks to land) (Section 5.5.4)
Quantities released to air or water during the reporting year of the initial release to land (e.g., volatilization from surface impoundments) are not included in the land disposal quantity.
A facility may indicate that on-site disposal includes quantities of the chemical being managed in “waste rock piles.”
v
Notes: There are a variety of ways that facilities can dispose of TRI chemicals to the land. In this part of the TRI-MEweb reporting software and Form R, facilities report the quantity of the chemical released to the land via onsite RCRA subtitle C landfills, other landfills, land treatment or land farming, RCRA Subtitle C surface impoundments, other surface impoundments, and other disposal.
“Other disposal” includes any spills or leaks to land. Note that if a portion of the TRI chemical that is disposed of to land onsite volatilizes to the air or washes to a water body during the reporting year, that quantity is not reported here, but in the section most appropriate for that medium.
A facility may indicate that reported on-site disposal quantities include quantities of the chemical being managed in “waste rock piles," and may provide the amount of the chemical managed in such piles. Waste rock refers to rock that contains insufficient metal concentration to economically process at any given time and is thus typically removed from a mine to allow access to the ore-grade rock.

## Slide 99: Off-Site Transfers
Transfer(s) of the Toxic Chemical in Wastes to Off-Site Locations (Section 6)
  These data include off-site receiving facility location
  Report quantities of chemical sent off-site to each POTW or other locations for recycling, energy recovery, waste treatment, or disposal
  Report only total quantity of chemical transferred off-site, not the quantity of entire waste stream mixture
  Range codes may be used for transfers of non-CSC chemicals under 1,000 lb.
  Basis of estimate codes are required for each transfer.
Notes: The off-site transfers section of TRI-MEweb covers Section six of Form R. Off-site transfers include any transfers of the TRI chemical to another facility for the purpose of waste management including off-site waste treatment, recycling, energy recovery, or disposal. As in Section 5, any quantity reported in Section 6 that is under 1,000 pounds AND that is for a non-CSC can instead be represented by one of the range codes shown here. Also, as in Section 5, basis of estimate codes are required for each quantity entered.
Note that similar quantities reported in Section 8 of Form R must be actual values and not range codes. The Section 8 Calculator in TRI-MEweb, which uses information reported in sections 5 and 6, will assume the midpoint of any ranges reported in Sections 5 and 6 when calculating quantities for Section 8.

## Slide 100: Transfers to POTWs
Discharges to Publicly Owned Treatment Works (Section 6.1)
  Include name and address for the receiving POTW
    POTW Widget in TRI-MEweb helps reporters identify their POTW
  For each different ultimate disposition of the chemical following the transfer to the POTW, enter the quantity, basis of estimate, and P code.
Facilities provide the ultimate disposition of toxic chemicals at POTWs using P codes.
  P codes are listed in the Reporting Forms and Instructions.
  For facilities that do not know ultimate disposition details, TRI-MEweb will apply distribution removal and release percentages to the total quantity of a chemical transferred to a POTW to help populate P code reporting
Notes: Facilities must report the quantities of TRI chemicals that are transferred in wastewater to a publicly owned treatment works, or POTW. When reporting a discharge to a POTW, TRI-MEweb and the Form R require the name of the POTW to which the TRI chemical is being transferred. Facilities can use a search tool in TRI-MEweb or one of the EPA websites shown here to find the official name of their POTW.
Facilities will report quantities individually for each transfer by waste management type to describe the chemicals’ ultimate disposition at the POTW. Waste management codes for the transfers of waste to POTWs, known as P Codes, are found in the RFI. If a facility does not have POTW ultimate disposition information, the POTW Disposition Calculator will help reporters by using default distributions.
Also note if you know the percentage of the chemical that is released by the POTW, you can enter it manually, and it will be applied in the automatic Section 8 calculations.

## Slide 101: Other Off-Site Transfers
Enter transfers to other off-site locations (Section 6.2).
  Include name, address, and EPA identification (RCRA ID) number of the receiving facility.
  Enter quantity, basis of estimate, and M code for each different waste management activity (waste treatment, disposal, recycling, and energy recovery).
  M codes are listed in the Reporting Forms and Instructions.
  Check “NA” box to indicate no transfers to off-site locations.
Common data and tools used to complete this section:
  Waste manifests and vendor receipts
  RCRA reports
  Waste characterization - analyses, profiles
v
Notes: The off-site transfers section of TRI-MEweb also covers all other transfers of the TRI chemical off-site for waste management. The name, address and EPA ID, if applicable, of the facility receiving the TRI chemical is entered. For each off-site location, the quantity and basis of estimate code associated with each waste management activity are entered. The types of waste management activities are specified using the appropriate “M code” for each activity. The list of “M codes” are available in the “Reporting Forms and Instructions” document as well in the TRI-MEweb reporting application. The quantities of TRI chemical sent off-site to be managed as waste are often recorded by facilities as part of their regulatory requirements and recordkeeping systems. Facilities should take advantage of existing sources of information to assist with developing their estimates for this and other sections of the TRI Form R.

## Slide 102: Tips for Off-Site Waste Transfers
Identify all sources of off-site transfers of TRI chemicals. Potential off-site waste transfers of reportable chemicals include:
  Hazardous waste
  Non-hazardous waste (e.g., waste oil and coolant)
  Trash
  Scrap metal (reuse versus recycle)
  Container residue: RCRA empty is NOT EPCRA empty
  BE COMPREHENSIVE!
Identify basis of estimate sources for waste composition data
Identify final disposition of each Section 313 chemical:
  Indicate disposal, waste treatment, energy recovery, recycling by selecting the appropriate P or M code.
  These codes are provided in Sections 6.1 and 6.2 of the Reporting Forms and Instructions.
Notes: Here are some tips specific to reporting off-site transfer quantities. First, Identify all possible sources of waste sent off-site. Hazardous waste is one source and other waste manifests may be helpful in calculating the quantity of some TRI chemicals sent off-site. However, also consider TRI chemicals in non-hazardous wastes, such as chemicals in waste oil, coolant, trash, or scrap metal. Also consider container residue – the RCRA definition of an “empty” drum may still contain TRI chemicals. These quantities need to be included as off-site transfers on Form R. For all quantities of the TRI chemical sent offsite for waste management, record the “M” code, describing how the chemical was managed offsite. If a waste going offsite for incineration contained 100 pounds of the TRI chemical, 100 pounds would be reported as an “other off-site transfer” along with the name and location of the site it is being sent to, and the “M code” for incineration. If another waste stream contained 300 pounds of the same TRI chemical and was being sent to a different location for metals recovery, the 300 pounds would be listed separately, along with the name and location of the receiving facility, and the M code for metals recovery.

## Slide 103: Wastes Otherwise Managed On-Site
On-Site Waste Treatment
Examples of on-site waste management include:
  Air pollution control devices
  Wastewater treatment processes
  Incineration or thermal destruction
  Chemical oxidization
Recycling Methods (Section 7)
Energy Recovery
  Neutralization
  Energy recovery devices
  Recycling devices
Notes: In completing the Form R, facilities also report how, and how much of, the TRI chemical was otherwise managed as a waste on-site, other than environmental releases. How much of the chemical was treated for destruction in air pollution control devises or wastewater treatment processes, for example; how much was used for energy recovery, how much was recycled, and descriptions of the actual processes that the waste stream went through at the facility. The information entered in this part of the TRI-MEweb reporting application covers Section 7 and portions of Section 8 of the Form R.

## Slide 104: Waste Treatment Methods and Efficiency
Report each waste treatment method that each waste stream containing the Section 313 chemical undergoes (Section 7A).
  Treatment methods include destruction or physical removal.
  Include all methods even if a method has no effect on the chemical.
  Report the efficiency of the waste treatment methods at eliminating the Section 313 chemical from the waste stream.
  Enter total quantity treated on-site for all methods in Section 8.6.
  Option to provide additional details about waste treatment in Section 8.11 Optional Pollution Prevention Information
v
Notes: When reporting on waste streams undergoing treatment on-site, “treatment” means that the waste chemical is removed from the waste stream or destroyed. In the Waste Treatment Methods and Efficiency section, facilities describe each waste stream containing the TRI chemical using a “waste stream code” that denotes whether the waste stream is solid, liquid, or gaseous. Next, facilities enter the codes that represent each of the waste treatment methods that the waste stream goes through in order. All treatment methods must be recorded, even if the method does not affect the TRI chemical.
For each waste stream, the facility also reports a code that represents the range of treatment efficiency that the combined waste treatment methods had on the TRI chemical. Finally, in Section 8.6, the facility reports the total quantity of the chemical that was destroyed by treatment on-site.
Note that all of the codes required for Section 7 can be obtained from the “Reporting Forms and Instructions” and through the TRI-ME web reporting applications.

## Slide 105: Energy Recovery Methods and Quantity
Enter on-site energy recovery methods (Section 7B) and total quantity (Section 8.2) for Section 313 chemical.
  Section 313 chemical must be combustible and have a significant heating value (>5,000 BTU/lb).
  Combustion unit is integrated into an energy recovery system (e.g., industrial furnace, industrial kiln, or boiler).
v
Enter codes in descending order by quantities combusted
TRI-MEweb collects methods and quantity data simultaneously.
Option to provide additional details about energy recovery in Section 8.11
Notes: The next section covers on-site energy recovery processes that the TRI chemical goes through and the quantities of the TRI chemical that was combusted for energy recovery. Only chemicals that have a significant heat value and for which the heat energy is actually recovered should be reported in this section. Up to three codes representing each energy recovery method that the TRI chemical enters are reported.

## Slide 106: Recycling Methods and Quantity
v
Enter recycling methods used (Section 7C) and total quantity for on-site recycling (Section 8.4) of the Section 313 chemical.
  Codes for recycling methods used are found in EPA’s TRI Reporting Forms and Instructions document
  Do not include energy recovery processes.
Enter codes in descending order by quantities recycled
TRI-MEweb collects methods and quantity data simultaneously
Option to provide additional details about recycling in Section 8.11
Notes: The next section covers on-site recycling processes that the TRI chemical goes through. Note that recycling recovers the TRI chemical from the waste stream so that it can be used over again. It does not include energy recovery. The quantity and up to two codes representing each recycling method that the TRI chemical enters are reported.

## Slide 107: Release and Other Waste Management Estimates
Helpful hints for accurate release estimates:
  Always use your best available information.
  Estimate the quantity of Section 313 chemical, not the entire waste stream.
  Differentiate fugitive from stack air emissions.
  Zero air emissions for volatile organic compounds are unlikely.
  Watch out for releases of Section 313 chemicals with qualifiers.
  Check your math and document your work!
Result of release estimation errors:
  Incorrect release estimates and inconsistencies could carry over from year to year.
v
Notes: Here are a few helpful hints for estimating release and other waste management quantities reported on the Form R.
First, consider all sources of information and use the best available information for release and other waste management estimates.
Be sure to estimate the quantity of the TRI chemical and not the entire waste stream. For example, when using data from a waste manifest that shows the weight of the entire waste mixture sent off-site, be sure to base release and other waste management estimates on only the amount of the TRI chemical in that waste mixture.
Be sure to differentiate between your fugitive and your stack air emissions. When reporting for a VOC, or volatile organic compound, be sure to estimate fugitive losses of the chemical – it is unlikely to have zero fugitive air emissions.
Pay attention to the TRI chemical qualifiers and remember that the form of the chemical described in the qualifier is the only form that needs to be considered for TRI.
Also, always check your math and document your work.
Be aware that errors can carry over from year to year.

## Slide 108: Source Reduction and Waste Management
Section 8 of Form R focuses on pollution prevention mandated by Section 6607 of the Pollution Prevention Act of 1990 (PPA).
The waste management hierarchy shows that pollution should be reduced at the source whenever feasible and released to the environment only as a last resort
Notes: The final section of the Form R, Section 8, is the section of Form R focused on pollution prevention. This pollution prevention hierarchy shown here was institutionalized by the Pollution Prevention Act of 1990, and the idea here is that facilities always want to be moving up this triangle toward source reduction. Facilities should look for opportunities for source reduction and think about how they can avoid creating wastes in the first place. If that is not possible, they should look at opportunities for recycling the chemical. If that’s not possible, they move down the hierarchy and determine if the chemical can be treated. If there is no way to destroy the chemical, then their last resort is disposal or release to the environment. So, we always want to be evaluating ways to move towards source reduction. Section 8 of the TRI Form R is intended to help track progress and identify opportunities for pollution prevention. In Section 8, facilities report quantities for the current reporting year, as in the other sections of the form, but quantities are also reported for the previous year, and they are projected out for the next two years. This provides a trend over time to look at to determine if there are more opportunities to move up this pollution prevention hierarchy.

## Slide 109: Production-Related Waste Managed (Section 8.1-8.7)
The sum of sections 8.1 through 8.7 represents the total quantity of waste generated through regular production activities at your facility for the reporting year.
Waste management quantities must be reported for prior year, current reporting year, following year, and second following year.
  Prior Year: TRI-MEweb automatically calculates Section 8.1 through 8.7 quantities from prior submissions (or indicates N/A if no report was submitted).
  Current Year: TRI-MEweb automatically calculates Section 8.1, 8.3, 8.5, and 8.7 quantities from Section 5 and 6 data. Reporters must enter total on-site energy recovery, recycling, and treatment quantities (Section 8.2, 8.4 and 8.6).
  Following Year and Second Following Year: Reporters must provide estimates for Section 8.1 – 8.7.
v
Notes: First you’ll enter the quantities of waste that you release, use for energy recovery, recycle, and treat, both on- and off-site. This is referred to as the “production-related waste.”
In Section 8.1, the quantity of the chemical released is reported. In Sections 8.2 and 8.3, the quantities of the chemical used for energy recovery on-site and off-site are reported. Remember, to be reported as energy recovery, the TRI chemical must have a significant heat value and that heat must be recovered. In Sections 8.4 and 8.5, the quantities of the chemical recycled on-site and off-site are reported. And, in Sections 8.6 and 8.7, the quantities of the chemical treated on-site and off-site are reported. Under TRI, treatment means “destroyed”, so metals, which cannot be destroyed, should not be reported in these sections.
Adding up the quantities in section 8.1 through 8.7 gives the total quantity of waste generated from production activities at the facility. This includes the total quantity released, treated, recycled, or used for energy recovery. Some of these quantities may have already been calculated to complete Form R section 5 for on-site releases and section 6 for off-site transfers. The TRI-MEweb application includes a Section 8 calculator tool that will help with these calculations. However, the quantities reported in sections 5 and 6 of the form can differ from those reported in Sections 8.1 through 8.7. The sections 5 and 6 quantities should include any TRI chemicals released and transferred as part of a remedial clean-up action or catastrophic one time event. These non-production-related quantities are NOT included in Sections 8.1 through 8.7. TRI-MEweb will ask if any of the quantities reported in sections 5 and 6 were associated with remedial actions or catastrophic one time events, and if so, how much. Then, using the information already entered into TRI-MEweb, the Section 8 calculator will populate the quantities for the current year column of Section 8. However, in the Source Reduction and Waste Management portion of the Form R, as shown here, facilities are not only required to report on the current year’s activities, but also the previous year’s quantities and estimates for the next two years.
If your facility reported on this chemical in the previous year, TRI-MEweb will pre-populate the prior year column. Facilities then only need to estimate quantities for the following two years.

## Slide 110: Production-Related Waste Managed (Section 8.1-8.7)
Notes: This screenshot of the Form R shows how source reduction and waste management information is reported to EPA for Sections 8.1-8.7. The production-related waste managed data are broken down by section and by reporting year quantities.

## Slide 111: Section 8: Relationship to Sections 5 and 6
PART II. SECTION 8.1 – 8.7 | 
8.1a | Total on-site disposal to Class I UIC wells, RCRA & other landfills = 5.4.1 + 5.5.1A + 5.5.1B – 8.8*
8.1b | Total other on-site disposal or other releases = 5.1 + 5.2 + 5.3 + 5.4.2 + 5.5.2 + 5.5.3A + 5.5.3B + 5.5.4 – 8.8*
8.1c | Total off-site disposal to Class I UIC wells, RCRA & other landfills = 6.1 (P33, P34) + 6.2 (M64, M65, M81) – 8.8*
8.1d | Total other off-site disposal or other releases = 6.1 (P30, P31, P32, P35, P36) + 6.2 (M10, M41, M62, M66, M67, M73, M79, M82, M90, M94, M99) – 8.8*
8.3 | Off-site energy recovery = 6.2 (M56, M92) – 8.8*
8.5 | Off-site recycling = 6.2 (M20, M24, M26, M28, M93) – 8.8*
8.7 | Off-site treatment = 6.1 (P37, P38, P39) + 6.2 (M50, M54, M61, M69, M95) – 8.8*
* Section 8.8 includes quantities of toxic chemicals disposed of or otherwise released on-site or managed as a waste off-site due to remedial actions, catastrophic events, or one-time events not associated with the production process.
Notes: This table shows the subsections of Section 8 that may be derived from information that was already recorded in Section 5 (onsite releases) and in Section 6 (offsite transfers) of the Form R. For example, quantities recorded for the chemical as on-site releases are reported in Section 8.1 unless the release was due to a catastrophic or other one-time event. Section 8.1 is for quantities of the chemical disposed of or otherwise released, onsite and offsite. Offsite releases and disposals come from the part of the Form R where offsite transfers are entered, and includes only those transfers that were disposed of or otherwise released rather than treated or recycled or used for energy recovery. Recall that for each off-site transfer, a code was entered representing the disposition of that chemical.
Information for Sections 8.3, 8.5, and 8.7 are also calculated from quantities already reported in other parts of the form. For current year quantities, TRI-MEweb will perform these calculations automatically using the data shown here.

## Slide 112: Section 8: Relationship to Section 7
PART II. SECTION 8.1 – 8.7 | 
8.2 | On-site energy recovery Determine quantity for activities described in 7B. Report quantity of the chemical actually combusted in energy recovery unit
8.4 | On-site recycling Determine quantity for activities described in 7C. Report quantity of the chemical actually recycled
8.6 | On-site treatment Determine quantity of the chemical for activities on waste stream described in 7A. Report quantity of the chemical actually destroyed (i.e., consider efficiency). Metals and metal category compounds cannot be reported here.
Notes: When completing the Form R in TRI-MEweb, the quantities needed for the three subsections of Section 8 shown here are entered alongside the on-site waste management methods that are reported in the previous Section of the Form. In sections 8.2, 8.4 and 8.6, facilities report the quantities of the TRI chemical used for on-site energy recovery, on-site recycling, and on-site treatment, respectively. Again, to be reported as energy recovery, the TRI chemical itself, and not only the entire waste stream, must have an energy value and be must be combusted in an energy recovery unit. To be reported as recycling, the TRI chemical itself must be recycled. And to be reported as treatment, the TRI chemical itself must be destroyed. Note that metals cannot be destroyed.

## Slide 113: Non-Production-Related Waste Managed
Enter the quantity of Section 313 chemical released into the environment or transferred off-site (Section 8.8) as a result of:
  Remediation
  Catastrophic events (e.g., earthquake, hurricane, fire, floods)
  Other one-time events not associated with production processes (e.g., pipe rupture due to unexpected weather)
Does not include quantities treated, recovered for energy, or recycled ON-SITE.
Quantities in Sections 8.1 through 8.7 should not include amounts reported in Section 8.8
  TRI-MEweb calculator will deduct non-production-related waste quantities from Sections 8.1 through 8.7
Notes: If quantities of the TRI chemical were released to the environment or transferred off-site as a result of a remediation activity, or a catastrophic or one-time event, these quantities are reported separately when completing the Source Reduction and Waste Management portion of the Form. This does not include chemicals that are treated onsite, recovered for energy onsite, or recycled on-site, no matter how those chemicals were generated. Note that these quantities are entered in Section 8.8 of the Form R and they are exclusive of the quantities entered in Section 8.1 through 8.7. In other words, there is no overlap. For example, if a facility has an ongoing remedial action for a TRI chemical, and there are fugitive releases to the air associated with that remedial action, the quantity of the chemical released to the air is not reported in section 8.1 because the release is from the remedial activity. The quantity is reported in Section 8.8. Facilities using TRI-MEweb are asked to quantify any amounts of the TRI chemical associated with remedial actions or catastrophic or one-time events and the Section 8 calculator automatically deducts these amounts from Sections 8.1 through 8.7.
Also note that quantities reported in Section 8.8 do NOT include preventable quantities, like those associated with spills from a production process, or a leaking pipe, or anything that could have been prevented, such as through more rigorous prevention or maintenance procedures.

## Slide 114: Production Ratio or Activity Ratio
Production ratio or activity ratio (Section 8.9)
  A ratio of production or activity involving the Section 313 chemical in the reporting year to production or activity in the previous year
  Puts year-to-year changes in chemical quantities released and managed as waste into the context of production
Reporting tips
  Consider using a production ratio when production is directly related to the amount of chemical used or produced.
  Consider using an activity ratio when the chemical is "otherwise used" and the amount is determined by a variable other than production.
  The Production Ratio/Activity Ratio is a ratio, not a percent change.
  You can provide information on the variable you used in your ratio in the “Optional Miscellaneous Info” section using the button in TRI-MEweb.
A Production Ratio Wizard is now available in TRI-MEweb to help you calculate your Production Ratio or Activity Ratio.
Notes: The production ratio or activity ratio for the chemical goes in Section 8.9. The production ratio is a unitless value that compares this year’s production involving this chemical to last year’s production. This helps facilities examine trends in their quantities released and managed. For example, releases could be decreasing over time because pollution prevention is being implemented resulting in increased efficiency. Or releases could be decreasing because production is going down.
The facility must decide if a production ratio or an activity ratio best reflects the use of the chemical for which they are reporting. For example, if the facility is reporting on a chemical that is in the paint used to paint ovens, using the number of ovens would be a good production ratio. As they make more ovens, they are going to be using proportionally more of the paint, if they do not implement any pollution prevention practices. However, if the chemical is used in a cleaning solution to clean tanks, it may be that the facility is increasing production by running larger jobs that require fewer cleanings. Production isn’t a good indicator of the year-to-year use of that chemical, so they would opt for using an activity ratio instead.
If a facility does implement pollution prevention practices, they still may see their chemical use remain the same if their production ratio is greater than one, meaning their production is going up. That would indicate they are using less of the chemical per unit of product.
If production is going up, the production ratio is going to be greater than one. If production is going down, the production ratio or activity ratio is going to be less than one, as in the tank washout example. Barring significant changes in production or activities at a facility, most production ratios and activity ratios are within 0.5 and 2, which would indicate a 50 percent decrease and a 100 percent increase in production or activities, respectively.

## Slide 115: Source Reduction Activities
Report Source Reduction activities implemented for the chemical and the methods used to identify those activities (Section 8.10).
  Use listed codes to report source reduction activities. Codes are organized into five categories.
  Include only new source reduction activities implemented started or completed during the reporting year
  Examples of Source Reduction Activities:
    Product redesign
    Material substitution (e.g., switched to aqueous cleaner)
    Process or equipment changes (e.g., implemented new technique, adjusted or replaced equipment)
    Changed production schedule to minimize equipment changeovers
You may also report the estimated annual reduction associated with each activity
  The reduction range codes reflect the percentage of the annual amount of chemical waste generation mitigated relative to the amount that would have been generated without the source reduction activity
Option to provide additional details about source reduction activities in Section 8.11
Notes: In the Source Reduction Activities portion of the Form R, Section 8.10, facilities report on the source reduction activities, implemented during the reporting year that could reduce the total quantity of chemical released (including disposal), recycled, combusted for energy recovery, or treated. The various source reduction activities are represented by codes that can be found as a “drop down” menu in TRI-MEweb or in the “Reporting Forms and Instructions” document. There are many types of activities that could be considered source reduction activities. Some are listed here. Reporters should review these codes, because they may not realize that some of the activities that they have implemented during the year would count as source reduction. For each source reduction code you enter in TRI-MEweb, a button to the right of the entry allows you to provide details on the source reduction practice in the next section of the Form R (Section 8.11, Optional Pollution Prevention Information). This information will be added to Section 8.11 (Optional Pollution Prevention Information), preceded by the code to which it relates.
If you choose to enter an estimated annual reduction for source reduction activities, the reductions associated with your pollution prevention efforts will be featured on EPA’s website through the TRI Pollution Prevention Search Tool at www.epa.gov/tri/p2.

## Slide 116: Optional Pollution Prevention (P2) Information
Report additional information in the open-ended P2 text fields (Section 8.11)
This is an opportunity to provide greater details about your source reduction activities, waste management practices, or other pollution prevention activities including barriers preventing P2 implementation.
Optional comments may be used to publicly highlight your facility’s actions to reduce the amount of toxic chemicals entering the environment.
Any comments entered in TRI-MEweb associated with Sections 7 and 8.10 are prepopulated in Section 8.11.
For additional guidance, see https://www.epa.gov/toxics-release-inventory-tri-program/pollution-prevention-p2-and-tri
Topics on which you may elect to provide information include:
  Source Reduction
  Barriers to Source Reduction
  Waste Management including recycling, energy recovery, and treatment practices
  Other information such as general environmental management and climate adaptation strategies
Reporting tips
  Be specific – e.g., what new materials were used, how was product design changed, how were processes altered.
  Provide useful URLs and resources used to identify or achieve source reduction.
  Put information unrelated to P2 in Section 9.1.
Notes: This section of the Form R allows facilities to provide any additional information on their source reduction, recycling, or pollution control activities to supplement their TRI report. The information may include activities from previous years. This section of the TRI Form is optional and is only for information related to source reduction, recycling and pollution control. Completing this section and the previous section provides an opportunity to publicly highlight any steps your facility took to reduce the amount of toxic chemicals entering the environment. Alternatively, if your facility faces barriers inhibiting the implementation of pollution prevention, EPA encourages you to use this Section to describe these barriers. EPA has increased the prominence and accessibility of the pollution prevention information reported to TRI. Visit www.epa.gov/TRI/P2 to learn about tools to access this information and identify pollution prevention practices that may be applicable to your facility.

## Slide 117: Optional Miscellaneous Information
Optional Miscellaneous Information (Section 9.1, Form R; Section 9.2, Form A)
  Facility can provide any useful additional information related to any portion of the Form R or Form A submission in this new data field.
  Examples of information to include:
    Changes in production
    Facility closures
    Staffing changes
    Calculation methods, e.g., emission factors
    Explanation of data quality alerts
TRI-MEweb provides a pick-list of suggested topics for this Section.
  When providing optional miscellaneous information, it is helpful to check the box next to the topic to which your information pertains.
Notes: In Section 9.1, facilities can enter any other information related to the Form R submission. Possible examples to include are: changes in production, facility closures, staffing changes, and calculation methods. TRI-MEweb also allows you to use this section to provide explanations related to individual data quality alerts generated by the system.
When providing information in this section, TRI-MEweb provides boxes where you can check the topic that describes the type of information you’re entering.

## Slide 118: Section VI: Form R Calculation Examples

## Slide 119: Fugitive Air Emissions Example: Section 5.1
Example
Using a Mass Balance Basis of Estimate (C):
  5,000 pounds of a volatile solvent are added during the year as part of the manufacture of a liquid adhesive. 4,950 pounds of the solvent are contained in the final liquid adhesive product. It is assumed all loses are due to uncontrolled evaporations
    Input (5,000 lb) = Output (4,950 lb) + Air Loss (50 lb)
    Fugitive air emissions from this process = 50 lb
    Assuming no other fugitive air emissions, the facility would report 50 lb air release for Section 5.1 and basis of estimate ‘C’
Law of Mass Balance: What Goes In = What Comes Out
Notes: In the example shown, a facility knows that it used 5,000 pounds of a volatile solvent during the reporting year. They also know that 4,950 pounds of the solvent were contained in the adhesive product that they manufactured. Using a simple mass balance calculation, they are able to determine that 50 pounds of the TRI chemical were released to the air through fugitive emissions. The facility then enters 50 pounds in Section 5.1 along with a basis of estimate code of “C”.

## Slide 120: Stack Air Emissions Example: Section 5.2
Example using an Emission Factor basis of estimate (E1):
  500,000 tons of coal are combusted in a fluidized bed combustor.
  EPA emission factor: 0.11 lb mercury emitted / 1,000,000 lb coal combusted.
  500,000 tons × 2,000 pounds / ton × (0.11 lb mercury / 1,000,000 lb coal) = 110 lb mercury.
  110 pounds of mercury are released through the stack.
  Note: A portion of mercury may be present in resulting ash and would need to be reported as such.
Notes: An example of an estimate based on a published emissions factor is shown here. A facility combusting 500,000 tons of coal in a fluidized bed combustor obtained a published emissions factor for mercury in such a system.
Using the emission factor, they were able to determine that 110 pounds of mercury was released through the stack, which they entered on the TRI form along with a basis of estimate code of “E1”.

## Slide 121: Wastewater Discharges Example – Section 5.3
Calculate the yearly pounds of methanol discharged using the following data concerning wastewater discharges of methanol:
MGD = million gallons per day
1 mg/l = 8.33 lb/million gal
Assuming 365 days of discharge and no other sources:
  4.33 lb/day × 365 day = 1,580 lb total release
  Basis of Estimate Code: M2
  Include receiving stream or water body name and Reach Code (optional)
  Indicate NA for contribution from stormwater
DATE | CONC. (MG/L) | FLOW (MGD) | AMT. (LB/DAY)
3/1 | 1.0 | 1,0 | 8.33
9/8 | 0.2 | 0.2 | 0.33
Average = 4.33 |  |  | 
Notes: Here is an example calculation for wastewater discharges using already existing and available monitoring data. This example is for methanol discharges, where this facility collected samples twice during the reporting year. The first sample was taken on March 1st, when the chemical was released at a concentration of 1.0 milligrams per liter with a flow rate of 1.0 million gallons per day. Converting milligrams per liter and million gallons per day into pounds per day results in 8.33 pounds per day by applying the appropriate conversion factors. Their second sample was taken on September 8th, where they measured the chemical at a concentration of 0.2 milligrams per liter, at a flow rate of 0.2 million gallons per day. Calculating that with the appropriate conversion factors again, comes out to 0.33 pounds per day. The two samples of 8.33 and 0.33 pounds/day are averaged to get 4.33 pounds per day. The number that goes on the Form R is not in pounds per day, but in pounds for the reporting year. So, this quantity must be multiplied by the operating days, say 365 days, to get the total pounds per year.

## Slide 122: POTW Transfers Example – Section 6.1
Example using an Engineering Calculations basis of estimate (O):
  A wet grinding process generates wastewater with 300 lb of lead (contained in particulates) during the year. This wastewater undergoes on-site filtration prior to being sent to the POTW. Manuals from the filter equipment vendor indicate a 95% removal efficiency for particulates of this size.
    300 × 0.95 = 285 lb removed from the wastewater
    300 – 285 = 15 pounds remaining in the wastewater after filtration
    15 pounds of lead are transferred off-site to the POTW
Notes: In the example shown here, a facility used engineering calculations to determine that it generated wastewater containing 300 pounds of lead particulates during the reporting year. Before being discharged to the POTW, the wastewater underwent a filtration step that was thought to have a 95 percent removal efficiency for this size of particulates. Therefore, the quantity of lead reported as transferred to the POTW is 15 pounds and the basis of estimate code for this combination of estimation techniques is “O”.

## Slide 123: Production and Activity Ratio Examples: Section 8.9
Example (Production Ratio): Oven manufacturing
  40,000 ovens assembled (Current RY) = 1.14
  35,000 ovens assembled (Prior RY)
Example (Activity Ratio): Tank washouts
  50 Washouts (Current RY) = 0.83
  60 Washouts (Prior RY)
Additional Production / Activity Variable Examples, by Industry
  Refractory Manufacturing: Tons of brick manufactured
  Chemical Wholesalers: Gallons of glycol ethers packaged
  Electric Power Generation: Megawatt-hours of electricity produced
  National Security: Man-days of training per year
  Synthetic Dye Manufacturing: Number of color changeovers
  Waste Treatment and Disposal: Tons of waste landfilled on-site
Notes: Let’s go through a couple of examples to illustrate the production and activity ratio.
The first example is an oven manufacturer, and at this facility 40,000 ovens were assembled this reporting year, compared to 35,000 ovens assembled in the prior reporting year. So dividing 40,000 by 35,000 results in a production ratio of 1.14. This is a unitless value. 1.14 would represent a 14% increase in production from last year to this year. But neither 14, or 0.14 should be reported. Only 1.14, the actual ratio, should be reported.
The facility must select a production or activity variable that best reflects to output or outcomes of the process in which the chemical is involved. If the TRI chemical use has no connection to production levels. In the activity ratio example shown here, the chemical is used to wash out tanks. In this case, the number of tank washouts completed is the best indicator of the output or outcome of the process in which the chemical is involved, so they would opt for using an activity ratio instead of a production ratio. There were 50 washouts this year compared to 60 the last year. That would result in an activity ratio of 0.83

## Slide 124: Section VII: Alternate Threshold Rule (Form A)

## Slide 125: TRI Form A Certification Statement
The “TRI Alternate Threshold for Facilities with Low Annual Reportable Amounts” provides facilities the option of submitting a simplified TRI Form A Certification Statement
Form A includes facility identification information and the chemical or chemical category identity
Form A does not include release, other waste management, or source reduction reporting
To be eligible to submit a Form A for a chemical, the following criteria must be met:
The chemical must not be a Chemical of Special Concern,
The total amount manufactured, processed, or otherwise used does not exceed 1 million pounds for that chemical, and
The facility does not exceed 500 pounds for the total annual reportable amount for that chemical
Notes: The “TRI Alternate Threshold for Facilities with Low Annual Reportable Amounts” provides facilities the option of submitting a simplified, two-page TRI Form A Certification Statement. If facilities meet the criteria, they have the option of submitting a TRI Form A in lieu of the Form R. The Form A does not require release or other waste management or source reduction information. It mainly is comprised of Part one of the Form R and the name and chemical or chemical category name and its CAS number or category number.
In order to use the Form A, the following criteria must be met. First the chemical cannot be a Chemical of Special Concern. Second, the facility cannot exceed one million pounds of the chemical manufactured, processed, or otherwise used. Third, the facility cannot exceed 500 pounds for the total waste managed of the TRI chemical.

## Slide 126: TRI Form A Certification Statement
The annual reportable amount is equal to the combined total quantities of the following waste management activities:
Released or disposed of at the facility
Treated, recycled, or combusted for the purpose of energy recovery at the facility
Transferred from the facility to off-site locations for the purpose of recycling, energy recovery, treatment, and/or disposal
Facilities must retain Alternate Threshold calculations documentation for three years from the submission of the Form A
If a facility submits a Form A and does not meet the qualifying criteria, it may result in an enforcement action
Notes: The annual reportable amount is equal to the combined total quantities of the following waste management activities for Sections 8.1 through 8.7.
Facilities must retain for three years from the date of the submission of the Form A sufficient documentation to support calculations made by the facility that confirm each chemical’s eligibility for the Alternate Threshold.

## Slide 127: Section VIII: TRI-MEweb Introduction

## Slide 128: TRI-MEweb and Submitting Via CDX
Electronic filing via TRI-MEweb is required.
  No paper submissions are accepted (except for trade secrets), including revisions and withdrawal.
  TRI-MEweb supports new reporting, revisions & withdrawals for RY 1991 – current year.
  TRI-MEweb resources including tutorials are available to help users at: https://www.epa.gov/toxics-release-inventory-tri-program/electronic-submission-tri-reporting-forms.
Use hard-copy form only for trade secret reporting.
  Information about trade secret reporting at: https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:rfi-home
All TRI reports must be prepared and certified by July 1st following the calendar year’s activities (aka Reporting Year (RY)).
  July 1, 2022 deadline for RY 2021 (January 1 - December 31, 2021) activities
v
v
Notes: 128
The Electronic Reporting rule requires electronic reporting via TRI-MEweb for all non-trade secret TRI reporting, which accounts for nearly all forms submitted to TRI. Electronic reporting is now required for all new reporting, withdrawals or revisions for Reporting Years 1991 through the current year.
TRI-MEweb has features to help reporters with their submissions including pre-populating forms with information from prior year reporting, validation and error checking steps, and e-mail confirmation of transmitted and certified submissions. Additionally, tutorials to help users with TRI-MEweb are available on the TRI website.
Paper submissions should only be used for trade secret reporting. Information about trade secret reporting is available on the TRI website.

## Slide 129: Accessing TRI-MEweb
TRI-MEweb is accessed through EPA’s Central Data Exchange (CDX).
  CDX is accessed through: https://cdx.epa.gov.
  TRI-MEweb users must have a CDX account.
  Select TRI-MEweb user role: preparer or certifying official.
    Preparers are able to create, prepare, revise and withdraw TRI Forms.
    Certifying officials have these abilities plus are able to certify forms. Certifying officials should be in a senior management role for the facility.
Within TRI-MEweb, new users must gain access to their facility profile.
  Option 1: Enter TRIFID and Technical Contact Name.
  Option 2: Enter the facility specific access code.
  Option 3: Begin a new facility profile if the facility has never reported to TRI
For assistance with accessing your facility, contact the CDX helpdesk at helpdesk@epacdx.net or call toll-free at (888) 890-1995
Notes: 129
To begin using TRI-MEweb, you must register and log into EPA’s Central Data Exchange, also known as CDX, which also hosts many other reporting applications for EPA programs. Users register either as a preparer or a certifying official. Preparers may perform every portion of the submission process except for the final electronic signature or certification step, which must be performed by a certifying official. The certifying official should be in senior management role for the reporting facility or company. Anyone representing the facility may be a preparer.
To begin reporting for a facility, all users must gain access to their facility’s profile, using one of three options: the first option is to enter the TRI Facility ID and the facility’s technical contact name and phone number. The second option is to enter a facility specific access key, which is provided to the technical contact. The third option is to begin a new profile for a facility that has never reported to TRI.

## Slide 130: Signing and Certifying Forms
New Certifying officials must complete the following two requirements:
  Electronic Signature Agreement (ESA)
    Must be completed only once, not annually, applicable to all facility profiles
    Option 1: Real-time ESA approval – verify user’s identity electronically
    Option 2: Mail in signature form – minimum of 5 business days to process
  TRIFID Signature Agreement
    The TRIFID Signature Agreement authorizes the certifying official to certify forms for the specific TRI facility.
    Facility profiles must be added to TRI-MEweb before a TRIFID Signature Agreement Form can be signed.
    Certifying officials must have a digitally signed TRIFID Signature Agreement for each facility profile before access to any pending submission(s) for certification is granted.
New certifying officials must obtain approval of an ESA and digitally sign a TRIFID Signature Agreement(s) for each facility profile(s) before pending submissions can be reviewed and certified.
Notes: In order to certify forms, certifying officials must complete two steps. The first step is to complete an electronic signature agreement. The ESA is only submitted once as long the certifying official remains with the facility. Existing certifying officials do not resubmit an ESA. New certifying officials should complete their ESA well in advance of the July 1st filing deadline to ensure they will be able to certify forms on time.
After the ESA is submitted, certifying officials must complete an TRIFID Certification Agreement for each facility they represent, confirming they are authorized to certify forms for the facility. The TRIFID Certification Agreement is completed in TRI-MEweb in the ‘Certification’ section of TRI-MEweb. Similar to the ESA, the TRIFID Certification Agreement is only submitted once as long the certifying official remains with the facility.

## Slide 131: Optional Facility-Level Information
Facilities may provide optional information on facility operations.
Section 9.1 of the Form R and Section 9.2 of Form A allow a facility to provide optional miscellaneous information on the form submission or facility.
However, some types of miscellaneous information do not fit well into a TRI reporting form or arise outside of the reporting process.
  TRI-MEweb allows you to provide optional facility-level information without preparing and submitting a TRI reporting form.
  Accessible on the Facility Management Screen: Click the Take Action button and select ‘Not Reporting?’
Notes: Reporters may submit optional facility-level information through TRI-MEweb. This option allows reporters to provide information about their facility’s status without submitting a TRI report, or providing information which does not fit well into a TRI reporting form.
Optional Facility-Level reporting is found in TRI-MEweb through the facility summary in the welcome screen or in the ‘My Facilities’ tab.

## Slide 132: Optional Facility-Level Information
Topics on which you may elect to provide information include:
  Facility name or address has changed.
  Facility contact information has changed.
  Facility closed either completely or temporarily
  Facility did not trigger reporting due to:
    Not having 10 or more full-time employee equivalents
    Not being in a covered NAICS sector
    Having fallen below reporting threshold for one or more chemicals
Benefits of providing this information include:
  Keeps address and contact information up-to-date to help EPA contact your facility
    Ensures email notices reach proper facility contacts
  Provides clarity on why reporting may have changed substantially
    Could minimize need for EPA to contact facility on data quality matters
Notes: Facilities may provide optional facility-level information on topics listed on this slide, as well as other categories. In particular, this option may be useful for facilities that are do not meet reporting criteria and wish to provide context why they have not reported. Also, this option may be used for updating facility information, such as technical or public contact changes, or facility or parent company name changes.

## Slide 133: For More Information and Assistance
For more information on TRI requirements see the second part of this training course on TRI Advanced Concepts.
For TRI reporting guidance, information and tutorials on the TRI-MEweb reporting software, and the latest changes to the TRI Program please visit: https://www.epa.gov/tri.
Industry-specific and chemical-specific guidance can be found at: https://ofmpub.epa.gov/apex/guideme_ext/f?p=guideme:gd-list.
For help accessing CDX accounts, password resets, accessing a facility, or completing an ESA, contact the CDX helpdesk: https://cdx.epa.gov/Contact.
Notes: This concludes the TRI Basic Concepts Module. The Advanced Concepts module is the second part of this two part training course.
The Advanced Concepts module assumes a basic understanding of the TRI program requirements. It reviews some of the basic concepts, but focuses on key concepts that will help to ensure accurate TRI reporting, including guidance on reporting exemptions, threshold determinations, chemicals with special requirements, and more on the recent changes to the TRI program.
The Advanced Concepts module, a great deal of additional TRI reporting guidance, and on-line tutorials for using the TRI-ME web can be accessed from the TRI homepage at www.epa.gov/tri.
For CDX and TRI-MEweb related help, including registering for CDX, password resets, accessing your facility profile in TRI-MEweb, or completing an ESA, please contact the CDX helpdesk.

## Slide 134: End of Module

## Slide 135: Quiz Answers
135
Notes: 135

## Slide 136: Quiz #1: Question 1
Would the facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
A manufacturing facility, owned by ABC Corporation, with 100 full-time employees
Select Yes or No
Answer: Yes
As a manufacturing facility, its primary NAICS code will be among those covered by EPCRA Section 313 (TRI). In addition, the facility employs more than 10 full-time employees. This facility would need to consider whether it has exceeded any activity thresholds for TRI chemicals or chemical categories to determine if it needed to report
Notes: Would the type of facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
A manufacturing facility, owned by ABC Corporation, with 100 full-time employees
The answer is Yes. As a manufacturing facility, its primary NAICS code will be among those covered by EPCRA 313 (TRI). In addition, the facility employs more than 10 full-time employees. This facility would need to consider whether it has exceeded any activity thresholds for TRI chemicals or chemical categories, to determine if it needed to report.

## Slide 137: Quiz #1: Question 2
Answer: No
The facility’s maintenance and warehouse activities are represented by a primary NAICS code that will not be among those covered by EPCRA 313 (TRI). In addition, the facility has fewer than 10 full-time employees. This facility would not need to report
Would the facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
A maintenance and warehouse facility, owned by ABC Corporation, with 5 full-time employees, a few blocks away from the manufacturing facility described in Question 1
Select Yes or No
Notes: Would the type of facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
A maintenance and warehouse facility, owned by ABC Corporation, with 5 full-time employees, a few blocks away from the manufacturing facility described in the first example
The answer is No. The facility’s maintenance and warehouse activities are represented by a primary NAICS code that will not be among those covered by EPCRA 313 (TRI). In addition, the facility has fewer than 10 full-time employees. This facility would not need to report.

## Slide 138: Quiz #1: Question 3
Answer: Yes
The maintenance and warehouse activities are considered part of the manufacturing facility because they are on adjacent properties. Since the employee threshold is exceeded, this facility would need to consider any chemical use at the warehouse and maintenance establishment along with that of the manufacturing facility to determine if the facility needed to report
Would the facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting?
A maintenance and warehouse facility, owned by ABC Corporation, with 5 full-time employees, next door to the manufacturing facility described in Question 1
Select Yes or No
Notes: Would the type of facility described below be covered by TRI and, therefore, need to consider its chemical use for possible reporting? Select Yes or No.
A maintenance and warehouse facility, owned by ABC Corporation, with 5 full-time employees, next door to the manufacturing facility described in the first example
The answer is Yes. The maintenance and warehouse activities are considered part of the manufacturing facility because they are on adjacent properties. This facility would need to consider any chemical use at the warehouse and maintenance portion along with that of the manufacturing portion of the facility, to determine if it needed to report.

## Slide 139: Quiz #2: Question 1
A plant uses benzene as a raw material to manufacture liquid industrial adhesive. The plant adds 27,000 lb of benzene to its liquid adhesive-making operation during the reporting year, but 3,000 lb are volatilized during the operation. How much of the benzene should be applied toward the processing activity threshold?
A. 27,000 lb B. 24,000 lb C. 3,000 lb
Select your choice
Answer: A is correct
27,000 total lb of benzene is processed. Always apply the total amount that enters a process toward the activity threshold. The quantity of benzene processed exceeds the processing threshold (25,000 lb) for chemicals with 25,000/10,000-pound reporting thresholds. Therefore, the facility would need to complete a TRI form for benzene. The quantity released to the environment would be reported on the TRI Form R.
Notes: A plant uses benzene as a raw material to manufacture liquid industrial adhesive. The plant adds 27,000 lb of benzene to its liquid adhesive-making operation during the reporting year, but 3,000 lb are volatilized during the operation. How much of the benzene should be applied toward the processing activity threshold? Select your choice.
A. 27,000 lb B. 24,000 lb C. 3,000 lb
A is correct. 27,000 total lb of benzene is processed. Always apply the total amount that enters a process toward the activity threshold. Because the plant’s benzene use exceeds the 25,000 lb processing threshold for chemicals with 25,000/10,000-pound reporting thresholds, the facility would need to complete a TRI form for benzene. The quantity released to the environment would be reported on the TRI Form R.

## Slide 140: Quiz #2: Question 2
If a facility processes 20,000 lb of to 4,4’-Methylenedi(phenyl isocyanate) in one operation and 10,000 lb of isophorone diisocyanate in another operation during the reporting year, what should it apply towards it's processing threshold for the diisocyanates category?
A. 10,000 lb B. 20,000 lb C. 30,000 lb
Select your choice
Answer: C is correct
4,4’-Methylenedi(phenyl isocyanate) and isophorone diisocyanate are both chemicals within the diisocyanates chemical category; therefore, the quantities of each chemical processed during the reporting year should be summed. The facility has exceeded the reporting threshold for processing (25,000 lb) and would need to report for the diisocyanates category.
Notes: If a facility processes 20,000 lb 4,4’-methylenedi(phenyl isocyanate) in one operation and 10,000 lb of isophorone diisocyanate in another operation during the reporting year, what should it apply towards it's processing threshold for the diisocyanates category? Select your choice.
A. 10,000 lb B. 20,000 lb C. 30,000 lb.
Answer C is correct. 4,4’-methylenedi(phenyl isocyanate) and isophorone diisocyanate are both chemicals within the diisocyanates chemical category; therefore, the quantities of each chemical processed during the reporting year should be summed. The facility has exceeded the reporting threshold for processing (25,000 lb) and would need to report for the diisocyanates category

## Slide 141: Quiz #2: Question 3
A facility processes 18,000 lb copper sulfate, 10,000 lb of cuprous oxide, and otherwise uses 12,000 lb of aqueous sulfuric acid solution in a closed system. For which TRI chemicals or chemical categories would the facility need to submit a TRI form?
A. Copper compounds and sulfuric acid B. only copper compounds C. only sulfuric acid
Select your choice
Answer: B is correct
The facility has exceeded the 25,000 lb processing threshold for copper compounds (18,000 + 10,000 = 28,000) and would need to submit a TRI form for copper compounds. The qualifier for sulfuric acid (see Section 313 Chemicals) indicates that it is only reportable in an aerosol form. Because the facility only used the sulfuric acid in an aqueous form (and does not generate acid aerosols), it does not need to consider it towards the otherwise use threshold, and no report for sulfuric acid is required
Notes: A facility processes 18,000 lb copper sulfate, 10,000 lb of cuprous oxide, and otherwise uses 12,000 lb of aqueous sulfuric acid solution in a closed system. For which TRI chemicals or chemical categories would the facility need to submit a TRI form? Select your choice.
A. copper compounds and sulfuric acid B. only copper compounds C. only sulfuric acid
Answer B is correct. The facility has exceeded the 25,000 lb processing threshold for copper compounds (18,000 + 10,000 = 28,000) and would need to submit a TRI form for copper compounds. The qualifier for sulfuric acid indicates that it is only reportable in an aerosol form. Because the facility only used the sulfuric acid in an aqueous form (and does not generate acid aerosols), it does not need to consider it towards the otherwise use threshold, and no report for sulfuric acid is required.